## Slide 1
CRR Deration and NPRR821
WMS
09/06/2017

## Slide 2: Introduction
Deration and how it works
Eliminating deration
Options around eliminating deration
Alternatives proposed by LCRA – Focus on the PTP price instead

## Slide 3: Deration
CRR deration was introduced as a market mitigation measure for a particular gaming strategy
CRR deration directly assigns reduced payments to specific CRRs that have impacts on oversold transmission elements
CRRs are only subject to deration if they involve a Resource Node
CRR payments incorporate a quantity called Hedge Value which limits derations to keep payments in line with proxy fuel costs at the Source or Sink
Unlike short-payments, derations are never refunded
Both derations and short-payments can cause a payment mismatch for entities converting the hedge to RT -> $ paid for CRRs ≠ $ charged for DAM PTPs

## Slide 4: DAM Congestion Rent
If there is not enough congestion rent collected for the hour to pay all of the CRRs (after deration has occurred), all CRRAHs are charged a pro-rated shortfall charge to cover the difference.
At the end of the month, if there are funds in the Balancing Account they are used to refund shortfall charges to CRRAHs.
Payment due to CRRAHs
Charges for Energy Bids
Charges for PTP Obligation Bids
Payments for Energy Offers
Payments for PTP Obligation Bids
Congestion Rent
Occurs hourly

## Slide 5: Current Monthly Timeline

## Slide 6: No Deration Monthly Timeline

## Slide 7: Interaction Among Markets – Ideal Conditions
The value of CRRs are based on the estimate of the expected congestion costs on the purchase path.
  The net amount paid for CRR ownership in auctions should converge to the net amount received in DAM by CRRAHs for their CRR.
  The net amount paid for PTPs in DAM should converge to the net amount received in RT by QSEs for their PTPs.
DA prices are based on the estimate of expected RT energy costs. In long run, the DASPP and RTSPP should converge.
Under ideal conditions (markets converged)
  CRR Auction Revenue = DAM CRR payout = DAM congestion rent = RT congestion rent (complete hedging)
  DAM SPP = RT SPP
  CRR+DAM+RT settlements = settling everything in RT

## Slide 8: NPRR821 Options
Original (DC Energy) - Eliminates deration, CRRs receive full target payment
Potential impacts-
Auction revenues are expected to increase due to CRRs having a higher value in the DAM. Increases cost of CRRs and increases payout to load of auction revenue.
Less excess Congestion Rent credited to Balancing Account due to increased CRR payout. This will tend to reduce the monthly load payout from the Balancing Account.
Increased chance of shortfall charges to CRRAHs, and less Congestion Rent increases chances of some shortfall charges not being refunded.
DC Energy comments - Eliminates deration with a ‘circuit breaker’ to temporarily reduce CRRs sold in the monthly auction if the Balancing Account balance drops to zero.
Additional impacts when ‘circuit breaker’ enacted, due to less CRRs sold:
Auction revenues reduced.
More excess Congestion Rent available for credit to the Balancing Account, blunting the effects listed above for original proposal.

## Slide 9: NPRR821 Options
Morgan Stanley comments – all CRRs subject to deration, not just those involving Resource Nodes; eliminates Hedge Value limitation on derations; and removes the Balancing Account fund.
Potential impacts-
Auction Revenues decrease as CRRs have lower value in DAM. Decreases costs of CRRs and decreases payout to load of auction revenue.
More excess Congestion Rent credited to Balancing Account due to decreased CRR payout. This will tend to increase the monthly load payout from the Balancing Account.
Decreased chance of shortfall charges to CRRAHs, but no refund of shortfalls.

## Slide 10: QSE PTP Obligations in DAM
Mechanism for hedging congestion costs in RT:
  Purchase a DAM PTP Obligation bid based on the DAM locational price difference.*
  Get paid (or charged) based on the RT locational price difference.*
  Net revenue from PTP Obligation bids is credited to DAM congestion rent.
  Net RT payments funded via Real-Time Revenue Neutrality Allocation, if insufficient RT congestion rent is collected.
  *Note that NOIEs can essentially purchase RT Options

## Slide 11: NPRR821 Options PTP Focus Instead of Deration
LCRA Option 1 and Option 2 both reduce the cost of DAM PTP Obligations, but differ on the circumstances.
    Option 1 reduces the PTP cost if a QSE is linked to a CRRAH that owns a derated CRR on the path.
    Option 2 reduces the PTP cost if any derated CRR exists on the path.
CRR full payment
CRR derated payment
PTP original cost
PTP reduced cost

## Slide 12: NPRR821 Options PTP Focus Instead of Deration
LCRA Option 1
Auction revenues are unlikely to be impacted because CRRs are still derated
Less excess Congestion Rent will be credited to Balancing Account due to decreased PTP revenue. This will tend to reduce the monthly load payout.
Increased chance of shortfall due to the reduction in Congestion Rent collected.
LCRA Option 2
Same impacts but increased magnitude due to the increase in eligible PTPs.

## Slide 13: Specific ERCOT Concerns Surrounding Alternatives
The option to adjust the PTP treatment favors price-taking behavior in the DAM over price sensitive bids and offers.
  This will crowd-out certain types of participation.
    Removes any incentive to place offers in the DAM that are reflective of real-time behavior. Regardless of the magnitude of a negative price for a particular resource an entity will not have an incentive to react.
  The outcome creates an inequity and has efficiency concerns. The DAM was not intended to favor price-taking behavior over price sensitive bids and offers.
The option to eliminate balancing account and de-rate everyone is a paradigm change and should not be moved forward without additional thought about the consequences.

## Slide 14: Appendix

## Slide 15: CRR Auction Revenue
CRR Auction and Auction Revenues
  All revenues distributed on load ratio share basis depending on whether the CRR source and sink belong to the same 2003 Congestion Management Zone or not.

## Slide 16: Impact of Removing the CRR Deration Process
Chart: Estimated Impact to the Rolling CRR Balancing Account
| 41640 | 41671 | 41699 | 41730 | 41760 | 41791 | 41821 | 41852 | 41883 | 41913 | 41944 | 41974 | 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 42248 | 42278 | 42309 | 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826
Actual | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20580 | 1767929 | 3864535 | 6717548 | 7988176.04 | 6692320.78 | 9903649.57 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 4294673.94 | 5056687.29 | 10000000 | 10000000 | 10000000 | 10000000
Estimated | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1262408.2885 | 2929297.4823 | 5015303.6562 | 5773233.2183 | 3371361.4409 | 6188236.3816 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 3733020.9447 | 4379469.9918 | 9445760.4146 | 10000000 | 10000000 | 9638542.4332
Post Rolling CRR Balancing Account

## Slide 17: Impact of Removing the CRR Deration Process
Chart: Estimated Impact to the Load-Allocated Payments
| 41640 | 41671 | 41699 | 41730 | 41760 | 41791 | 41821 | 41852 | 41883 | 41913 | 41944 | 41974 | 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 42248 | 42278 | 42309 | 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826
Actual | 3685632.01 | 9055518.51 | 5418730.32 | 0 | 127275.69 | 1980934.62 | 3686296.43 | 9302875.39 | 974674.13 | 1001607.47 | 1455336.09 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4332031.41 | 5578528.36 | 3452239.45 | 3962069.03 | 2080168.79 | 2166073.06 | 895981.46 | 2017986.45 | 648836.89 | 3392223.16 | 3519949.15 | 7420347.79 | 5540995.62 | 6567916.3 | 4758625.29 | 5417370.23 | 0 | 0 | 3330951.21 | 4070196.23 | 11284166.33 | 2943795.34
Estimated | 3583428.8531 | 8706480.4348 | 5038086.9579 | 0 | 0 | 1780038.4007 | 3453034.8648 | 9279090.9225 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 485083.9028 | 5563273.5084 | 3331150.5354 | 3849526.1757 | 1977791.9062 | 2036620.4763 | 775680.5453 | 1726216.6709 | 46491.6428 | 2447140.1307 | 2224785.984 | 5848234.0409 | 1672389.0678 | 6505044.7408 | 4561277.7973 | 3106523.1461 | 0 | 0 | 0 | 3333046.9941 | 10903051.4638 | 0
Post Rolling CRR Balancing Account

## Slide 18: Deration by Path Type

## Slide 19: Deration
Chart: CRR Payments ($M)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 2015 | 2016 | 2017
Sum of CRR Payments | 17.8624 | 17.7087 | 15.5498 | 22.633 | 21.9188 | 40.0118 | 32.5612 | 21.825 | 21.6655 | 19.0716 | 9.4785 | 14.2534 | 8.5953 | 12.3241 | 32.8156 | 28.981 | 32.6459 | 63.3904 | 38.5049 | 25.4373 | 23.3596 | 49.3633 | 35.3829 | 18.686 | 31.6396 | 28.5472 | 55.2036 | 77.6397 | 86.3945 | 95.8924 | 45.0874
Sum of Derated Payments | 0.48521 | 0.43003 | 0.74959 | 0.51305 | 1.1063 | 0.39467 | 0.13187 | 0.015469 | 0.12131 | 0.11273 | 0.10262 | 0.12967 | 0.12054 | 0.29203 | 0.60263 | 0.94533 | 1.2954 | 1.5723 | 3.8688 | 0.063026 | 0.19753 | 2.311 | 0.56182 | 0.1158 | 3.2082 | 0.183 | 0.38142 | 3.3055 | 2.4815 | 0.13523 | 0.04298