## Slide 1
Review of Protocol Language associated with ERS Performance Calculations During TDSP Outages

## Slide 2: Performance Events
8.1.3.1.4 Event Performance Criteria for Emergency Response Service Resources
An ERS Resource’s performance shall not be evaluated for an ERS deployment if one of the following is true:
  For non-weather-sensitive Resources, one or more sites of an ERS Resource were disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline. QSEs must provide verification of such events from the TDSP or MRE; or
(d) For weather-sensitive Resources 10% or more sites of an ERS Load were disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline.

## Slide 3: Testing
8.1.3.2 Testing of Emergency Response Service Resources
Testing will be considered void and would require re-testing for any non-weather-sensitive Resources if one or more sites of an ERS Resource were disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline. QSEs must provide verification of such events from the TDSP or MRE.
(ix) Testing will be considered void for any weather-sensitive Resources if 10% or more sites of a weather-sensitive Resource were disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline. QSEs must provide verification of such events from the TDSP or MRE.

## Slide 4: Availability Non-Weather Sensitive
Note: WS ERS availability is deemed to be 1 … monthly tests and/or events are used in lieu of a calculated availability factor
8.1.3.3.1 Suspension of Qualification of Non-Weather-Sensitive Emergency Response Service Resources and/or their Qualified Scheduling Entities
(3) If a QSE’s portfolio-level availability factor is less than 0.95 excluding the intervals for Resources that had one or more sites of an ERS Resource disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline, ERS Resources in that portfolio that were not disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline shall be subject to the following:

## Slide 5: Availability Non-Weather Sensitive
Step 1:
  Calculate Resource and Portfolio Availability with power interruption intervals included.
  If Portfolio Availability is ≥ 0.95 payment is based on this Availability Factor
  If Portfolio Availability is ≤ 0.95 then go to Step 2
Step 2:
  Calculate Portfolio Availability with power interruption intervals excluded.
    Interval exclusion is done at the Resource level
    If one or more sites in an aggregation has a power interruption for an interval, that interval is excluded for the Resource
  If Portfolio Availability is ≥ 0.95 payment is based on Step 1 Availability Factor
  If Portfolio Availability is ≤ 0.95 then go to Step 3
Step 3:
  For Resources without power interruptions, determine if squaring is necessary (Resource Availability < 0.85)
  If none, payment is based on Step 1 Availability Factor
  If one or more are found, recalculate Portfolio Availability after the squaring and payment is based on this Portfolio Availability

## Slide 6: Payment Reductions for WS ERS Loads
8.1.3.3.2 Payment Reduction and Suspension of Qualification of Weather-Sensitive Emergency Response Service Loads and/or their Qualified Scheduling Entities
If the QSE portfolio-level event performance factor for the QSE’s portfolio of Weather-Sensitive ERS Loads for the ERS Contract Period as calculated in Section 8.1.3.3.4, Performance Criteria for Qualified Scheduling Entities Representing Weather-Sensitive Emergency Response Service Loads, is greater than or equal to 0.90 or if 10% or more sites of an ERS Load were disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline, ERCOT shall not impose a payment reduction for any of the those ERS Loads. Otherwise, ERCOT shall compute QSE portfolio-level Demand reduction values for each test and event throughout the ERS Contract Period as the greater of zero or the portfolio-level baseline ……
Note: ERCOT has and will avoid testing during periods of widespread outages affecting WS ERS Resoruces

## Slide 7: QSE Portfolio level Adjustment
8.1.3.3.3 Performance Criteria for Qualified Scheduling Entities Representing Non-Weather-Sensitive Emergency Response Service Resources
(b) Event Performance:
(iv) ERCOT will not include any Resources in the calculation of the ERSEPFqr if one or more sites of an ERS Resource were disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline. QSEs must provide verification of such events from the TDSP or MRE.

## Slide 8: QSE Portfolio level Adjustment
8.1.3.3.4 Performance Criteria for Qualified Scheduling Entities Representing Weather-Sensitive Emergency Response Service Loads
(1) A QSE’s ERS performance will be evaluated based on the performance of its portfolio of Weather-Sensitive ERS Loads during ERS deployment events in an ERS Standard Contract Term as follows:
(e) ERCOT will not include any weather-sensitive ERS Loads in the calculation of the ERSEPF if 10% or more sites of an ERS Load were disabled or unverifiable due to events on the TDSP side of the meter affecting the supply, delivery or measurement of electricity either during the event or prior that impacts the creation of a credible baseline. QSEs must provide verification of such events from the TDSP or MRE.

## Slide 9: ERS Unavailability
Scheduled Unavailability (ERS Loads)
  Up to 2% of committed intervals of unavailability are excluded from the Availability calculation if scheduled and submitted at least 3 days in advance.
  Unavailability that exceeds the 2% threshold should still be reported but will not be excluded from the Availability calculation
  Revisions and cancellations are allowed
    Additional intervals are excluded if submitted at least 3 days in advance
    Reductions in intervals will be used for availability if submitted 1 day in advance
Planned Maintenance (ERS Generators)
  Submitted no later than 2 business days prior to ERS SCT
  Limited to 2% of committed intervals
  Revisions and cancellations are allowed
    Cannot increase the number of intervals
    Additional intervals are excluded if submitted at least 3 days in advance
    Reductions in intervals will be used for availability if submitted 1 day in advance

## Slide 10: ERS Power Interruptions and Unplanned Unavailability
Power Interruptions (on TDSP side of meter)
  No limit on number of intervals submitted
  Submitted after the fact
  ERCOT will produce reports of NWS sites in competitive areas of ERCOT with significant numbers of consecutive intervals flagged as power interruptions that appear to be Harvey related (start date/time – end date/time)
    AMS status flags
    IDR status flags
  QSEs may submit power interruption notices using these as backup.
  Sites in NOIE areas will still require supporting documentation from TDSPs
  Power interruption submissions will be validated against ERCOT interval status flags … for this and for the future
  ERCOT will change code to avoid using power interruption intervals in calculating baselines
New submission type ‘Unplanned Unavailability’ (ERS Loads and Generators)
  No limit on number of intervals submitted
  Submitted after the fact
  Can be used to notify ERCOT of periods of unavailability related to equipment issues behind the meter
  Drop-down list on unavailability form will be modified to allow this as a submission type