## Slide 1
NPRR 785 Q&A
Operations Analysis
3/1/17

## Slide 2: Description of NPRR 785
NPRR 785 synchronizes COPs of Wind and Solar PV resources with their respective forecast. (STWPF/STPPF)
  Every hour (~1-2 min after the forecast is received*), ERCOT will update the existing COP HSL value for the next 168 hours (from the current operating hour) with the most recently received Forecast, subject to the resource’s HRL and previous update.
    An XML message will be generated when a WGR or PVGR’s COP HSL value has been updated/changed.
  ERCOT will not “create” COPs. ERCOT will only update the HSL values for hours that have a COP submission.
    Each QSE that represent a Resource A COP must submit a COP for all hours that fall in the rolling 168 hour forecast window.
*Currently Wind Forecast is received 10min past the hour and Solar Forecast is received 10min past the hour.

## Slide 3: Description of NPRR 785
QSEs are still required to submit a COP for every hour.
  For hours that do not have a forecast (hour no. 169, hour no. 170, …) it is suggested using the resource’s High Reasonability Limit (HRL) as its COP-HSL
QSEs are still required to ensure the COP HSL appropriately reflects anticipated operating conditions.
  QSEs will have the ability to submit a COP HSL value that is equal to or lower than the most recent forecast.
  For an hour where a QSE “override” exists, ERCOT’s hourly COP update process will use the lowest value between the QSE submission and the most recent forecast as its COP HSL for the hour, subject to the resource LSL.

## Slide 4: Diagram

## Slide 5: Examples
Forecast Value | COP Submission | Outcome
98 | 100 | “Entire” COP for the resource is Rejected
100 | 100 | COP is Accepted. From a forecast overwrite stand point, this hour will be updated during ERCOT’s next hourly COP update. ERCOT’s next hourly COP update will set COP-HSL = max(Forecast, LSL).
100 | 90 | COP is Accepted. From a forecast overwrite stand point, this hour will be treated as an “overridden” hour. ERCOT’s next hourly COP update will set COP-HSL = max(min(Forecast, 90),LSL).

## Slide 6: XML Notification
The following .XML message will be triggered when a Resource’ COP-HSL values are updated with forecast.
  Note, only one XML message will be generated per Resource.
 | CM-COP-UPD-NOTF COP HSL for <RES_NAME> from trade dates <MM/DD/YYYY> (first forecast date) to <MM/DD/YYYY> (last forecast date) have been updated to Forecast values. | Notify QSE when a WGR’s or PVGR’s COP HSL value is updated with the forecast value. |  |  |