## Slide 1
Boundary Threshold for the Load Review Process
Sandeep Borkar and Calvin Opheim
September 2017
TAC Meeting

## Slide 2: Agenda
Background
Recommendation
Process overview
Next steps

## Slide 3: Background
After several deliberations at the PLWG and the RPG new language was approved for Planning Guide section 3.1.7 via PGRR 42.
PG section 3.1.7 specifies the process used for determining Load level used in start cases for the Regional Transmission Plan (RTP) and Tier 1 independent review
PG section 3.1.7 (f) requires that
“ERCOT-proposed revisions to the boundary threshold used to implement the requirements of this section will be recommended by the Technical Advisory Committee (TAC) and approved by the ERCOT Board.”

## Slide 4: Recommendation
ERCOT proposes a boundary threshold of 5% be utilized
This number is based on
  experience from the load review dry run in 2017 RTP
  experience forecasting loads for the ERCOT region and review of historical differences
The 5% threshold was proposed for the trial run at the January 2017 RPG meeting – RPG stakeholders were neutral on this proposal

## Slide 5: Load Forecast Review Process
ERCOT 90th percentile Forecast
SSWG Load Level
5% Bound
ERCOT 90th percentile Forecast
SSWG Load Level
5% Bound
ERCOT 90th percentile Forecast
SSWG Load Level
Justified?
RTP Load Level
RTP Load Level
RTP: Loads compared by weather zone
Tier 1 RPG review: Loads compared by TO (if necessary)

## Slide 6: RTP/Tier 1 Load Level
5% Bound
ERCOT 90th percentile Forecast
SSWG Load Level
5% Bound
ERCOT 90th percentile Forecast
SSWG Load Level
5% Bound
ERCOT 90th percentile Forecast
SSWG Load Level
SSWG Load Level
RTP Load Level
RTP Load Level
RTP Load Level

## Slide 7: Results from the load review dry run
3
2
2
Chart: Results from Load Review Dry Run
| Weather zones where SSWG Load is within 5% boundary | Weather zones identified for load review using 5% boundary | Weather zones where SSWG load < ERCOT 90/10 forecast
 | 2 | 4 | 2

## Slide 8: Conclusion & Next steps
ERCOT has developed procedures that will be used to review load forecasts
  The goal is to ensure that ERCOT is comfortable with the load forecasts
  ERCOT is appreciative of the support provided by TSPs
Seek TAC recommendation and Board approval on the proposal to use 5% as the boundary threshold

## Slide 9: Questions
Sandeep Borkar
Sandeep.Borkar@ercot.com
512-248-6642
Calvin Opheim
Calvin.Opheim@ercot.com
512-248-3944

## Slide 10
Appendix

## Slide 11: Bounded higher-of methodology (Conceptual)

## Slide 12: Load review process (Conceptual)
Rationale:
Historic load growth
Committed load additions
Forecast methodology
Past forecast performance
Special circumstances
Other?
Preliminary RTP start cases will be shared to allow TDSPs to review the impact of load distribution on pockets within the weather zones.

## Slide 13: Planning Guide 3.17 Reference
[PGRR042: Insert Section 3.1.7 below on January 1, 2018:]
3.1.7 Steady State Transmission Planning Load Forecast
(1) ERCOT shall use the following process for determining the Load level to be used in the starting base cases for the Regional Transmission Plan and in the steady-state evaluation of a Tier 1 project pursuant to Protocol Section 3.11.4, Regional Planning Group Project Review Process:
(a) ERCOT will compare the ERCOT 90/10 Load forecast with the summed SSWG bus-level Load forecast for each Weather Zone.
(b) If the ERCOT 90/10 Load forecast is higher, ERCOT will use this forecast for the Weather Zone.
(c) If the SSWG Load forecast is higher than or equal to the ERCOT 90/10 Load forecast, but below the ERCOT 90/10 Load forecast plus a boundary threshold determined in accordance with paragraph (f) below, ERCOT will use the SSWG Load forecast for the Weather Zone.
(d) If the SSWG Load forecast is higher than or equal to the ERCOT 90/10 Load forecast plus the boundary threshold, ERCOT will use the ERCOT 90/10 Load forecast plus the boundary threshold for the Weather Zone.

## Slide 14: Planning Guide 3.17 Reference (Cont.)
(e) If a TSP(s) believes that the ERCOT 90/10 Load forecast plus the boundary threshold does not adequately represent the Weather Zone or an area within the Weather Zone, the TSP(s) may present ERCOT with additional information to justify using a higher Load forecast, including the SSWG Load forecast, for that Weather Zone. ERCOT, in its sole discretion, may choose to use a higher Load forecast than indicated in paragraph (d) above if it reasonably determines that the Load forecast indicated in paragraph (d) above does not adequately represent the Weather Zone or an area within the Weather Zone. If ERCOT uses a Load forecast higher than the ERCOT 90/10 Load forecast plus the boundary threshold in the evaluation of a Tier 1 project, ERCOT must explain and document the basis for that choice, using aggregated information as needed to shield Protected Information, in its independent review.
(f) ERCOT-proposed revisions to the boundary threshold used to implement the requirements of this section will be recommended by the Technical Advisory Committee (TAC) and approved by the ERCOT Board.