## Slide 1
<number>
Profiling Working Group
Update to COPS
October 10th, 2017
Sheri Wiegand (TXU) – Chair
Sam Pak (Oncor) – Vice-Chair
Notes: <number>

## Slide 2
Annual Validation Update – no change
<number>

## Slide 3
Annual Validation Update
<number>
September 27, 2017 PWG Meeting
  All TDSPs report 814_20 submittals are complete
  ERCOT to review submittals and provide list of any missing via MarkeTrak
  Investigative discussion regarding current AV process reviewing:
    “Flip – Flops” from year to year
    Verification of changes
    Weather impacts

## Slide 4: Annual Validation – Investigative Process
Annual Validation Study - Process
AV algorithms for AMS changes were re-run for 2015 – 2017 (CenterPoint territory only)
Each AV has a three year look back
Only the winter months of January and February are considered
To be included, ESIs must have 90% of the data for the 6 months reviewed
Calculation of the correlation (RSQ) of Average Dry Bulb temperature verses Daily Usage
  If 3 of the 6 months >= 0.6 , then RESLO to RESHI profile
  If 6 of the 6 months <= 0.4 , then RESHI to RESLO profile
<number>
Notes: <number>

## Slide 5: Annual Validation – Investigative Process – cont.
Annual Validation “Flip-flops”
Given the algorithms, IDR meters (including AMS) will not ‘flip-flop’ in two consecutive years (i.e. RESHI to RESLO one year and the next year back to RESHI)
Only NIDR meters may change every year as the algorithm is different
For the study population (CNP residential)…
  2017 AV: 43,505 profile changes
    2016 AV: Only 6 (NIDR) ESIs were on the change list for both
    2015 AV: 499 (NIDR/IDR) ESIs were changing back
<number>
Less than one-tenth of a percent of AV ESIs ‘flip-flopped”.

## Slide 6: Annual Validation – Investigative Process – cont.
Annual Validation Weather Impacts – 2015
<number>
More cooler winters in the evaluation will result in a higher number of changes from RESLO to RESHI which is indicative of electric heating.

## Slide 7: Annual Validation – Investigative Process – cont.
Annual Validation Weather Impacts - 2016
<number>
More mild winters result in fewer profile changes.

## Slide 8: Annual Validation – Investigative Process – cont.
Annual Validation Weather Impacts - 2017
<number>
When all review periods are warmer winters, correlations resulting in a larger number of ESIs moving from RESHI to RESLO.
Concern if this accurately represents an ESIs cold weather response (electric heat).

## Slide 9: Annual Validation – Investigative Process – cont.
<number>
PWG is further reviewing proposed ‘once a RESHI, always a RESHI’ suggestion and if warranted will submit an LPGRR.
Conclusions
No significant flaws were found in the AMS/IDR algorithm for residential changes
Profile changes are highly dependent on the severity of winter
Future Considerations
Once an ESI proves its response to cold temperatures, ESI remains on RESHI profile
Change RSQ correlation values and/or algorithm
Only review NIDR ESIs for AV

## Slide 10
<number>
Next PWG meeting date:
October 25th, 2017 WebEx only
9:30 am
AGENDA
Annual Validation update & discussion
  Status update
  Review of proposed LPGRR regarding RESHI load profiles
http://www.ercot.com/committees/board/tac/cops/pwg/

## Slide 11
<number>