## Slide 1
Southern Cross Transmission Directives
Ancillary Service Related
October 2017 PDCWG/OWG
ERCOT Staff

## Slide 2: Summary
Directives | Area | Working Group
Directive #8 - Frequency and Voltage support | Primary frequency response study | PDCWG (ROS)
 | Study voltage support requirements | RPG at the conclusion of Directive #5 (Other)
Directive #9 - Ancillary Services | Issues related to MSSC and margin between min RRS procurement, Contingency Reserve requirements Issues related to study of frequency overshoot and LRs UFR setting to DWG | OWG (ROS)
 | Issues related to NSRS and Regulation Service | PDCWG (ROS)
 | Issues related to study of frequency overshoot and LRs UFR setting | DWG (ROS)

## Slide 3: Directive #8
Issues & Corresponding Studies:
Primary frequency response study PDCWG
  Review existing PFR & Voltage Support requirements for DC Ties
  Examine the benefits & feasibility of a DC-Tie to have a Governor-like response.
  Examine if requirements should be put in place to require DC-Tie to temporarily suspend ramping when system frequency deviation is larger than a certain threshold.
ERCOT shall (a) study and determine whether Southern Cross Transmission or any other entity scheduling flows across the Southern Cross DC tie should be required to provide or procure voltage support service or primary frequency response, or their technical equivalents, (b) implement any necessary revisions to its standards, guides, systems, and protocols, as appropriate, and (c) certify to the Commission when it has completed these actions.
October 11 PDCWG Meeting

## Slide 4: Directive #9
ERCOT shall (a) evaluate what modifications to existing and additional ancillary services, if any, are necessary for the reliable interconnection of the Southern Cross DC tie, (b) implement any needed modifications to ancillary-services procurement, (c) recommend how the costs of such required ancillary services are to be allocated, and (d) certify to the Commission when it has completed these actions.
Issues & Corresponding Studies:
Most Severe Single Contingency (MSSC) OWG
  1375 MW or 2100 MW?
Non-Spin Reserve Service has a minimum floor based on MSSC from 6 am to 10 pm. OWG & PDCWG
  Reconcile the MSSC with existing Non-Spin floor for on-peak hours.
Margin between minimum Responsive Reserve Service (RRS) procurement (2300 MW) and minimum Contingency Reserve (MSSC based) requirement. OWG
  Examine if changing MSSC (i.e. min Contingency Reserve) will bring a corresponding need to change RRS floor.
Impact on Regulation Service during DC-Tie ramps PDCWG
  Study the impact of DC-Tie ramps on Regulation, Non-Spin & RRS requirements
October 11 PDCWG & October 20 OWG

## Slide 5: Directive #9 (cont’d)
ERCOT shall (a) evaluate what modifications to existing and additional ancillary services, if any, are necessary for the reliable interconnection of the Southern Cross DC tie, (b) implement any needed modifications to ancillary-services procurement, (c) recommend how the costs of such required ancillary services are to be allocated, and (d) certify to the Commission when it has completed these actions.
Issues & Corresponding Studies:
Study impact on Frequency due to forced outage of DC Tie while exporting or importing. PDCWG, DWG & DSWG
  Study impact on system frequency due to DC-Tie trip when exporting and evaluate if a new type of A/S product may be needed to arrest the resulting frequency overshoot.
  Evaluate the risk of & frequency of triggering Load Resources due to DC-Tie trips when importing. Examine if the under-frequency relay settings for Load Resources warrant a change.