## Slide 1
2018 LTSA Current Trends load forecast
November 2017
RPG Meeting

## Slide 2: Agenda
Load forecast trends

## Slide 3: Load forecast trends
Chart: Load forecast trends
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038
NCP - LTSA 2018 CT (2009 weather year) - Pun adjusted | 78496.5625 | 80071.4146 | 81233.8293 | 82381.1024 | 83703.8356 | 85017.8498 | 86184.1932 | 87273.631 | 88506.4423 | 89748.7198 | 91005.2543 | 92328.3167 | 93639.4975 | 94961.176 | 96237.787 | 97503.0232 | 98777.5156 | 100056.9623 | 101323.4327 | 102584.6652 | 104069.8308
LTSA 2016 CT - 2006 weather year - final pun adjusted | 74551.5727 | 74763.5542 | 75613.6311 | 76195.6357 | 76858.1615 | 77284.4325 | 77824.5927 | 78411.1677 | 78738.8969 | 79125.3017 | 79755.5484 | 80184.5648 | 80849.7388 | 81516.3022 | 81787.8833

## Slide 4: Current Trends forecast assumptions
Based on 2017 LTDF for the 2009 weather year
Existing EE savings included in the LTDF – no additional EE growth adjustments included
1000 MW of rooftop PV distributed evenly on a load share basis across all weather zones
*values are for the 2031 summer peak demand

## Slide 5: Reasoning for increase
The 2016 CT forecast had 2,800 MW of EE and 300 MW of rooftop PV
The 2016 CT forecast was based on 2006’s weather which results in a peak forecast that is 1,200 MW less when compared to using 2009’s forecast
The 2018 CT forecast is 3,500 MW higher for Coast, 3,300 MW higher for Far West, 2,100 MW higher for South Central, and 1,700 MW higher for South
The 2018 CT forecast is 1,800 MW lower for North Central
*values are for the 2031 summer peak demand