## Slide 1: Commercial Operations Subcommittee (COPS) IDR Meter Reads Problem Statement 11-30-2017

## Slide 2: IDR METER READS
Problem Statement
Approximately 24% of ERCOT Load meter data is not available for Initial Settlement
(15-Minute IDR Meter Data submitted by TDSPs monthly, therefore, ERCOT estimates 15-Minute usage data based on proxy day data for Initial Settlement. TDSP data for IDR metered premises is available for Final and/or True-up Settlements.)
Notes: <number>

## Slide 3: IDR METER READS
Impacts
Settlements
  Unaccounted For Energy (UFE)
  Load Ratio Charge Types
    Real-Time Energy Imbalance (RTEIAMT)
    “Allocation to Load” Charge Types, E.g., Ancillary Services Obligation, Admin Fee, and CRR Balancing Account (Based on Initial MLRS, not trued-up)
  Competitive Retailer (CR) and Retail Customer Cash Flow and Financial Reporting
Credit: ERCOT, CR or Retail Customer
Demand Integration
Notes: <number>

## Slide 4: IDR METER READS
Solution Impact Considerations:
TDSP specific Tariff changes may be required for IDR Metered Premise(s) and/or TDSPs’ application of 4CP
AMS Meters cannot be deployed for all “BUSIDRRQ” Profiled Premises due to:
  Some Billing Determinants required by TDSP specific Tariffs are not currently available through AMS Metering technology
  Location of Metering equipment may create communication issues – I.e., meter vault location or company’s basement
Notes: <number>

## Slide 5: IDR METER READS
Additional Impact Considerations:
Retail Customer impacts may be experienced since some meter data may not be available to the Customer’s Energy Management System without the availability of a Private Use Network
CRs may continue to require the 867_03 Monthly Usage Interval Data, as well as, receiving their daily data from ERCOT for Customer invoicing
A Market solution may require system changes by CRs, TDSPs and/or ERCOT
Notes: <number>

## Slide 6: The Numbers by Meter Type
Sample Month: June 2017
NIDR – Non-Interval Data Recorder Meter or Scalar Meter
AMS – Advanced Meter System or Smart Meter
NOIE – Non-Opt in Entity
COMP_IDR - Competitive IDR or BUSIDRRQ (≈68% >= 700 kW/kVA and ≈32% < 700 kW) )
Meter Type | Number of Meters | Load by Meter Type (MWh) | Percent of Load by Meter Type (%) | Percent of Actual Meter Data Used for Initial Settlement (%) | Percent of Estimated Meter Data Used for Initial Settlement (%)
NIDR | 234,507 | 343,316 | 1% | 1% | 0%
AMS | 7,078,892 | 15,495,009 | 45.50% | 45.50% | 0%
NOIE | 1,405 | 8,939,979 | 26.30% | 24.20% | 2%
COMP_IDR | 12,212 | 9,270,890 | 27.20% | 3.70% | 24%
Total | 7,327,016 | 34,049,194 | 100% | 74.40% | 26%
Notes: <number>

## Slide 7: Daily UFE
  Daily Load Change from January 1, 2016 through March 31, 2017
Notes: <number>

## Slide 8: Monthly UFE
  UFE Monthly Average from July 2016 through March 2017
  Initials: Between -0.98% and 0.79%
  Finals: Between 0.03% and 0.5%
  Monthly Load Change from January 1, 2016 through March 31, 2017
  AMS: Between -1,935 MWh and 1,028 MWh
  NIDR: Between -6,848 MWh and 1,821 MWh
  BUSIDRRQ: Between -50,919 MWh and 45,857 MWh
Notes: <number>

## Slide 9: Cash Flow and Financial Reporting
  Competitive Retailers and Retail Customers
  Incur erroneous costs due to load estimation
  Experience sporadic cash flow
  Cannot close their accounting books until after Final Settlement for the whole month is complete (55 days after the last day of the month)
  Cannot provide good financial reporting until after Final Settlement for the month is complete
Notes: <number>

## Slide 10: Retail Customer Cash Flow
Example: Large Industrial Retail Customer
Notes: <number>

## Slide 11: Credit
ERCOT Credit Impacts:
Adjusted Metered Load (AML) based on estimated IDR meter data has an impact, directly or indirectly, on the following Credit components:
  Minimum Current Exposure (MCE)
  Real Time Liability (RTL)
  Real Time Liability Extrapolated (RTLE)
  Real Time Liability Completed and Not Settled (RTLCNS)
  Real Time Liability Forward (RTLF)
  Outstanding Invoice Amounts (OIA)
  Unbilled Final Amount (UFA)
  Unbilled Real-Time Amount (URTA)
Notes: <number>

## Slide 12: Credit
Low Initial Estimate:
  A low load estimate could result in ERCOT requiring insufficient credit support from a Counter Party to cover its obligations
  A large adjustment up in Final Settlement could result in a higher uplift to the market in the event of a default
High Initial Estimate:
  A high load estimate will result in ERCOT requiring more credit support from a Counter Party than necessary, which will persist until the initial invoice rolls out of the Real-Time Liability Extrapolated (RTLE) calculation
Notes: <number>

## Slide 13: Demand Integration
  While the majority of the customer sites participating in Emergency Response Service (ERS) have AMS meters, the majority of the response continues to be from customer sites with IDR meters
  The evaluation of ERS resource performance for tests, events, and contract term availability are dependent on the availability of the corresponding meter data
  More timely performance determination would allow ERCOT to provide quicker feedback to ERCOT Operations and QSEs providing ERS on the amount of ERS capacity available and ERS QSEs would have more timely information to use to take corrective action and to anticipate performance implications on payments
Notes: <number>

## Slide 14: IDR METER READS
In addition…
Approximately 14% of ERCOT Non-Modeled Distributed Generation (DG) meter data is not available for Initial Settlement
(15-Minute IDR Data is submitted by TDSPs monthly, therefore it is not available until Final and/or True-up Settlements.)
Notes: <number>

## Slide 15: The Numbers For Non-Modeled DG
Sample Month: June 2017
DG – Distributed Generation
EPS – ERCOT Polled Settlement Meter
IDR – Interval Data Recorder
Meter Type | Initial Non-Modeled DG Settlement (MWh) | Final Non-Modeled DG Settlement (MWh) | Non-Modeled DG Meter Data Not Available for Initials (MWh) | Percent of Non-Modeled DG Meter Data Available for Initial Settlement (%) | Percent of Non-Modeled DG Meter Data Not Available for Initial Settlement (%)
EPS and IDR | 58,962 | 68,865 | 9,903 | 86% | 14%
Notes: <number>

## Slide 16: Non-Modeled DG Cash Flow
Example: Non-Modeled DG
Notes: <number>

## Slide 17: IDR Meter Reads
Goal:
Submission of TDSP read meter data for Loads with Interval Data Recorder Meters and Non-Modeled Distributed Generators with Interval Data Recorders prior to Initial settlement of an Operating Day.
Notes: <number>

## Slide 18: IDR METER READS
Questions?
Next Steps?

## Slide 19: Appendix A - Definitions
Interval Data Recorder (IDR)
A metering device that is capable of recording energy in each Settlement Interval under Section 9, Settlement and Billing, and Section 10, Metering.
Interval Data Recorder (IDR) Meter
An IDR where the ESI ID is required to be assigned a BUSIDRRQ Load Profile Type code and data is submitted in accordance with Section 10.3.3.3, Submission of Settlement Quality Meter Data to ERCOT.
Notes: <number>

## Slide 20: Appendix A - Definitions
Non-Modeled Generator
Capable of producing energy
Cannot provide Ancillary Services
Less than 10MW
Greater than 10MW and registered with PUCT as a Self-Generator
Settled at a Load Zone
Notes: <number>