## Slide 1
Proposed Ancillary Service Methodology And Quantities For 2018
ERCOT Staff

## Slide 2: Schedule for Stakeholder Discussion
Sep 15, 2017 – QMWG (w Current Methodology)
Oct 09, 2017 – QMWG (w Proposed Changes)
Oct 11, 2017 – PDCWG
Nov 01, 2017 – WMS (Endorsed Unanimously)
Nov 02, 2017 – ROS (Endorsed Unanimously)
Nov 30, 2017 – TAC
Dec 12, 2017 – BOD

## Slide 3: Scope of Discussion
ERCOT is not proposing any changes to the methodology for determining Regulation Service & Responsive Reserve quantities for 2018.
ERCOT is proposing two changes to the methodology for determining Non-Spin Reserve for 2018.
A redline version of the draft methodology and spreadsheets that contain the associated preliminary quantities for January through October of 2018 have been posted on the meeting page for November 30 TAC meeting.

## Slide 4: Regulation Service Methodology – 2018
The preliminary Regulation quantities for January 2018 thru October 2018 have been computed using current methodology (2016 and 2017 five-minute net load variability) and Wind Adjustment tables.
The Wind Adjustment tables (previously called “GE Tables”) track incremental MWs of Regulation needed to account for additional variability per 1000 MW increase in installed Wind capacity.
  This table has been updated for 2018.

## Slide 5: Hourly Avg. Regulation Comparison
Chart: MW
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
2017 Reg Down | 279 | 291 | 277 | 298 | 322 | 312 | 314 | 312.5 | 308.9583 | 302.9583
2018 Reg Down | 283 | 292 | 295 | 296 | 320 | 301 | 304 | 301.7083 | 308.7917 | 293.8333
Chart: MW
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
2017 Reg Up | 309 | 315 | 302 | 318 | 340 | 332 | 335 | 343.125 | 332.5833 | 315.9583
2018 Reg Up | 299 | 309 | 306 | 316 | 339 | 330 | 333 | 331.0417 | 326.375 | 308.5833

## Slide 6: Responsive Service Methodology (RRS) - 2018
The preliminary RRS quantities for January 2018 thru October 2018 have been computed using current methodology (2016 and 2017 system inertia conditions) and updated RRS table.
    The RRS quantities for 2018 do not reflect any potential impact of recent NSOs.
The RRS table tracks RRS requirements for different inertia conditions.
  This table has been updated for 2018. The increments in inertia levels are now uniform across all study scenarios.

## Slide 7: Hourly Avg. RRS Comparison
Chart: RRS Hourly Average
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
2017 RRS | 2700 | 2733.3333 | 2734.3333 | 2734.3333 | 2625.6667 | 2493.6667 | 2369.5 | 2379.3333 | 2503.5 | 2662
2018 RRS | 2828.7604 | 2880.9017 | 2849.9907 | 2858.7325 | 2715.2892 | 2502.7574 | 2410.1652 | 2440.375 | 2554.2262 | 2783

## Slide 8: Non Spinning Reserve Methodology (NSRS) - 2018
ERCOT is proposing two changes to Non Spin Service Methodology for 2018.
  Include solar generation and solar forecast in the calculations for Net Load and Net Load Forecast i.e. include effects of solar in Net Load Forecast error & Net Load up ramp risk calculation.
  Include an adjustment to account for additional over-forecast uncertainty from projected increase in installed wind capacity in 2018.
The preliminary Non Spin quantities for January 2018 thru October 2018 have been computed using the above changes to the current methodology (2015, 2016 and 2017 Net Load Forecast Error and risk of Net Load Ramp).

## Slide 9: Adjustment to Non-Spin based Wind Growth – 2018
Average hourly adjustment to Non Spin Requirement = 121 MW

## Slide 10: NSRS Jan 2018
*1375 MW Floor in On-peak hours (HE 7 thru 22)
Chart: NSRS Requirement - Jan 2018
Jan-17 | 925 | 1231 | 1910 | 1792 | 1503 | 1511
A - Current Methodology | 981.3758 | 1276.8589 | 1982.8866 | 1561.4997 | 1566.0122 | 1471.6153
C - Proposed Methodology (Jan-18) | 1103.1611 | 1409.3312 | 2130.7142 | 1683.4318 | 1673.5285 | 1605.2033

## Slide 11: NSRS Mar 2018
Chart: NSRS Requirement - Mar 2018
Mar-17 | 935 | 1470 | 2135 | 1947 | 1472 | 1490
A - Current Methodology | 827.064 | 1367.2272 | 1960.1367 | 1715.3568 | 1466.2371 | 1375
C - Proposed Methodology (Mar-18) | 967.35 | 1505.479 | 2110.6969 | 1819.0263 | 1572.4043 | 1387.0741

## Slide 12: NSRS Aug 2018
Chart: NSRS Requirement - Aug 2018
| HE1-2 & HE23-24 | HE3-6 | HE7-10 | HE11-14 | HE15-18 | HE19-22
Aug-17 | 855 | 1218 | 1853 | 1558 | 1375 | 1375
A - Current Methodology | 1130.8243 | 1404.1368 | 1889.4851 | 1668.2785 | 1375 | 1375
C - Proposed Methodology (Aug-18) | 1255.8961 | 1525.1639 | 2002.6156 | 1751.8239 | 1375 | 1375

## Slide 13: Hourly Avg. NSRS Comparison
Chart: NSRS Hourly Average
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
2017 NSRS | 1478.6667 | 1690 | 1574.8333 | 1440.5 | 1605.1667 | 1522.1667 | 1303.5 | 1372.3333 | 1577.6667 | 1587.8333
A - Current Methodology | 1473.3748 | 1554.7708 | 1451.837 | 1384.3516 | 1457.1951 | 1454.9086 | 1329.6533 | 1473.7874 | 1481.8256 | 1474.2155
C - Proposed Methodology (2018 NSRS) | 1600.895 | 1673.6912 | 1560.3384 | 1497.2606 | 1601.2933 | 1542.6263 | 1385.8389 | 1547.5833 | 1584.6075 | 1569.9164

## Slide 14: Summary
Following is a summary of the 2018 A/S Methodology,
  ERCOT is not proposing any changes to the methodology for determining Regulation Service & Responsive Reserve quantities for 2018.
  ERCOT is proposing two changes to the methodology for determining Non-Spin Reserve for 2018.
ERCOT is seeking TAC’s endorsement for the 2018 Ancillary Service Methodology.