## Slide 1
Market Update
QSE Managers Working Group
Market Analysis
12/4/2017

## Slide 2: Supplemental Ancillary Services Market (SASM) Update
Insufficiency shown above and in MIS reports caused by rounding

## Slide 3: Manual Overrides
No manual overrides

## Slide 4: SASM Timeline Discussion
System implementation can cause the first hour for offline units to be eligible for an award to be later than might be expected
X
X+30 min
X+35 min
X+45 min
X+60 min
First hour for a resource with Y hour start time to be eligible for an award
Notify Market
Determine AS amount
Execute SASM
Award Notification
COP Updated
12:00
12:30
12:35
12:45
???
1:00

## Slide 5: SASM Timeline Discussion
First hour eligible = SASM Execution Time + 1 Hour Time Delay + Start Up Time
The 1 Hour Time Delay was a hardcoded parameter but changed to a configurable parameter in June 2017
Delay is meant to account for execution time, award notification, and time to receive notification
X
X+30 min
X+35 min
X+45 min
X+60 min
Notify Market
Determine AS amount
Execute SASM
Award Notification
COP Updated
12:00
12:30
12:35
12:45
12:35 + 1 Hour Time Delay + Start Up Time
1:00
First hour for a resource with 3 hour start time to be eligible for an award

## Slide 6: SASM Timeline Discussion
For example, a resource with a 3 hour start time in the following timeline cannot be awarded until 5 AM (HE 6) even if SASM executed at 12:35 AM
X
X+30 min
X+35 min
X+45 min
X+60 min
Notify Market
Determine AS amount
Execute SASM
Award Notification
COP Updated
12:00
12:30
12:35
12:45
12:35 + 1 hour delay + 3 hour start time = 4:35 rounds up to 5:00 (HE 6)
1:00
First hour for a resource with 3 hour start time to be eligible for an award

## Slide 7: Example with 30 Minute Delay
For example, a resource with a 3 hour start time in the following timeline cannot be awarded until 5 AM (HE 6) even if SASM executed at 12:35 AM
X
X+30 min
X+35 min
X+45 min
X+60 min
Notify Market
Determine AS amount
Execute SASM
Award Notification
COP Updated
12:00
12:30
12:35
12:45
12:35 + 30 minute delay + 3 hour start time = 4:05 rounds up to 5:00 (HE 6)
1:00
First hour for a resource with 3 hour start time to be eligible for an award

## Slide 8: Example with 15 Minute Delay
For example, a resource with a 3 hour start time in the following timeline can be awarded for 4 AM (HE 5) even if SASM executed at 12:35 AM
X
X+30 min
X+35 min
X+45 min
X+60 min
Notify Market
Determine AS amount
Execute SASM
Award Notification
COP Updated
12:00
12:30
12:35
12:45
12:35 + 15 minute delay + 3 hour start time = 3:50 rounds up to 4:00 (HE 5)
1:00
First hour for a resource with 3 hour start time to be eligible for an award

## Slide 9: 15 Minute Delay May Not Solve All Issues
Depending on timing, any amount of delay can still cause this issue to occur
For example, a resource with a 3 hour start time in the following timeline cannot be awarded for 4 AM (HE 5) even if SASM executed at 12:50 AM
X
X+30 min
X+35 min
X+45 min
X+60 min
Notify Market
Determine AS amount
Execute SASM
Award Notification
COP Updated
12:15
12:45
12:50
1:00
12:50 + 15 minute delay + 3 hour start time = 4:05 rounds up to 5:00 (HE 6)
1:15
First hour for a resource with 3 hour start time to be eligible for an award

## Slide 10: Options
Keep the configurable time delay parameter at 1 hour
Reduce the time delay
ERCOT has no specific recommendations but suggests against changing the time delay to less than 10 minutes to give a buffer for execution time and receiving the notification