## Slide 1
Summary of GIC Model Development on 01/12/2018
Presentation to PGDTF
Qiuli Yu and Leslie Williams
ERCOT
January 12, 2018

## Slide 2: RARF Update On January 09 of 2018
Substation
  Substation Current Records – 319
  Contact REs and correct coordinate missing issue – clean 12 records
  Substations with MacombMap coordinates decreases from 42 to 30
Transformer
  Query out 811 records
  9 transformers are in the expired gen sites
  We really need data of 802 transformers
  Transformers missing VG and RDC decreases from 136 to 93
ERCOT internal department and client service are working with REs
01/09/2018 | Total Records | Records with VG and RDC | Percent
Transformer | 802 | 709 | 88.4%

## Slide 3: TSPs GIC Data Submission and Data Issues
Data submission
  ERCOT spend one more week for TSPs’ delayed submissions
  ERCOT spend another week to review and suggest modifications to TSPs’ submissions
  TSPs, please send your submission as early as possible, at least by the deadline!
Data Issues
  Some bus – substation mappings are still missing:
637
732
2464
6702
33630
33646

## Slide 4: Issues with GIC Model Development
PSSE Version 34.3.1
  Can not create default GIC input file directly. Have to create Excel template first, then convert the Excel template to a *.gic file
  The Bus set was incomplete, and Siemens sent the patch
  Manually copy the complete set of buses from PSSE Network data
  May consult Siemens instructor during Feb. GIC training
  Switched Shunt Reactors
  PSSE GIC Module can only allow one switched shunt reactor at the same bus
  How to deal with two or three parallel switched shunt reactors at the same bus?