## Slide 1
Annual Validation Study
Of Residential AMS Change Counts
Using Varying Numbers
of Historical Years
Bill Boswell
PWG Meeting
December 12, 2017

## Slide 2: Study Details
The 2017 residential AMS validation used the previous three years of “winter” data as specified in the Profile Decision Tree
Winter is defined as January and February so the 2017 study used 6 months of data from 2015-2017
After discussing the large numbers of changes, the PWG requested ERCOT that study extending the historical period to 4 and 5 years
CenterPoint and ONCOR data were used because these TDSP’s have sufficient AMS residential meters to support the 4 and 5 year study

## Slide 3: Residential AMI Counts
Chart: Year
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
AEP TEXAS CENTRAL | 0 | 149520 | 319996 | 519787 | 689187 | 700194 | 708199 | 715037
AEP TEXAS NORTH | 0 | 58593 | 98653 | 132377 | 147907 | 148791 | 148698 | 149038
CENTERPOINT ENERGY | 130695 | 800896 | 1730168 | 1953342 | 1990474 | 2040155 | 2088078 | 2136314
ONCOR ELECTRIC DELIVERY | 525511 | 1344203 | 2073415 | 2755190 | 2791586 | 2833898 | 2873385 | 2918880
TEXAS-NEW MEXICO POWER | 0 | 0 | 31508 | 85310 | 115201 | 161578 | 186909 | 204504

## Slide 4: RESHI/RESLO Percentage Split by TDSP
Note: These percentages are based on the Profile Counts of March 2017
Chart: 
| AEP TEXAS CENTRAL | AEP TEXAS NORTH | CENTERPOINT ENERGY | ONCOR ELECTRIC DELIVERY | TEXAS-NEW MEXICO POWER | ERCOT
RESHIWR | 66.0665 | 49.4954 | 30.8469 | 58.657 | 45.9962 | 49.1747
RESLOWR | 33.9335 | 50.5046 | 69.1531 | 41.343 | 54.0038 | 50.8253

## Slide 5: RESLO to RESHI
If the existing assignment is LOWR (or a DG variation such as LOPV) then
if the required data were not available to calculate R-square values
for any of the 6-10 months then do not change assignment;
else if NYears = 3 AND any 3 of the 6 R-square value is >= 0.6
then assign HIWR;
else if NYears = 4 AND any 5 of the 8 R-square values is >= 0.6
then assign HIWR;
else if NYears = 5 AND any 7 of the 10 R-square values is >= 0.6
then assign HIWR;
else do not change assignment.

## Slide 6: RESHI to RESLO
If the existing assignment is HIWR (or a DG variation such as HIPV) then
if the required data were not available to calculate R-square values
for any of the 6-10 months then do not change assignment;
else if NYears = 3 AND all 6 R-square values are <= 0.4
then assign LOWR;
else if NYears = 4 AND all 8 R-square values are <= 0.4
then assign LOWR;
else if NYears = 5 AND all 10 R-square values are <= 0.4
then assign LOWR;
else do not change assignment.

## Slide 7: RES Change Counts Using 3-5 Historical Years