## Slide 1
Annual TAC Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2017
ERCOT Market Analysis and Validation
January 25, 2018

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: RUC-Committed Effective Resource-Hours

## Slide 4: RUC-Committed Resource-Hours in 2017
(*) - The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, or still being off-line for some portion of the RUC-committed hours or Resources not following RUC instructions
 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 562 | 165 | 397
Effective Resource-Hours (*) |  |  | 
Total Count | 534 | 163 | 371
Average LSL | 109 | 99 | 115
Average LDL | 142 | 144 | 141
Average BP | 156 | 164 | 151
Average HSL | 291 | 211 | 337

## Slide 5: RUC Commitment Reasons
534 effective RUC resource-hours in 2017
  433 resource-hours (81%) for congestion
  66 resource-hours (12%) for capacity
  35 resource-hours (7%) for Hurricane Harvey
There were no resource-hours of commitment for ancillary service shortages, system inertia, or extreme cold weather/startup failures
163 effective resource-hours (31%) were successfully bought back
  This value is similar to what was observed in previous years

## Slide 6: RUC Committed Resources Dispatched above LDL
When Resources did not successfully opt out, there were 68 resource-hours when the Resource was dispatched above its LDL
  For 58 resource-hours, the RUC-instructed Resource was mitigated
    Expected given the number of RUC instructions for local congestion
  For 2 resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor
  For 8 resource-hours, the RUC-instructed Resource was not mitigated and the LMP at the Resources was less than the RUC offer floor.
    This implies an issue with the Energy Offer Curve (EOC) for the Resource

## Slide 7: Reliability Deployment Price Adders
Month of 2017 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
JAN | 2 | 244.25
FEB | 19 | 0.84
MAR | 9 | 0.80
APR | 41 | 0.40
MAY | 29 | 9.94
JUN | 47 | 4.35
JUL | 31 | 1.05
AUG | 58 | 0.58
SEP | 42 | 0.61
OCT | 16 | 12.48
NOV | 8 | 0.46
DEC | 4 | 0.35

## Slide 8: RUC Make-Whole and Claw Back 2014 - 2017
** 2017- $540K in Make-Whole paid out. Only $1.67 was uplifted to Load.

## Slide 9: RUC Improvements in 2017
RUC shadow price cap reduction (April) – shadow price caps for transmission constraints in RUC reduced from about $1,000,000/MWh to about $100,000/MWh
NPRR744 implementation (June) - Fixed the opt-out decision inconsistency between the SCED and Settlements systems by using the same trigger for both systems
Provided additional constraint information from all RUC iterations to Operators
  Previously, only the final iteration was displayed (September)
Improved logic for notification times on Resources that are coming out of an outage (November)

## Slide 10: Conclusions
In 2017, 562 instructed RUC resource-hours resulted in 534 effective RUC resource-hours
  As compared to 1,514 and 1,417 for all of 2016, respectively
  31% of effective resource-hours were bought back
The total RUC make-whole amount was ~$0.54M
  Primarily covered through capacity-short charges
Implementation of NPRR744 resolved common inconsistencies between settlement treatment and the triggering of the Reliability Deployment Price Adder
Discussions on ways to enhance both RUC functionality and transparency are continuing between ERCOT and the stakeholders

## Slide 11: Appendix

## Slide 12: RUC-Committed Effective Resource-Hours by Opt Out Status
Month | 2014 | 2015 | 2016 | 2017
Jan | 88 | 8 | 33 | 7
Feb | 547 | 0 | 28 | 20
Mar | 305 | 0 | 47 | 14
Apr | 51 | 8 | 62 | 47
May | 82 | 71 | 74 | 33
Jun | 38 | 9 | 111 | 52
Jul | 11 | 6 | 222 | 39
Aug | 7 | 10 | 83 | 76
Sep | 1 | 75 | 111 | 54
Oct | 24 | 75 | 155 | 16
Nov | 389 | 0 | 20 | 8
Dec | 7 | 0 | 0 | 5
Month | 2014 | 2015 | 2016 | 2017
Jan | 0 | 0 | 11 | 2
Feb | 17 | 0 | 12 | 0
Mar | 94 | 0 | 0 | 0
Apr | 0 | 0 | 11 | 0
May | 2 | 6 | 57 | 20
Jun | 0 | 45 | 165 | 76
Jul | 0 | 5 | 96 | 27
Aug | 0 | 6 | 49 | 23
Sep | 0 | 9 | 59 | 12
Oct | 2 | 64 | 13 | 0
Nov | 0 | 0 | 0 | 3
Dec | 0 | 0 | 0 | 0
Did Not Opt Out
Opted Out

## Slide 13: RUC Make-Whole and Claw Back 2014-2015
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2014 | 2015 | 2014 | 2015 | 2014 | 2015 | 2014 | 2015 | 2014 | 2015
Jan | -135 | 0 | 135 | 0 | 0 | 0 | 908 | 23 | 988 | 0
Feb | -2165 | 0 | 2139 | 0 | 26 | 0 | 437 | 0 | 6123 | 0
Mar | -402 | 0 | 402 | 0 | 0 | 0 | 1272 | 0 | 3044 | 0
Apr | -161 | -5 | 161 | 5 | 0 | 0 | 0 | 0 | 698 | 114
May | -171 | -240 | 171 | 240 | 0 | 0 | 15 | 3 | 1425 | 941
Jun | -187 | -16 | 187 | 16 | 0 | 0 | 0 | 0 | 583 | 203
Jul | -1 | -2 | 1 | 2 | 0 | 0 | 29 | 10 | 78 | 33
Aug | -9 | -13 | 9 | 13 | 0 | 0 | 13 | 0 | 121 | 318
Sep | 0 | -139 | 0 | 139 | 0 | 0 | 0 | 175 | 44 | 1688
Oct | -29 | -76 | 29 | 76 | 0 | 0 | 59 | 126 | 608 | 1098
Nov | -540 | 0 | 540 | 0 | 0 | 0 | 123 | 0 | 4242 | 0
Dec | -31 | 0 | 31 | 0 | 0 | 0 | 0 | 0 | 250 | 0

## Slide 14: RUC Make-Whole and Claw Back 2016-2017
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2016 | 2017 | 2016 | 2017 | 2016 | 2017 | 2016 | 2017 | 2016 | 2017
Jan | -29 | 0 | 29 | 0 | 0 | 0 | 0 | 228 | 499 | 0
Feb | -4 | -7 | 4 | 7 | 0 | 0 | 38 | 0 | 192 | 206
Mar | -13 | -79 | 13 | 79 | 0 | 0 | 608 | 0 | 212 | 467
Apr | -70 | -175 | 70 | 175 | 0 | 0 | 3 | 0 | 1673 | 1387
May | -45 | -21 | 45 | 21 | 0 | 0 | 88 | 640 | 1569 | 208
Jun | -176 | -40 | 176 | 40 | 0 | 0 | 115 | 163 | 2229 | 490
Jul | -372 | -57 | 372 | 57 | 0 | 0 | 156 | 34 | 3341 | 627
Aug | -138 | -121 | 138 | 121 | 0 | 0 | 2 | 15 | 2427 | 873
Sep | -240 | -25 | 240 | 25 | 0 | 0 | 46 | 79 | 2447 | 759
Oct | -153 | -4 | 153 | 4 | 0 | 0 | 81 | 47 | 3581 | 159
Nov | 0 | -10 | 0 | 10 | 0 | 0 | 275 | 25 | 145 | 147
Dec | 0 | -2 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 77