## Slide 1
Real Time Co-Optimization of Energy and AS
ERCOT
January 31, 2018

## Slide 2: RTC Procedural History
Initial white paper in late 2014 with discussions at SAWG throughout 2015
White paper last updated in February 2016
  Includes two high level approaches
  Requires further stakeholder input and decisions
Worthwhile to provide an RTC review given the time that has passed

## Slide 3: RTC Procedural History
Project 47199 – Project To Assess Price-Formation Rules In ERCOT'S Energy-Only Market
  Many Stakeholders have filed comments regarding issues on price formation in ERCOT – RTC is one of the issue they have opined on
  ERCOT updated the project regarding a Local Reserve Product as part of RTC in comments filed 9/29/17
  ERCOT updated the project regarding RTC Cost Benefit studies in comments filed 12/7/2017
Project 41837 - PUCT Review of RTC in the ERCOT Region
  Update on ERCOT and Stakeholder Activities Related to RTC was filed 7/14/2017
    Provides a high level RTC activities summary
    Discussion on coordination of the VOLL, SWOC, and Max value on the Ancillary Services Demand Curves
    Update on the RTC Cost and Time Estimates
RTC Cost Benefit Studies
  The IMM and ERCOT are working together to simulate the introduction of RTC in historical Security Constrained Economic Dispatch ("SCED") cases. Estimated to be complete in 6 months (June 2018).
  ERCOT is analyzing improvements that RTC could have on the RUC Optimization.
  ERCOT is conducting an assessment of the effect that the existence of RTC may have on historical SASM activity

## Slide 4: Impacts of Ancillary Service Capacity (Reserves) on LMP (from PJM education materials)
Regardless of methodology, reserves and energy come from the same supply pool.
Allocating portions of the supply pool to each requirement will, at times, impact the marginal clearing price of both.
In general, allocating resources to energy and reserves must be done SIMULTANEOUSLY to minimize the impacts of one product on the other in order to globally minimize the cost of both.
If allocating resources to energy and reserves is done sub-optimally, the impacts of one product on another will be overstated. i.e. when required Ancillary Services and energy are not procured simultaneously

## Slide 5: What is RTC and How does it Differ from the Current ORDC?
RTC allows for the optimal coordination of the provision of energy and AS among all resources in the real-time market and, similar to the current ORDC, the pricing of AS shortages in accordance with defined AS demand curves
Unlike the current ORDC, a demand curve for each ancillary service would be applied within the SCED engine to allow SCED to internally optimize the provision of energy and AS among all resources, subject to each resources’ capabilities and offers
  AS capacity is no longer blocked from SCED by the HASL
  Establishes offer-based prices for AS capacity and energy in the real-time market through SCED under normal operating conditions, and under AS shortage conditions in accordance with the defined AS demand curves

## Slide 6: Key Changes Associated with the Implementation of RTC
The pricing of operating reserve shortages as a function of VOLL and LOLP under RTC is generally consistent with the approximation achieved under ORDC B+
The following represent key changes associated with RTC beyond ORDC B+:
Least cost provision of energy and ancillary services
Potential reduction in RUC and SASM activity
Reduced risk and increased opportunity for resources
Fewer manual processes by ERCOT operators

## Slide 7: 1. Least-cost Provision of Energy and AS
Real-time conditions often vary from the day-ahead and can change the resources that are optimal to provide energy and AS
For example, a transmission constraint could bind in the RTM and cause a resource selected in the DAM to provide AS to be more economic in real-time to provide energy than reserves
  RTC would automatically shift the AS from the resource in the constrained area to a resource outside the constrained area in a manner that is economically advantageous to both resources, and benefits loads by selecting the lowest cost resources to provide energy and AS
  Can also provide reliability benefits compared to the current market design when AS capacity in an import-constrained area may prevent access by SCED to energy required for congestion relief

## Slide 8: 2. Potential Reduction in RUC and SASM Activity
Implementation of RTC would also include modifications to the RUC engine, such that the ability to coordinate the provision of energy and AS among resources in the RTM would be recognized in RUC
Compared to the current market, offers the potential to reduce RUC activity, particularly in broader import-constrained areas
SASM activity would be reduced due to the coordinated access to the ERCOT portfolio of resources for the provision of energy and AS in RT

## Slide 9: 3. Reduced Risk and Increased Opportunity for Resources
Access by individual resources to the ERCOT portfolio of energy and AS in real-time
  Less SASM activity and access to the ERCOT portfolio of energy and AS in real-time results in less financial risk compared to current SASM process
  Increased opportunity for individual resources to economically optimize the provision of energy and AS in the real-time market

## Slide 10: 4. Fewer Manual Processes by ERCOT Operators
Automated identification and resolution of infeasible AS
Automated release of AS capacity to provide energy during AS shortage conditions
Reduced RUC recommendations and SASM activity

## Slide 11: Consideration of Locational Reserve Requirements in RTC
ERCOT historically and currently has only system-wide AS requirements
  The current RTC white paper does not address the possible inclusion of AS with locational requirements and associated locational AS demand curves
  Based on recent discussions, it is anticipated that there will be further examination of the possible need for locational AS requirements and the manner in which those potential requirements would be incorporated into RTC

## Slide 12: Regulatory Changes Associated with the Implementation of RTC
The current RTC white paper identifies the need to coordinate the system-wide offer cap and the maximum value of the AS demand curves in RTC
Proper coordination of these values require resolution through possible changes to PUCT Subst. R. 25.505

## Slide 13: General Concerns Associated with the Implementation of RTC
The costs that will be incurred by ERCOT
The costs that will be incurred by market participants
The time and resources associated with implementation and potential competition with other projects
Some stakeholders have expressed concerns that introducing additional efficiency-enhancing measures such as RTC into the market may be detrimental to longer-term market policy objectives

## Slide 14: Links to Relevant Documents
May 8, 2017 SAWG – Need to co-ordinate values on VOLL SWOC PBPC training:
  http://www.ercot.com/content/wcm/key_documents_lists/118092/RT_Co-Opt_Coordination_of_VOLL_SWOC_PBPC.pptx
July 14, 2017 SAWG – Scarcity Pricing Examples under RTC - Spreadsheet
  RT Co Optimization Scenario Automated
September 18, 2017 SAWG – RTC White paper (Updated)
  http://www.ercot.com/content/wcm/key_documents_lists/131797/RT_Co-optimization_Scope_UPDATED_09292017.docx