## Slide 1: FERC Order 841: Storage in W/S Markets
February 15, 2018

## Slide 2: FERC Definition of Storage
A resource capable of receiving electric energy from the grid and storing it for later injection of electric energy back to the grid.
  Declined to state where the resource is located on the grid.
  Declined to give states the ability to opt-out.

## Slide 3: FERC Order 841
Finds current tariffs unjust and unreasonable in terms of barriers to storage participation, resulting in reduced competition and higher rates.
Tariffs do not provide bidding parameters for storage resources to offer services other than frequency regulation
Tariffs do not specify how storage resources could purchase electricity
ISO/RTOs are required to create a participation model for storage that includes addressing the unique characteristics of storage to both buy and inject electricity into the grid

## Slide 4: Storage Participation Model Must
Ensure that a resource can provide all capacity, energy and A/S into ISO/RTO markets
  Including services not purchased through organized markets (black start, primary frequency response, reactive power, etc.)
Resource can set w/s market prices as either a buyer or a seller at LMP
Account for physical/operational characteristics through bidding parameters
  Technology neutrality
Establish a minimum size requirement that does not exceed 100 kW

## Slide 5: Storage Participation Model
Storage Characteristics-Gives RTO/ISO Discretion as to Whether These Attributes are Required
  Maximum and Minimum State of Charge
  Maximum Charge Limit-maximum MW quantity resource can receive from the grid
  Maximum Discharge Limit-maximum MW quantity resource can provide to the grid
  Minimum Charge Time
  Maximum Charge Time
  Minimum Run Time
  Maximum Run Time
  Minimum Charge Limit
  Minimum Discharge Limit
  Charge Ramp Rate
  Discharge Ramp Rate

## Slide 6: Storage Participation Model
Type of telemetry consistent with service provided
  Necessary for responsive reserves
  May not be necessary for capacity and energy

## Slide 7: Next Steps
RTOs/ISOs have 270 days to file compliance tariffs
RTOs/ISOs have 365 days to implement tariffs

## Slide 8: DER Participation
Deferred making any determinations with respect to aggregated DER participation
Will continue to explore DER aggregation reforms
Announced a technical conference, with questions to supplement record in RM18-9-00

## Slide 9: Mona Tierney-Lloyd
Sr. Director, Western Regulatory Affairs