## Slide 1: Four-CP Response in ERCOT Competitive Area 2009 - 2014
Carl L Raish

## Slide 2: 4 CP Response Methodology
Analysis limited to ESIIDs in competitive ERCOT areas with ‘BUSIDRRQ’ profile types
  Transmission charges are based on ESIID-specific load during CP intervals
  ESIIDs classified by connection at transmission or distribution voltage level
  Distribution ESIIDs were classified based on weather sensitivity
Classified days as CP Days, Near-CP Days and Non-CP Days
  Near-CP days
    Base-lined transmission total load for all summer weekdays using the 20 days nearest in time (before and after) excluding CP days and holidays
      Applied Day-of-Adjustment factor to baseline
    Days with at least 100 MW reduction for Hour-ending 5:00 PM were classified as near CP days – found 69 Near-Peak days between 2009 - 2014
  Non-CP days were all remaining non-holiday weekdays (June 1 – Sep 30)
Classified ESIIDs based on Weather Sensitivity and Load Factor
  Weather sensitivity (R2 for week-day use vs average temperature >= 0.6)
  Load Factor based on week-day afternoon usage (1:00 PM – 6:00 PM)
  High LF > 0.85
  Medium LF > 0.60
  Low LF ≤ 0.60

## Slide 3: 4 CP Response Type Classification
All ESIIDs subject to 4-CP charges were base-lined
  Non-weather sensitive: 20 Non-CP days clostest in time (before and after)
  Weather sensitive using regression baseline
  Day-of-adjustment factor from midnight to 3:00 PM was applied to baseline
Used baselines to calculate hour-ending 5:00 pm CP and Near-CP reductions (MW and percent) for three years closest to the analysis year (40 – 48 days of possible reductions)
  Usually used the analysis year, the year before and the year after
  If the frequency and magnitude of MW17 reductions on CP and Near-CP days met thresholds the ESIID was classified as 4-CP responder
  If not, just the analysis year and year after were examined
    This was done to improve the classification of ESIIDs that started responding to 4-CP during the analysis year)
ESIIDs classified as responders were also examined for usage patterns indicating ‘day-use’ reduction for the 9:00 am – 4:00 pm time period on CP- and Near-CP days.
Based on the frequency and magnitude of ‘day-use’ reductions ESIIDs were classified as reducing or not reducing ‘day-use’ on CP- and Near-CP days.

## Slide 4: Quantifying 4-CP and Near-CP Reductions
ESIIDs already classified as responders were used in the calculation for a day if they reduced by more than the lesser of 10% or the ESIID’s average reduction determined during the classification for the hour-ending 5:00 PM
ESIIDs with a lower reduction or ESIIDs already classified as non-responders were not part of the reduction calculation.
If the ESIID was classified as a peak responder, a scalar day-of-adjustment was applied to the baseline for calculating the load reduction for the CP/Near-CP day.
No scalar adjustment was applied to ESIIDs previously classified as having ‘day-use’ response.
The methodology was modified from last year to narrow in on response from responding ESIIDs and to more effectively remove the impact of non-responding ESIIDs from reduction calculations.

## Slide 5: ERCOT Daily Peaks June – September 2014
Examined ERCOT Load daily peaks to determine possible Near-CP days

## Slide 6: Total Load - Transmission Connected ESIIDs - 2014
Examined Transmission ESIID Load to Identify Near-CP days

## Slide 7: Hour Ending 17:00 Response on 4 CP Days 2009 - 2014

## Slide 8: 4 CP 15-Minute Response 2009 - 2014

## Slide 9: 4 CP 15-Minute Response 2009 - 2014
Number of Near-CP days averaged about 10 per year
Since 2009, no CP intervals have occurred prior to interval ending 4:00 pm
Of the 24 CP intervals since 2009, only 5 appear to have been shifted by 4-CP response
  2 shifted one interval earlier
  2 shifted one interval later
  1 (7/16/2010) shifted one day earlier and one interval later

## Slide 10: 4 CP Response – ERCOT REP Survey
Key

## Slide 11: 4 CP Response – ERCOT REP Survey
Notifications: REP 1 – 27 REP 2 – 16 REP 3 – 4
REP 1 missed July CP, otherwise REP notifications were sent for all actual CP days

## Slide 12: 4 CP Response – ERCOT REP Survey
238 ESIIDs reported by REPS as being on 4-CP notification programs in 2013 or 2014
182 (76%) were classified by ERCOT as 4-CP responders.

## Slide 13: Number of ESIIDs with 4 CP Responses – 2014

## Slide 14: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Responding Transmission Connected ESIIDs

## Slide 15: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
Responding NWS Distribution Connected ESIIDs

## Slide 16: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Responding WS Distribution Connected ESIIDs

## Slide 17: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
All Responding 4-CP ESIIDS

## Slide 18: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
Reductions by Voltage Group

## Slide 19: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
Reductions as a Percent of Total Voltage Group Load

## Slide 20: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Percentage of Load Reduction by Load Factor and Voltage Group

## Slide 21: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Percentage of Load Reduction based on Customer Peak

## Slide 22: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Peak Response
Day-use Response

## Slide 23: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Peak Response
Day-use Response

## Slide 24: Hour-ending 17:00 Reductions on 4 CP Days - 2014

## Slide 25: Questions?
ON
OFF
craish@ercot.com 512/248-3876

## Slide 26
Appendix 1 – ESIIDs Responding

## Slide 27: Number of ESIIDs with 4 CP Responses – 2009

## Slide 28: Number of ESIIDs with 4 CP Responses – 2010

## Slide 29: Number of ESIIDs with 4 CP Responses – 2011

## Slide 30: Number of ESIIDs with 4 CP Responses – 2012

## Slide 31: Number of ESIIDs with 4 CP Responses – 2013

## Slide 32: Number of ESIIDs with 4 CP Responses – 2014

## Slide 33
Appendix 2 – Transmission MW Response

## Slide 34: Hour-ending 17:00 Reductions on 4 CP Days - 2009
Responding Transmission Connected ESIIDs

## Slide 35: Hour-ending 17:00 Reductions on 4 CP Days - 2010
Responding Transmission Connected ESIIDs

## Slide 36: Hour-ending 17:00 Reductions on 4 CP Days - 2011
Responding Transmission Connected ESIIDs

## Slide 37: Hour-ending 17:00 Reductions on 4 CP Days - 2012
Responding Transmission Connected ESIIDs

## Slide 38: Hour-ending 17:00 Reductions on 4 CP Days - 2013
Responding Transmission Connected ESIIDs

## Slide 39: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Responding Transmission Connected ESIIDs

## Slide 40
Appendix 3 – Distribution NWS MW Response

## Slide 41: Hour-ending 17:00 Reductions on 4 CP Days – 2009
Responding NWS Distribution Connected ESIIDs

## Slide 42: Hour-ending 17:00 Reductions on 4 CP Days – 2010
Responding NWS Distribution Connected ESIIDs

## Slide 43: Hour-ending 17:00 Reductions on 4 CP Days – 2011
Responding NWS Distribution Connected ESIIDs

## Slide 44: Hour-ending 17:00 Reductions on 4 CP Days – 2012
Responding NWS Distribution Connected ESIIDs

## Slide 45: Hour-ending 17:00 Reductions on 4 CP Days - 2013
Responding NWS Distribution Connected ESIIDs

## Slide 46: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
Responding NWS Distribution Connected ESIIDs

## Slide 47
Appendix 4 – Distribution WS MW Response

## Slide 48: Hour-ending 17:00 Reductions on 4 CP Days - 2009
Responding WS Distribution Connected ESIIDs

## Slide 49: Hour-ending 17:00 Reductions on 4 CP Days - 2010
Responding WS Distribution Connected ESIIDs

## Slide 50: Hour-ending 17:00 Reductions on 4 CP Days - 2011
Responding WS Distribution Connected ESIIDs

## Slide 51: Hour-ending 17:00 Reductions on 4 CP Days - 2012
Responding WS Distribution Connected ESIIDs

## Slide 52: Hour-ending 17:00 Reductions on 4 CP Days - 2013
Responding WS Distribution Connected ESIIDs

## Slide 53: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Responding WS Distribution Connected ESIIDs

## Slide 54
Appendix 5 – Total MW Response

## Slide 55: Hour-ending 17:00 Reductions on 4 CP Days - 2009
All Responding 4-CP ESIIDS

## Slide 56: Hour-ending 17:00 Reductions on 4 CP Days - 2010
All Responding 4-CP ESIIDS

## Slide 57: Hour-ending 17:00 Reductions on 4 CP Days - 2011
All Responding 4-CP ESIIDS

## Slide 58: Hour-ending 17:00 Reductions on 4 CP Days - 2012
All Responding 4-CP ESIIDS

## Slide 59: Hour-ending 17:00 Reductions on 4 CP Days - 2013
All Responding 4-CP ESIIDS

## Slide 60: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
All Responding 4-CP ESIIDS

## Slide 61
Appendix 6 – Reductions by Voltage Level

## Slide 62: Hour-ending 17:00 Reductions on 4 CP Days - 2009
Reductions by Voltage Group

## Slide 63: Hour-ending 17:00 Reductions on 4 CP Days - 2010
Reductions by Voltage Group

## Slide 64: Hour-ending 17:00 Reductions on 4 CP Days - 2011
Reductions by Voltage Group

## Slide 65: Hour-ending 17:00 Reductions on 4 CP Days - 2012
Reductions by Voltage Group

## Slide 66: Hour-ending 17:00 Reductions on 4 CP Days - 2013
Reductions by Voltage Group

## Slide 67: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
Reductions by Voltage Group

## Slide 68
Appendix 7 – Reductions as a Percent of Total Load

## Slide 69: Hour-ending 17:00 Reductions on 4 CP Days - 2009
Reductions as a Percent of Total Voltage Group Load

## Slide 70: Hour-ending 17:00 Reductions on 4 CP Days - 2009
Reductions as a Percent of Total Voltage Group Load

## Slide 71: Hour-ending 17:00 Reductions on 4 CP Days - 2010
Reductions as a Percent of Total Voltage Group Load

## Slide 72: Hour-ending 17:00 Reductions on 4 CP Days - 2011
Reductions as a Percent of Total Voltage Group Load

## Slide 73: Hour-ending 17:00 Reductions on 4 CP Days - 2012
Reductions as a Percent of Total Voltage Group Load

## Slide 74: Hour-ending 17:00 Reductions on 4 CP Days - 2013
Reductions as a Percent of Total Voltage Group Load

## Slide 75: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
Reductions as a Percent of Total Voltage Group Load

## Slide 76
Appendix 8 – Percent of Load by Group

## Slide 77: Hour-ending 17:00 Reductions on 4 CP Days - 2009
Percentage of Load Reduction by Load Factor and Voltage Group

## Slide 78: Hour-ending 17:00 Reductions on 4 CP Days - 2010
Percentage of Load Reduction by Load Factor and Voltage Group

## Slide 79: Hour-ending 17:00 Reductions on 4 CP Days - 2011
Percentage of Load Reduction by Load Factor and Voltage Group

## Slide 80: Hour-ending 17:00 Reductions on 4 CP Days - 2012
Percentage of Load Reduction by Load Factor and Voltage Group

## Slide 81: Hour-ending 17:00 Reductions on 4 CP Days - 2013
Percentage of Load Reduction by Load Factor and Voltage Group

## Slide 82: Hour-ending 17:00 Reductions on 4 CP Days - 2014
Percentage of Load Reduction by Load Factor and Voltage Group

## Slide 83
Appendix 9 – CP Day Graphs

## Slide 84: Hour-ending 17:00 Reductions on 4 CP Days - 2009

## Slide 85: Hour-ending 17:00 Reductions on 4 CP Days - 2010

## Slide 86: Hour-ending 17:00 Reductions on 4 CP Days - 2011

## Slide 87: Hour-ending 17:00 Reductions on 4 CP Days - 2012

## Slide 88: Hour-ending 17:00 Reductions on 4 CP Days - 2013

## Slide 89: Hour-ending 17:00 Reductions on 4 CP Days - 2014