## Slide 1: LRIS v2 / Self-scheduled Third party DR Provider Data Submission Proposal (Revised based on comments)
Carl L Raish

## Slide 2: NAESB Data Transport System
NAESB Data Transport System is currently in use for LRIS v1 and for REP submissions of ESIIDs in their Demand Response/Price Response programs
Files are exchanged via the Internet but are encrypted to protect data
An alternative to a TX Set solution … with some modifications, the LRIS v1 approach could accommodate DRPOR registration
Likely to be much less costly (for ERCOT and participants) and a shorter implementation period

## Slide 3: NAESB Data Transport System (continued)
Could be an interim solution and would not preclude eventual transition to an implementation in TX Set
Submitters would have to be licensed to use NAESB (or use a licensed service provider) and would have to be set up in ERCOT systems
NAESB file and business practice documentation would need to be modified … would require submission to and approval by NAESB
  We do have some experience with this for LRIS v1 and DRData

## Slide 4
http://www.ercot.com/mktrules/guides/data_transport

## Slide 5: NAESB System Users
DR Provider opting for LMP-$G settlement (would have to be set up in ERCOT as a QSE)
  DR provider would have to submit a Resource Asset Registration Form (RARF) to establish a ‘DR Resource’ in ERCOT systems
  DR Resource would be Load Zone specific
  DR Provider could then use the process to register as the DRPOR for ESIIDs participating in one of its ‘DR Resources’
REPs that want to register as the DRPOR for ESIIDs (but are not opting for LMP-$G settlement)
  REP must be the Rep-of-Record for the ESIID
  REP would register ESIIDs participating in one or more of the REP’s demand response/price response programs
  If REP wishes to get LMP-$G settlement, they would need to follow requirements in the first bullet above
Would not apply to resources/sites in NOIE areas
  LRIS v1 would remain as an option to a NOIE LSE
  Third-Party DR Providers can work with NOIEs to provide passive response or LRIS

## Slide 6: Site File
Field definitions and Validations
  DUNS Number -- must be in ERCOT System as a REP or a QSE
  Resource Code
    Non-blank if DR Provider is opting for LMP-$G settlement and must match RARF in ERCOT system
    Blank if submitted by a REP not opting for LMP-$G settlement
  ESIID
    If submitted by a REP not opting for LMP-$G settlement, must be the REP-of-Record on the submission date
    If submitted by a DR Provider opting for LMP-$G settlement
      May not be in more than one Resource
      May not be in ERS, TDSP Standard Offer Program, a Load Resource
      Must be consistent with other sites (Residential or Non-residential) in the Resource
      Must be currently active
      Must be in the Load Zone associated with the Resource
  Stop Date
    To indicate end of site’s participation on program (leave blank if active)
    If Resource Code is not blank, must be after the Resource Start Date (on the RARF)
    If from a REP not opting for LMP-$G settlement, must be after Rep-of-Record Date

## Slide 7: Site File Processing
Complete files of participants would be submitted each time (to avoid the need for sending update transactions to ERCOT)
Site files would be submitted prior to noon on the day before an operating day
If two or more entities send files prior to noon on the day before an operating day that contain the same ESIID, all with a blank stop date, the first entity submitting a file on that day would be designated as the DRPOR for that ESIID
  If no submission is received for an ESIID on the day before an operating day, the DRPOR for the ESIID is not changed from any prior submissions
  Notification of acceptance or rejection of DRPOR status would be sent to all submitting entities
  The noon submission requirement would give losing/gaining entities lead time to re-assess the amount of capacity available
Invalid rows would be ignored … no DRPOR relationship established

## Slide 8: Site File Processing (continued)
For a REP not opting for LMP-$G settlement, the REP’s DRPOR relationship would end automatically when the REP loses REP-of-Record status
Move-ins/move-outs would not affect the DRPOR relationship … if established it would continue to be in effect
If an ESIID becomes Inactive, the DRPOR relationship would end
Notifications would be sent to DR Providers opting for LMP-$G settlement to alert them concerning
  move-ins/move-outs, and
  ESIID de-energized or inactive

## Slide 9: Response Files
An Error File would be sent to submitter
  List of sites with validation issues
  Would include a final summary row of the number of rows submitted, rows okay, and rows with errors
  A file with only a summary row would be sent if no errors were detected
Site Loss file would be sent to losing DRP
Site Gain file would be sent to gaining DRP to alert entity that the site had previously belonged to another DRPOR
Notification files:
  File would be sent to REP-of -Record advising them that they have an ESIID that has begun participating (or has ended participation) with another entity
  In the event of a REP switch, a file would be sent to the gaining Rep-of-Record
  ESIID status notification (Move-in/Move-out, De-energized, Inactive) would be sent to the current DRPOR

## Slide 10: Disputes Over DRP Site Ownership
Losing entity would submit a MarkeTrak issue to claim the loss as invalid (similar to REPs claiming inadvertent gain/loss)
MarkeTrak notifies gaining entity that the gain is being challenged
Losing and gaining entities continue sending follow-up information through MarkeTrak to each other until a consensus is achieved
  The objective would be to establish the DRPOR relationship based on what the customer wants

## Slide 11: Disputes Over Site Ownership (continued)
Beyond providing the MarkeTrak System, ERCOT would take no role in resolving the dispute and would continue to honor the most recent submission for DRPOR
All site submissions would be treated as prospective
  ERCOT normally would not retroactively change historical DRPOR
  On a limited basis ERCOT would revise historical DRPOR status and re-evaluate settled deployments for Final- and True-up Settlements to address:
    Large changes in site participation
    Significant changes in the interval data available for event analysis
ERCOT would report disputes in summary form (and at a detail level if needed) to PUCT for use in identifying entities that are making excessive use of the process to challenge gains and/or losses