## Slide 1
Analysis of Load Reductions Associated with 4-CP Transmission Charges in ERCOT
Carl L Raish
Principal Load Profiling and Modeling
Demand Side Working Group – April 22, 2016

## Slide 2: Counts of ESIIDs on REP Sponsored Price/Demand Response Programs
Product Type | Description/Example | 2013 | 2014 | 2015
Time of Use | ‘Free Nights’, ’Free Weekends’ | 135,320 | 290,328 | 328,642
Peak Rebate | Rebates for DR during high price intervals | 2,468 | 413,772 | 499,085
Real Time Pricing | Price indexed to 15-minute LMPs | 4,358 | 9,700 | 5,621
Block & Index Pricing | Fixed price block with indexed price for use in excess of the block | 23,928 | 6,976 | 9,574
Other Load Control | Direct control of end-uses not necessarily tied to high price events | 3,488 | 19,304 | 14,927

## Slide 3: How 4CP Works
‘BUSIDRRQ’ customers ≥ 700 kW or served at transmission (69 kV) voltage are subject to 4CP charges.
  Simple average of the metered load during ERCOT system monthly peak 15-minute intervals in four summer months -- June, July, August & September.
  Multiplied by the applicable prevailing TDSP Tariff, as approved by PUC.
  Is the basis for the monthly 4CP-based rates for the following calendar year.
Analysis for this report was limited to ESIIDs in competitive ERCOT areas with ‘BUSIDRRQ’ profile types (ERCOT already has the data for retail settlement purposes).
  Municipals and COOPs can benefit by reducing 4CP loads, a few indicated they do actively reduce their load.
  Only aggregate data available for them, and, to date, load reductions for most NOIEs cannot be detected at that level
  An initial look at the limited number of NOIEs with significant reductions using the methodology presented indicates about 300 MW of 4CP related load reduction.

## Slide 4: Analysis Methodology
Identify 4CP and Near-CP days.
Identify High-Price days.
Classify customers by voltage level (Transmission/Distribution) and weather sensitivity.
Classify customers subject to 4CP charges:
  Develop baselines (WS and NWS) for each customer.
  Classify customers as those who reduce load at significant levels/frequencies and those who do not.
  Classify customers by type of reduction:
    Load reduction that targets the afternoon hours of 4CP/Near-CP days.
    Load reduction that starts early in the day and continues through the 4CP time period.
Calculate load reductions for specific 4CP/Near-CP days.
  Limited to customers identified in step 3 those who reduce load.
  Include customer’s load in over-all reduction calculation if they have a significant reduction on the specific day.
  Classify customer by load-factor category and calculate sub-totals.
Evaluate the interaction of high price events and 4CP response:
  Identify customers reported by their retailer as being on time-sensitive rates (real-time /block and index pricing).
  Quantify and compare their load reductions on 4CP and High-Price days.

## Slide 5: Identify 4CP and Near-CP Days
Response not apparent by examining ERCOT system Load
649 MW of 4 CP Response was ultimately found on 9/08/2015
About 1% of the ERCOT load
Drilling down to ‘BUSIDRRQ’ load on that day doesn’t provide much help
649 MW is about 4% of the total ‘BUSIDRRQ’ load

## Slide 6: Identify 4CP and Near-CP Days
About 300 transmission ESIIDs initially found to be reducing by 270 MW.
Reduction is about 7% of the class load.
The very high group daily load factor, results in a clear indicator of when a significant load reduction is occurring.
Transmission Customer Class Load

## Slide 7: Identify 4CP and Near-CP Days
Analyzed Transmission Class total load for all summer weekdays.
  Used the Non-weather sensitive baseline excluding CP and high-price days
  Calculated and applied the Day-of-adjustment.
Days with more than 100 MW of response for hour-ending 17:00 were classified as Near-CP days.
  Found 80 Near-CP days from 2008 – 2015.
CP and Near-CP days were analyzed for this report

## Slide 8: Transmission Load on Near CP Response Days
MW17 Reduce = 154
MW17 Reduce = 150
MW17 Reduce = 170
MW17 Reduce = 165
MW17 Reduce = 218
MW17 Reduce = 275

## Slide 9: Transmission Load on Near CP Response Days
MW17 Reduce = 137
MW17 Reduce = 102
MW17 Reduce = 102
MW17 Reduce = 131
MW17 Reduce = 183

## Slide 10: Historic 4CP/Near CP Intervals (2009-2015)
Most common 4CP / Near CP intervals are 4:45 and 5:00 PM
Tuesday and Wednesday are most likely to be 4CP days

## Slide 11: Identify High-Price Days
Pulled load zone prices for 2011 – 2015 (ERCOT was operating under Nodal Market Rules).
Took simple average of interval-by-interval prices across load zones.
Identified days with 4 or more consecutive intervals with prices greater than $200 / MWh.
Number of Days with Consecutive Prices Over $200/MWh
Average Price Distribution for Consecutive Prices Over $200/MWh
75 High-Price days identified

## Slide 12: Classify customers subject to 4CP charges
All ESIIDs subject to 4-CP charges were base-lined.
  Classify customers by weather sensitivity.
    Calculate R2 for distribution ESIIDs on daily-use for summer non-holiday weekdays versus average daily dry bulb temperature for the analysis year.
    If R2 ≥ 0.6 treat ESIID as weather sensitive.
  Non-weather sensitive baseline: 20 Non-CP days (before and after) occurring closest to the day being analyzed.
  Weather sensitive: using regression baseline (ERCOT load profile models) using 3 years of historical interval data.
  Scalar Day-of-adjustment factor from midnight to 3:00 PM was applied to baseline.
Non-CP days defined as weekday, non-holiday days.
  Excluded CP days and high-price days.
  Also excluded Near-CP days.

## Slide 13: Classify customers subject to 4CP charges
Classify customers that respond on 4CP/Near-CP days
  Used baselines to calculate hour-ending 5:00 pm 4CP and Near-CP reductions
    Calculate reduction percent and frequency for three years closest to the analysis year (42 days of possible reductions for 2015)
  Otherwise, looked at reductions for the analysis year plus year-after (except 2015)
    To improve the classification of ESIIDs that started responding to 4-CP starting with the analysis year
2015 Responder Classification
6,349 (56%) of 11,338 customers classified as responders for 2015

## Slide 14: Classify customers subject to 4CP charges
Responder ESIIDs from previous step were then classified into two response categories based on how they modified usage on CP and Near-CP days
  Reduced CP Hour Use -- ESIID that reduced usage during 4:00 PM – 5:00 PM on CP/Near-CP days but did not reduce significantly ahead of those times.
  Reduced Day Use -- ESIIDs that reduced CP Hour Use and also usually lowered usage from 9:00 AM – 4:00 PM) on those days.
    Day use reduction:
      The average day use reduction was > 10%, and
      The average number of intervals below the baseline was >= 20
    If 50%, or more, of days with CP Hour reduction also had day use reduction, customer was classified as reducing day use
2015 Responder Classification

## Slide 15: Calculate load reductions for specific 4CP/Near-CP days
Calculations limited to customers that met all of the following:
  Customers classified as responders by the previous step.
  Baseline indicated the customer did reduce load for the hour ending 5:00 pm for that day.
  Customer reduced load by at least 10%, or, if less than 10%, by more than its average 5:00 pm reduction determined by the previous classification step.
If the customer was classified as targeting its reduction for the afternoon hours, a scalar day-of-adjustment was applied to the baseline.
  Adjustment factor was calculated as the ratio of actual- to baseline-use from midnight to 3:00 pm on the CP/Near-CP day.
  Baseline intervals for the entire day were then multiplied by the adjustment factor.
If the customer was classified as starting to reduce earlier in the day, no scalar day-of-adjustment adjustment was applied to its baseline.

## Slide 16: Reductions by Response Type on 4 CP Days - 2015
Peak Response
Day-use Response
CP Reduce = 354
CP Reduce = 412
CP Reduce = 163
CP Reduce = 195

## Slide 17: Reductions by Response Type on 4 CP Days - 2015
Peak Response
Day-use Response
CP Reduce = 420
CP Reduce = 424
CP Reduce = 185
CP Reduce = 221

## Slide 18: Total Reductions on 4 CP Days - 2015
CP Reduce = 517
CP Reduce = 604
CP Reduce = 606
CP Reduce = 645

## Slide 19: Non-Responders on July 30, 2015
Total Load for customers initially classified as responders who did not appear to respond on July 30, 2015.
The method seems to work … no significant response that’s unaccounted for.
Distribution WS
Distribution NWS

## Slide 20: 4 CP / Near CP 15-Minute Response 2009 - 2015

## Slide 21: Hour Ending 17:00 Response on 4 CP Days 2009 - 2015

## Slide 22: 4 CP 15-Minute Response 2009 - 2015
Of the 28 4CP intervals since 2009, only 6 appear to have been shifted by 4CP response
  3 shifted peak one interval later (all from 16:45 to 17:00)
  2 shifted one interval earlier (both from 16:45 to 16:30)
  1 (7/16/2010) shifted one day later and one interval earlier

## Slide 23: Number of ESIIDs with 4 CP Responses – 2015
Across the 4 months ~2,000 (17%) of the ESIIDs subject to 4CP charges responded
Response rates: High LF 8%, Medium LF 11%, Low LF 32%
Low LF accounts for 57% of all responders

## Slide 24: Hour-ending 17:00 MW Reductions on 4 CP Days - 2015
All Responding 4-CP ESIIDS
Peak reduction exceeds day-use response and accounts for 67% of the total response
Except for September, most of the MW response came from Low LF ESIIDs

## Slide 25: Hour-ending 17:00 MW Reductions on 4 CP Days - 2015
Reductions by Voltage Group
Most of the MW response comes from Transmission and Distribution NWS ESIIDs

## Slide 26: Hour-ending 17:00 MW Reductions on 4 CP Days - 2015
Reductions as a Percent of Total Load Factor Group Load
Across all participants, ESIIDs reduce about 5% of their total load
Low LF ESIIDs reduce the highest percent of their total load (~17%)

## Slide 27: Hour-ending 17:00 Reductions on 4 CP Days - 2015
Percentage of Load Reduction by Load Factor and Voltage Group
Low LF and Transmission ESIIDs provide close to half of the total reduction

## Slide 28: Interaction of Price and 4-CP Response
REPs provided lists of ESIIDs participating in Real Time/Block & Index Pricing annual for 2013 – 2015.
  1,535 ESIIDs on RTP/BI pricing also are subject to 4CP charges.
  828 ESIIDs were identified as 4CP responders and were analyzed to evaluate the interaction between 4CP- and Price-response.
During 2013 – 2015, 25 days were classified as high-price days
  The sustained hourly prices on these high-price days ranged from $207 – 4,421.
  Two high-price days also were CP days (Sep 3, 2013 and Jul 30, 2015) and one high-price day was a Near-CP day (Aug 11, 2015).
Load reductions on high-price days were quantified using the same baseline methodology as used for the 4CP/Near CP analysis
  Day-of-adjustment periods were varied to include intervals prior to the onset of high prices for the day.
Regression was run to estimate the relationship of load reduction on high price days (excluding the 4CP and Near-CP days) to the sustained high price on those days.
  Independent variable was the log of price.
  Load reduction was set to zero if it was estimated as negative.

## Slide 29: Interaction of Price and 4-CP Response
Estimated Load Reduction on CP Days For RTP/BI ESIIDs
236.5 MW average CP/Near CP load reduction on high-price days
234.7 MW average CP load reduction on other than high-price days (excluding 7/21/2014)
No significant incremental CP load reduction related to high prices
RTP/BI ESIIDs do provide ~40% of the total 4CP load reduction

## Slide 30: Interaction of Price and 4-CP Response
Estimated Load Reduction on selected CP Days For RTP/BI ESIIDs
CP Reduce = 255
CP Reduce = 167
CP Reduce = 291
CP Reduce = 228

## Slide 31: Interaction of Price and 4-CP Response
Estimated Load Reduction on Near-CP Day For RTP/BI ESIIDs
CP Reduce = 231
CP Reduce = 252

## Slide 32: Interaction of Price and 4-CP Response
Estimated Load Reduction on selected High-Price Non-CP Days For RTP/BI ESIIDs
MW Reduce = 72
MW Reduce = 169
MW Reduce = 13
MW Reduce = 137

## Slide 33: Interaction of Price and 4-CP Response
Estimated Load Reduction for RTP/BI ESIIDs on Days with Sustained High Prices
Regression Estimates for Selected Price Points
Based on findings thus far, these price responsive MWs are also included in the 4CP response

## Slide 34: Questions?
ON
OFF
craish@ercot.com 512/248-3876