## Slide 1
Public Summary
Frontier Associates LLC
June 2014

## Slide 2: Background
PUC Subst. Rule §25.505(e)(5): Load serving entities (LSEs) shall provide ERCOT with complete information on load response capabilities that are self-arranged or pursuant to bilateral agreements between LSEs and their customers.
ERCOT sent an electronic survey to all LSEs in June-July of 2013 seeking customer counts on dynamic pricing/demand response contracts –‘Your response to the survey will allow ERCOT to gain a better understanding of the amount of responsive Load and numbers of retail energy consumers actively responding to Load reduction signals’

## Slide 3: Purpose of the project
It’s important to understand retail DR & price response
Impacts of retail demand response and price response on the long term load forecast
Advanced metering
  Enablement of DR is an important element in the return on the AMI investment
Ability to track growth of these products is a key metric in measuring the success of the ERCOT retail market

## Slide 4: Background
The survey revealed the numbers of current customers in the ERCOT region subject to retail price response/demand response products, including:
Time of Use pricing
Critical Peak pricing/rebates
Real-Time pricing
Direct Load Control
4CP response
  For REPs in the competitive market, the survey did not ask for the LSE’s estimates of the MWs of demand reduction or strike prices
  ERCOT then worked with Load Serving Entities to develop a plan for collecting and analyzing data

## Slide 5: Project path
Phase 1 – Initial Survey
  Results presented to market in Aug 2012 (RMS and DSWG)
Phase 2 – Data collection
  Collected ESIID information from REPs Summer 2013
  Additional survey used to collect events from REPS
  Phone calls with NOIEs
Phase 3 – Analysis
  After data collection, evaluation of price elasticity and how it affects:
    Load forecasting
    Wholesale market price formation
    Resource adequacy
Phase 4 – Report to market
We are here!

## Slide 6: Evaluation Project
ERCOT worked with Frontier for analysis and reporting
  Defined approach, data requirements for a subset of the categories
  Report on findings and results including presentations to stakeholders
  All data is anonymized and Frontier signed NDA
  Using the information collected from the survey and customer usage information in ERCOT’s possession, our analysis sought to quantify the amount of demand reduction that ERCOT could expect from these various programs and products during various events (e.g., a potential 4CP event or a spike in wholesale market prices).

## Slide 7: Summary Statistics

## Slide 8: Summary Statistics
21 REPs submitted validated ESIIDs to ERCOT
177,451 ESIIDs with validated submissions
  18,385 were excluded from analysis
    1,780 ESIIDs became inactive/de-energized after June 15 and still not active
    2,214 ESIIDs became inactive/de-energized after June 15 and went to different REP
    956 ESIIDs became inactive/de-energized after June 15 and returned to same REP
    13,322 ESIIDs stayed and went to different REP
  117,570 ESIIDs were reported on Time of Use pricing products
    TOU products are incentives for long-term behavioral shifts rather than event-based demand response. Analysis of these products and premises is beyond the scope of this initial analysis and is deferred to a future project.
  41,496 ESIIDs remained for analysis by Frontier

## Slide 9: Summary Statistics
Premises participating in multiple programs
Premises participating in a single program

## Slide 10: Approach to Quantifying Changes in Demand Associated with DR Actions
Identify “events” (e.g., price spikes, days with a high probability of setting a CP, curtailment requests).
Historical baseline method: Look at load patterns for a set of customers on previous days and compare (after making appropriate adjustments) with the load shape on the day of the event.
Regression analysis: Estimate the average impacts of various events on consumption of the customer(s), while statistically controlling for the effects of other factors which might affect energy consumption (including the weather).
IMPORTANT NOTE: All data was anonymized with REP and NOIE identities masked by ERCOT prior to providing to Frontier.

## Slide 11: Approach to Quantifying Changes in Demand Associated with DR Actions
Program | Data Source | Method of Analysis
OLC - Other Load Control | 15-minute interval consumption data (anonymized) from 05/01/2013 to 10/15/2013 for each ESI ID in this type of program. Event information, as reported by two REPs operating larger programs (including start and stop times). Start date for participation in the program, as reported by REP, for over 10,000 ESI IDs. | Baseline analysis focused on events as reported by REPs. Impacts were calculated on a customer-specific basis, for each program. An historical baseline was constructed, same as the ERCOT ERS “Middle 8-of-10” methodology, and actual usage was compared against baseline usage to estimate demand response
4CP | Aggregated IDR data for consumers served at transmission voltage for each regulated transmission and distribution utility (TDU) service area from 2001 to early 2014. Frontier’s evaluation was limited to use of aggregated (non-individual) data. The ERCOT staff then conducted supplemental baseline analysis (using a different baseline approach) of individual accounts that showed evidence of demand reduction during a 4CP. | A probabilistic analysis (logistic regression) was conducted to identify the days most likely to have elicited a 4CP response, based on weather, time of day, and other factors. Baseline analysis focused on actual and potential 4CP days (summer weekday afternoons). Baselines excluded weekend days, holidays, prior CPs, and near-CPs. Additionally, a regression model quantified the response of the aggregate usage of the transmission voltage customers in each TDU service area to 4CPs and “near 4CPs,” while controlling for other factors.

## Slide 12: Approach to Quantifying Changes in Demand Associated with DR Actions
Program | Data Source | Method of Analysis
RTP (Real Time Pricing) and BI (Block & Index) | Anonymized data for 4,100 RTP customers and 23,000 BI customers (10/15/2011-10/15/2013), along with location-related information for each account. Wholesale price data. Start date for program, as reported by REP, for each ESI ID enrolled in this type of program. Weather data. | Regression baseline focused on pricing events, defined as LZ SPPs at three distinct price levels: $300/MWh $1,000/MWh $3,000/MWh Additional models were estimated looking at single price spike levels (e.g., just $3,000MWh). An historical baseline was constructed, same as the ERCOT ERS “Middle 8-of-10” methodology, and actual usage was compared against baseline usage to estimate demand response.
PR (Peak Rebate) | 15-minute interval consumption data (anonymized) for each ESI ID in this type of program. | An historical baseline was constructed, same as the ERCOT ERS “Middle 8-of-10” methodology, and actual usage was compared against baseline usage to estimate demand response.

## Slide 13: 4CP Response: A Summary
See Appendix for additional 4CP information.
Estimated Average Demand Response During a 4CP in 2013 | 
 | Total MW
Demand Response from Energy Consumers Served at Transmission Voltage in Competitive Areas (regardless of their participation in formal programs) (1) | 250
Programs Implemented by NOIEs (2) | 200
Other Load Control Programs activated during a CP | Small
RTP and B&I Programs (incidental impacts during a CP) | Small
Rough Estimate of Other Response not otherwise accounted for (3) | 50
TOTAL | 500
Notes: | 
(1) An historical baseline calculation yields an estimate of 251 MW. Regression analysis suggests a reduction of 201 MW on average over the past 5 years. | 
(2) Based on a review of savings estimates reported by NOIEs. We have been unsuccessful in independently confirming these estimates. | 
(3) This is a conservative estimate based on judgment, to account for response by industrials with IDRs served at a voltage other than transmission and industrials within NOIE service areas. | 

## Slide 14: Customer Segment Providing the 4CP Response
Chart: 
| Transmission Voltage Consumers in Competitive Areas | Commercial and Industrial Consumers in NOIE Areas | Residential Consumers in NOIE Areas | Rough Estimate of Other Response not otherwise accounted for
 | 250 | 68 | 132 | 50

## Slide 15: Energy Consumption (in kWh) by Transmission Voltage Customers on CP of June 27, 2013, Contrasted against Baseline Energy
Chart: Interval of the Day (up to 96)
Chart: Interval of the Day (up to 96)
Zooming In. . .

## Slide 16: Energy Consumption (in kWh) by Transmission Voltage Customers on CP of July 31st, 2013, Contrasted against Baseline Energy
Chart: Interval of the Day (up to 96)
Chart: Interval of the Day (up to 96)
Zooming In. . .

## Slide 17: Energy Consumption (in kWh) by Transmission Voltage Customers on CP of August 7th, 2013, Contrasted against Baseline Energy
Chart: Interval of the Day (up to 96)
Chart: Interval of the Day (up to 96)
Zooming In. . .

## Slide 18: Energy Consumption (in kWh) by Transmission Voltage Customers on CP of September 3rd, 2013, Contrasted against Baseline Energy
Chart: Interval of the Day (up to 96)
Chart: Interval of the Day (up to 96)
Zooming In. . .

## Slide 19: Distribution of the 4CP Response in 2013 by TDU Service Area
Chart: Average Demand Reduction (MW) During a CP in 2013
| 1 = Centerpoint | 2=Oncor | 4=TNMP | 5=AEP Central | 7=AEP North
 | 80.6096 | 82.4383 | 4.3527 | 30.914 | -0.31548

## Slide 20: Load Control Programs
NOIE programs indicate a potential for demand reduction of well over 200 MW
Four REPs reported programs; two provided data
Demand response estimates from the REP programs are quite small in comparison to the NOIEs
  Numerous self-initiated events were reported
    Many were too short in duration to provide a meaningful database for analysis
    Many involved only a small subset of total enrolled premises
  Estimated event-specific demand response not reported publicly due to low number of participating REPs
Reported participation provides a benchmark for analyzing growth in this product type in future years

## Slide 21: Peak Rebate Programs
These programs had fewer than 2,000 participants in areas opened to retail competition in 2013
Participants are mainly residential energy consumers
It appears as though only one of the two REPs offering this type of program used it in 2013 – probably due to the low number of price spikes (see Appendix)
Estimated demand response not reported publicly due to low number of participating REPs

## Slide 22: Response to a Price Spike
Estimated Demand Response During a Spike in Wholesale Energy Prices in 2013 (1,2) | 
(For a Load Zone Settlement Point Price above $3,000/MWh) | 
 | Total MW
RTP and B&I Programs | 
Customers with IDR Meters | 180
Customers with AMS Meters | 2
Rough Estimate of Other Response not otherwise accounted for (3) | 50
Load Control Programs Implemented by NOIEs | 200
Peak Load Rebate Programs | 0.5
TOTAL | 432.5
Notes: | 
There were very few price spikes in ERCOT in 2013 (see Appendix). Consequently, many programs were not activated and the estimates here do not reflect potential demand reduction. Methodology: Regression analysis. | 
(3) This is a conservative estimate based on judgment, to account for price-responsive industrials within NOIE service areas. | 

## Slide 23: Response to Price Spikes by Consumers with IDR Meters in Competitive Areas
Chart: MW Reduction
| Price of $300/MWh | Price of $1000/MWh | Price of $1000/MWh
ERCOT | 90.2418 | 91.9812 | 180.443

## Slide 24: Response to Price Spikes by Consumers with IDR Meters in Competitive Areas– Baseline Approach
Intervals with North Zone price higher than $3000/MWh are selected as price spikes. The ERCOT ERS “Middle 8-of-10” methodology was adopted.
Note that Feb 2nd, 2011 price spike event was deleted due to overlapping ERCOT EEA and ERS deployment.
Events | Date | # of customers in the program | MW Saving
2 | 3/3/2011 | 292 | -3.0
3 | 6/27/2011 | 374 | 0.9
4 | 8/1/2011 | 380 | -10.3
5 | 8/2/2011 | 380 | -0.5
6 | 8/3/2011 | 380 | 10.3
7 | 8/4/2011 | 380 | 30.2
8 | 8/5/2011 | 380 | 7.5
9 | 8/23/2011 | 382 | -2.8
10 | 8/24/2011 | 383 | 28.7
11 | 4/5/2013 | 1192 | 181.9
12 | 9/3/2013 | 1531 | 90.1

## Slide 25: Observations
Yes, the demand side of ERCOT’s market responds to price signals (e.g., spikes in wholesale prices and 4CP-based transmission prices).
Gaps in the data and the small number of price spikes in 2013 may have prevented us from detecting the full potential of these programs and pricing products in reducing demand during “events.”

## Slide 26: Next Steps
2014 data collection project
  September 30, 2014 - snapshot by REPs for which ESI IDs are in programs
  November 1, 2014 - file submission to ERCOT*
  November 15, 2014 - error correction file submission to ERCOT
    * pushed file submission back by 2 weeks to allow any error handling to be completed prior to Thanksgiving Holiday
    REP should make all necessary corrections and re-send the full file to ERCOT. ERCOT will use the last file sent for data analysis.
  November 15, 2014 – ERCOT will send Survey Monkey links to REPs to gather REP-specific event information
TOU Analysis
  What are our expectations?
  What can we accomplish without asking REPs for more data?

## Slide 27
APPENDIX

## Slide 28: Pricing Events -- June
June 2013, North Load Zone

## Slide 29: Pricing Events – July
3000
July 2013, North Load Zone

## Slide 30: Pricing Events – August
Aug. 2013, North Load Zone

## Slide 31: Pricing Events – September
Sept. 2013, North Load Zone

## Slide 32: 4CP Background
The Four Coincident Peaks in ERCOT are the highest-Load 15-minute settlement intervals in each of the four summer months (June, July, August, September)
These intervals are the basis of various Transmission & Distribution (T&D) charges for much of the ERCOT Load
  Non-Opt In Entities (Muni’s and Co-ops), at the boundary meter level
  Retail Choice customers with peak demand ≥700 kW (Interval Data Recorder meter required)
Combined, over 44% of total ERCOT Load is subject to 4CP charges
Chart represents percentages of Load at IE 1700 on Aug. 3, 2011, ERCOT’s all-time system peak
“Large C&I” = IDR Required
Retail choice load

## Slide 33: How 4CP Works
  Simple average of the metered load during ERCOT system monthly peak 15-minute intervals in four summer months -- June, July, August & September
  Multiplied by the applicable prevailing TDSP Tariff, as approved by PUC
  Is the basis for the monthly 4CP-based rates for the following calendar year

## Slide 34: Historic 4CP Intervals (2003-2013)
Most common 4CP intervals are between 4:15 and 5:00 PM
Mondays and Fridays are the least likely 4CP days
August 13, 2007, is the outlier

## Slide 35: Summer peak interval trends
4CP @ IE 17:00

## Slide 36: Summer peak interval trends
4CP @ IE 17:00

## Slide 37: Summer peak interval trends
4CP @ IE 16:45

## Slide 38: Summer peak interval trends
4CP @ IE 16:45

## Slide 39
The 4CP price signal
CREZ project activation = new 4CP incentives
>$5.2B in new facilities energized in 2013 – 5 times the average
  These dollars will be recovered via 4CP TCOS rates over 30 years
Source: ERCOT Transmission Projects Information Tracking (TPIT) Report, Nov. 2013
Date | ‘Postage Stamp’ TCOS Rate (per 4CP kW)
4/16/2010 | $26.05
4/8/2011 | $28.10
4/12/2012 | $29.36
3/23/2013 | $30.95
11/30/2013 | $40.86
3/19/2014 | $41.08
}
58% increase in 4 years