## Slide 1
Analysis of NOIE Load Reductions Associated with 4-CP Transmission Charges/Price Response in ERCOT
Carl L Raish
Principal Load Profiling and Modeling
Demand Side Working Group – June 17, 2016

## Slide 2: How 4CP Works
All NOIEs in ERCOT are served at transmission (69 kV) voltage and are subject to 4CP charges.
  Simple average of the metered load during ERCOT system monthly peak 15-minute intervals in four summer months -- June, July, August & September.
  Is the basis for the monthly 4CP-based rates for the following calendar year.
Analysis for this report was based on interval data from NOIE boundary metering (ERCOT already has the data for retail settlement purposes).
  Municipals and COOPs can benefit by reducing 4CP loads, in previous annual surveys a few indicated they do actively reduce their load.
  Only aggregate data available for them, and, to date, load reductions for most NOIEs cannot be detected at that level
  Our previous look based on ERCOT’s Mid-8-of-10 baseline found about 300 MW of 4CP related load reduction.
  This analysis shifted to using the Regression baseline which has demonstrated improved accuracy in identifying NOIEs that respond and the amount of response.

## Slide 3: Analysis Methodology
Used same 4CP, Near-CP and High-price days as identified for the analysis of competitive ESIIDs.
To enable use of the Regression baseline NOIEs were assigned to their predominant single weather zone.
Analysis was limited to the largest NOIEs that account for 90% of summer weekday kWh (33 – 34 NOIEs depending on year).
Regression model was estimated for an analysis year using three closest years of data for each NOIE and interval estimates produced for each day.
Baseline-to-actual percent difference was calculated for non-CP days for each NOIE and the 75th percentile level difference was determined.
For each NOIE, counted CP- and Near-CP days as days as reducing days if the MW17 percent reduction on the CP- / Near-CP day exceeded 75th percentile difference.
NOIE was deemed a 4CP responder for the analysis year if reductions were counted for:
  More than half its CP days, or
  Half its CP days and more than half its Near-CP days, or
  More than 40% of its CP days and more than 60% of its Near-CP days, and
  Its average 4CP reduction for the analysis year exceeded the 75th percentile difference.
4CP responder NOIEs were also examined for price response during the analysis year.

## Slide 4: Total NOIE Reductions on 4 CP Days - 2015
CP Reduce = 221
CP Reduce = 911
CP Reduce = 783
CP Reduce = 357

## Slide 5: NOIE Specific 4-CP Responses – Aug 10, 2015
Reduce 6.6%
Reduce 13.9%
Reduce 12.2%
Reduce 8.2%

## Slide 6: NOIE Specific 4-CP Responses – Aug 10, 2015
Reduce 4.9%
Reduce 17.5%
Reduce 11.8%
Reduce 23.1%

## Slide 7: NOIE Specific 4-CP Responses – Aug 10, 2015
Reduce 12.0%
Reduce 7.2%
Reduce 10.6%
Reduce 4.5%

## Slide 8: NOIE Specific 4-CP Responses – Aug 10, 2015
Reduce 0.7%
Reduce 9.5%
Reduce 6.9%
Reduce 6.6%

## Slide 9: NOIE Specific 4-CP Responses – Aug 10, 2015
Reduce 1.2%
Reduce 0.5%
Composite of 18 Responding NOIEs
Reduce 911 MW
Percent 6.4%

## Slide 10: Competitive + NOIE Reductions on 4 CP Days - 2015
Reduce MW 704
Percent 5.1%
Reduce MW 1,496
Percent 8.9%
Reduce MW 1,371
Percent 8.5%
Reduce MW 1,002
Percent 6.5%

## Slide 11: 4 CP / Near CP 15-Minute Response 2009 - 2015

## Slide 12: Hour Ending 17:00 Response on 4 CP Days 2009 - 2015

## Slide 13: Interaction of Price and 4-CP Response
During 2013 – 2015, 25 days were classified as high-price days
  The sustained hourly prices on these high-price days ranged from $207 – 4,421.
  Two high-price days also were CP days (Sep 3, 2013 and Jul 30, 2015) and one high-price day was a Near-CP day (Aug 11, 2015).
Load reductions on high-price days were quantified using the same baseline methodology as used for the 4CP/Near CP analysis
  Day-of-adjustment periods were varied to include intervals prior to the onset of high prices for the day.
Regression was run to estimate the relationship of load reduction on high price days (excluding the 4CP and Near-CP days) to the sustained high price on those days.
  Independent variable was the log of price.

## Slide 14: Interaction of Price and 4-CP Response
4CP Responder NOIEs Estimated Load Reduction on CP Days
601.0 MW average CP/Near CP load reduction on high-price days
529.3 MW average CP load reduction on other than high-price days (excluding 6/30/2014, 7/21/2014)
Small incremental CP load reduction related to high prices

## Slide 15: Interaction of Price and 4-CP Response
4CP Responder NOIEs Estimated Load Reduction on CP Days
CP Reduce = 541
Price $92
CP Reduce = 253
Price $2,333
CP Reduce = 778
Price $337
CP Reduce = 356
Price $39

## Slide 16: Interaction of Price and 4-CP Response
4CP Responder NOIEs Estimated Load Reduction on Near-CP Days
CP Reduce = 600
Price $142
CP Reduce = 771
Price $563

## Slide 17: Interaction of Price and 4-CP Response
4CP Responder NOIEs Estimated Load Reduction on selected High-Price Non-CP Days
MW Reduce = 0
Price $1,203
MW Reduce = 428
Price $4,422
MW Reduce =0
Price $729
MW Reduce = 215
Price $609

## Slide 18: Interaction of Price and 4-CP Response
Estimated Load Reduction for 4CP Responder NOIEs on Non-CP Days with Sustained High Prices
Regression Estimates for Selected Price Points (negative estimates set to zero)
Based on findings thus far, these price responsive MWs are also included in the 4CP response

## Slide 19: NOIE 4-CP Response - 2009
2 Responder NOIEs
MW Reduce = 91
MW Reduce = 40
MW Reduce = 59
MW Reduce = 41

## Slide 20: NOIE 4-CP Response - 2010
7 Responder NOIEs
MW Reduce = 16
MW Reduce = 0
MW Reduce = 396
MW Reduce = 52

## Slide 21: NOIE 4-CP Response - 2011
13 Responder NOIEs
MW Reduce = 717
MW Reduce = 375
MW Reduce = 529
MW Reduce = 868

## Slide 22: NOIE 4-CP Response - 2012
17 Responder NOIEs
MW Reduce = 1,008
MW Reduce = 264
MW Reduce = 286
MW Reduce = 396

## Slide 23: NOIE 4-CP Response - 2013
16 Responder NOIEs
MW Reduce = 671
MW Reduce = 316
MW Reduce = 524
MW Reduce = 232

## Slide 24: NOIE 4-CP Response - 2014
18 Responder NOIEs
MW Reduce = 12
MW Reduce = 39
MW Reduce = 729
MW Reduce = 449

## Slide 25: NOIE 4-CP Response - 2015
18 Responder NOIEs
MW Reduce = 221
MW Reduce = 783
MW Reduce = 911
MW Reduce = 357

## Slide 26: Questions?
ON
OFF
craish@ercot.com 512/248-3876