## Slide 1
Monthly COP Error Analysis
Alex Lee
Lead Operations Planning Engineer
Alex.Lee@ercot.com
ROS Meeting
ERCOT Public
March 1, 2018

## Slide 2: Overview
COP Error Definition
COP Error Scope
COP Error Analysis
Monthly Trends
Observation and Impact

## Slide 3: COP Error Definition
COP Error = COP Capacity – SCED Capacity
  Negative Error means Under-Scheduling in COP
  Positive Error means Over-Scheduling in COP
Example 1: Generator A
  COP: ON with HSL equals to 200 MW
  SCED: ON with HSL equals to 150 MW
  COP Error = 200 – 150 = 50 MW (Over-Scheduling)
Example 2: Generator B
  COP: OFF with HSL equals to 100 MW
  SCED: ON with HSL equals to 100 MW
  COP Error = 0 – 100 = -100 MW (Under-Scheduling)

## Slide 4: COP Error Scope
Only generator resources (excludes load resources).
Excludes Renewables and Batteries.
Excludes startup and shutdown Hours.

## Slide 5: COP Error Analysis
COP Error for Operating Day Hour Ending :
Monthly COP Error for Hour Ending consists of:
where n is the number of days in given month

## Slide 6: COP Error Analysis (continued)
Box Chart of n samples:
Monthly Mean Absolute Error (MAE):
Maximum
Minimum
Median
75th Percentile
25th Percentile

## Slide 7
Monthly Mean Absolute Error (MAE) = 384 MW
Monthly COP Error by Delivery Hour: Latest
Latest means after the Adjustment Period

## Slide 8
Monthly Mean Absolute Error (MAE) = 9,222 MW
Monthly COP Error by Delivery Hour: Day-Ahead at 12:00

## Slide 9
DA = Day-Ahead OD = Operating-Day
Over-Scheduling Error
Under-Scheduling Error
COP Error = COP Capacity – SCED Capacity
Monthly COP Error by Snapshot Timepoint
Day-Ahead between noon and 2pm
is when COPs are significantly updated.

## Slide 10: Observation and Impact
COP Error is large (~9,000 MW) up to Day-Ahead at noon.
Any reliability assessment before Day-Ahead at 2pm contains significant error.