## Slide 1
Resource Definition Task Force Progress Update
March 2018

## Slide 2: Background
Previous attempts at addressing non-modeled generation or distributed generation have struggled to resolve the various issues.
This task force is intended to resolve issues with the protocols regarding resources and definitions in ERCOT.
  Attempting to resolve with a single over-arching NPRR to address everything is expected to stretch out the timeline significantly to get overall agreement.
The recommended approach is to selectively identify and resolve issues
  It is anticipated that several NPRRs will be developed to address existing issues.
  Topics or definitions the group is unable to resolve but require further review will be included in a whitepaper that is shared with PRS.

## Slide 3: Stages of Activities
Stage 1 - Align definitions to identify differences
  Initial Framework by Jay identifies resource types. (see slide 6)
  Initial table comparing NERC/PURA/PUCT/ERCOT generated
  Develop consensus on new Terms and/or definitions
  Align with Jay’s Resource analysis
    Revise and streamline to capture key issues and gaps
  Publish new Terms/Definitions
    Terms or definitions without agreement will be included in the whitepaper.
  Should suggested changes be sent to PRS for approval?
Estimated duration 6-8 months

## Slide 4: Stages of Activities (cont)
Stage 2 – Clarify Definitions for Transmission connected resources
  Revise/replace “Non-modeled” term per new definitions
  Recommend/Submit first NPRR.
Estimated Duration 6 months

## Slide 5: Stages of Activities (cont)
Stage 3 – Clarify definitions for Distribution connected resources
  Generate new categories addressing multiple configurations
  Utilize definitions established in step 1 where possible.
  Include current and proposed future DG categories together, or address in separate NPRRs?
  Submit NPRR(s).
Estimated duration 6-8 months

## Slide 6: Initial Framework (see RTF Aug 11, 2017)

## Slide 7: Current definition (Protocol Section 2.1)

## Slide 8: Existing Resource Definition Framework

## Slide 9: Framework (continued)
  All-Inclusive Generation Resources (comprised of Generation Resources and Non-Modeled Resources) must meet existing designated technical and data provision requirements (“Technical Requirements”) as well as the Market Requirements.
  Generation Resources must also meet additional qualification requirements depending on the “Services” they are providing:
    Example – Additional requirements to be qualified for providing Black Start Services

## Slide 10: Example Technical Requirements
Draft
* Term used as part of the original NPRR190-for example only
*
*

## Slide 11
  COPs
  Offer curves
  Following Base Points
  Dispatch Instructions outside of Emergency conditions
  Etc.
This is not a comprehensive list of the Market Requirements for Generation Resources.
The rules should not change any requirements for Generation Resources, so sections of the Protocols related to requirements exclusively for Generation Resources should not change for this effort.
Example Market Requirements

## Slide 12
Generation Resource Breakdown

## Slide 13: Revise terminology for resources in the ERCOT systems
Old Nomenclature
Generation Resource
Non-modeled Generator
Unregistered generator
(Distribution connected Generation > 10MW)
Revised nomenclature
Generation Resource (no change)
New term(s)
  Transmission connected
  Distribution connected
Microgenerator (see PUCT defs)
Generation Resource

## Slide 14: Some Examples
  The following pages illustrate a few simplistic examples of Generators.
  In each example, Generators that are owned by different companies are shown in different colors.
  Transmission voltage elements are shown in green and blue; distribution voltage elements and/or PUN-owned transmission are shown in gray.

## Slide 15: Examples
100 MW
Traditional Generation Resource
with POI to transmission
9.9 MW
< 10 MW Generator with POI to transmission
Examples of Transmission Connected Resources

## Slide 16
4 MW
5 MW
1 MW
PUN with no single generator or aggregation >10MW
9.9 MW
9.9 MW
20 MW
PUN with Aggregation of gens >10MW
100MW
100 MW
150 MW
PUN with gens >10MW
Examples of PUN Resources

## Slide 17
9.9MW
Generator < 10MW on Distribution System
not in SCED or AS Market
9.9 MW
9.9 MW
Multiple gens < 10MW on Distribution System
with different Service Delivery Points
1
MW
8
MW
Aggregation of gens at common
Service Delivery Point < 10MW
Note: Unregistered Generator < 1 MW on Distribution System not shown
1MW
1-20 MW
1-20 MW
9.9MW
Generator < 10MW on Distribution System
not in SCED or AS Market
20MW
Examples of Distribution Connected Resources

## Slide 18: Examples of Distribution Connected Resources
>10 MW
Generator > 10 MW
on Distribution System
1-20 MW

## Slide 19: Proposed Category Nomenclature
Transmission Generation Resource (TGR) Transmission-connected Registered with ERCOT as GR Participates in the market SCED A/S Modeled in ERCOT systems Telemetry, etc. Settled Nodally |  |  | Settlement Only Transmission Generator (SOTG) Transmission-connected less than 10 MW Registered with ERCOT as SOG Settled for exported energy only Intermittent sources will typically export based on fuel availability. Self-dispatched may choose to export based on prices Modeled in ERCOT systems Reliability systems only Not scheduled/dispatchable Settled - Load Zone |  | Transmission Self-Generator (TSG) Transmission-connected Registered with PUC as a Self-Generator and registered with ERCOT as SOG May occasionally export, but does not generate with the intent to sell at wholesale If it exports, then settled for exported energy only Continuous exports will be re-evaluated for TGR Modeled in ERCOT systems Reliability systems only Not scheduled/dispatchable Settled - Load Zone |  |  |  | 
Distribution Generation Resource (DGR) Distribution connected Registered with ERCOT as GR >10 MW require to register as GR Participates in the market SCED A/S Pseudo-Modeled in ERCOT systems Future--Modeling light? Telemetry, etc. Settled nodally |  |  | Settlement Only Distribution Generator (SODG) Distribution connected but less than 10 MW Registered with ERCOT as SOG Settled for exported energy only Intermittent sources will typically export based on fuel availability. Self-dispatched may choose to export based on prices Mapped in ERCOT systems Not scheduled/dispatchable Telemetry light? (ex--NPRR829) Settled - Load Zone |  | Unregistered Distribution Self-Generator (UDSG) Distributed generation greater than 1 MW co-located with larger load, but smaller than minimum facility load. Registered with PUC as a Self-Generator but not registered with ERCOT May not export—otherwise must register with ERCOT as SODG. Neither Mapped nor modeled in ERCOT systems (future mapping?) No settlement policy since no exports. |  |  | Unregistered Distributed Microgenerator (UDMG) Distribution connected less than 1 MW No requirement for registration Reported by DSP per PUCT 25.211(n) (competitive choice) Reported by NOIEs per ERCOT protocol 10.2.2.1.b(ii) for 50kW -1 MW Not reported by NOIEs for <50kW Neither Mapped nor modeled in ERCOT systems (future mapping of accumulations?) No ERCOT settlement policy— NOIEs, REPs may provide compensation for exports | 
 | **Settlement Only means that the generator may not participate in Ancillary Services Market, RUC, SCED, or make Energy Offers. |  |  |  |  |  |  |  | 

## Slide 20: Proposed Resource Definition Framework
**Settlement Only generator means that they may not participate in Ancillary Services Market, RUC, SCED, or make Energy Offers.

## Slide 21: Example Registration Flowchart page 1

## Slide 22: Points brought up during discussions for consideration in future NPRRs (Stage 2+)
Clarify Implicit Definitions in Protocols for Distribution connected resources 10 MW and greater
All transmission connected resources would be required to be registered and modeled, regardless of size.
A Transmission connected self-generator may be registered as an Non-modeled even though it might occasionally produce more than 10 MW net output for payment during an ERCOT-declared Emergency.
  ERCOT would review output and determine if a generator is exceeding the threshold and should subject to registering as a Generation Resource.
Any resource that wants to participate in Ancillary service market or SCED is required to register as a Generation Resource.
Existing resources that are not currently registered, but might be required to register under any proposed requirements and choose to register as Non-modeled generators, may be grandfathered if they cannot meet specific “Technical Requirements” (reactive, governor).

## Slide 23: Topics for Additional Discussion
  How to handle Aggregations of distribution connected generators that want to register as Generation Resources ?
  Energy Storage registration/modeling issues.
    This will not be a significant area of focus as part of this task force and will instead be included in the whitepaper for further discussion.
  To what extent do we construct definitions-- and do definitions correlate to obligations? This may be a whitepaper issue.