## Slide 1
Revised Analysis of PUN LDFs
Jian Wu
3/19/2018

## Slide 2: Outline
Background
Analysis Methodology
Performance Result
Conclusion

## Slide 3: Background
May 2017, NPRR 831 is proposed with new methodology of PUN LDF
Jun. 2017 PUN net load is stored in historical database
Sep.2017 analysis of new methodology was presented in WMS meeting. Follow up analysis was requested
Oct.2017 new methodology is approved by TAC
Nov.1.2017 NPRR 831 is implemented
Nov.2017, first PUN LDF is published

## Slide 4: Methodology
To evaluate the LDF performance, 5 minute load data from implementation date 11/3/2017 till 2/9/2018 was pulled.
The absolute difference between LDF and actual load was then calculated by every 5 minutes for all three LDF sets.
Snapshot Date
Load data from this period compared to posted LDFs
Next Snapshot Date

## Slide 5: Methodology
5min PUN net load data was used to calculate PUN LDFs.
Four “snapshot” dates were used according to LDF post:
  11/2/2017
  12/13/2017
  1/15/2018
  1/18/2018
These dates represent the start points of usage for the LDFs .
Studying period: 11/3/2017-2/9/2018 .

## Slide 6: Methodology
For each snapshot date, three separate LDFs sets were calculated using three different lengths of historical data.
In the 28-day method, hourly load data from the previous 28 days from the snapshot was averaged by hour to calculate the LDFs.
Snapshot Date
Previous 28 days
Averages by hour used to compute LDFs

## Slide 7: Methodology
In the 7-day method, hourly load data from the previous 7 days from the snapshot was averaged by hour to calculate the LDFs.
Snapshot Date
Previous 7 days
Averages by hour used to compute LDFs

## Slide 8: Methodology
In the 7-day method, hourly load data from the previous 7 days from the snapshot was averaged by hour to calculate the LDFs.
In the 1-day method, hourly load data from the previous operating day was used to calculate the LDFs.
Snapshot Date
Previous 1 day
Hourly loads used to compute LDFs

## Slide 9: Methodology
The initial analysis began by identifying PUNs that were net consumers on average for the previous 60 days. 12 PUNs were identified.
For each identified PUNs, LDFs were calculated using the 28-day, 7-day and 1-day methodology for all four snapshot dates.
The three sets of LDFs were then compared.

## Slide 10: Methodology
10 of the twelve PUNs showed little (<15 MW) difference on average between the two sets LDFs for each of the four snapshot dates.
This suggests that, for most PUNs in ERCOT, the LDFs calculated will be consistent regardless of which method is used.
Chart: Average Absolute Difference Between 28-Day and 7-Day LDF Methodology
| HE1 | HE2 | HE3 | HE4 | HE5 | HE6 | HE7 | HE8 | HE9 | HE10 | HE11 | HE12 | HE13 | HE14 | HE15 | HE16 | HE17 | HE18 | HE19 | HE20 | HE21 | HE22 | HE23 | HE24
PUN A | 2.709 | 2.7384 | 3.852 | 3.209 | 3.1582 | 3.3086 | 3.1542 | 3.2068 | 3.374 | 3.1768 | 3.2711 | 4.2758 | 4.7188 | 4.6382 | 4.5661 | 3.5957 | 3.3771 | 3.6287 | 3.5563 | 3.5184 | 3.4888 | 3.775 | 3.9057 | 4.0108
PUN B | 38.4591 | 39.1968 | 37.7488 | 38.4884 | 40.7554 | 42.7887 | 42.7363 | 45.9522 | 46.1803 | 42.1304 | 40.8974 | 43.4508 | 45.1953 | 40.538 | 36.8672 | 35.159 | 38.213 | 36.7257 | 37.3814 | 35.4223 | 32.287 | 30.8502 | 34.1309 | 32.3376
PUN C | 7.3585 | 7.799 | 8.3135 | 7.5257 | 6.3843 | 8.6706 | 12.9907 | 15.7594 | 17.0408 | 18.3821 | 16.0951 | 13.3889 | 11.7696 | 12.9323 | 16.9434 | 15.9679 | 15.4984 | 17.9187 | 13.6019 | 16.5361 | 15.7086 | 13.0285 | 9.8026 | 6.4564
PUN D | 9.4835 | 9.5116 | 9.3541 | 9.3355 | 9.5588 | 9.3471 | 9.327 | 9.3646 | 9.8171 | 10.2213 | 10.6568 | 10.6179 | 10.8802 | 10.8735 | 11.3326 | 11.358 | 11.4931 | 11.4877 | 11.3409 | 10.9318 | 10.5254 | 10.5814 | 10.7961 | 10.8045
PUN E | 0.95777 | 0.94795 | 0.94185 | 0.94341 | 0.94146 | 0.93336 | 0.93067 | 0.94147 | 0.95907 | 0.95654 | 0.9411 | 0.93499 | 0.94142 | 0.94331 | 0.94325 | 0.94014 | 0.94299 | 0.93354 | 0.92898 | 0.93289 | 0.93544 | 0.93937 | 0.94151 | 0.94223
PUN F | 0.11423 | 0.1416 | 0.13025 | 0.044223 | 0.10439 | 0.50747 | 1.1237 | 1.4768 | 1.5789 | 1.3535 | 1.3253 | 1.3822 | 1.3576 | 1.1878 | 1.2144 | 1.1915 | 1.0097 | 0.66973 | 0.028864 | 0.17359 | 0.17707 | 0.20581 | 0.31983 | 0.34498
PUN G | 0.058929 | 1.157 | 0.095824 | 0.24284 | 0.16346 | 0.33711 | 1.1882 | 1.7745 | 0.48294 | 0.94757 | 0.4012 | 1.205 | 2.8984 | 2.7342 | 1.3114 | 0.0437 | 2.567 | 0.36342 | 0.72036 | 1.4243 | 0.3046 | 0.93776 | 1.8153 | 1.9272
PUN H | 12.2399 | 12.0232 | 12.1485 | 12.0569 | 11.8178 | 10.7235 | 10.6588 | 11.1804 | 11.7221 | 11.4548 | 11.2229 | 10.4844 | 10.2315 | 10.2716 | 10.0823 | 9.5407 | 9.1021 | 9.2951 | 10.4476 | 11.322 | 11.7487 | 11.9083 | 11.6322 | 12.1091
PUN I | 2.3561 | 2.2035 | 2.0321 | 2.0384 | 2.2395 | 2.6174 | 3.2073 | 3.7797 | 4.6429 | 6.4946 | 6.559 | 5.2723 | 5.3274 | 5.5236 | 4.1215 | 4.6974 | 4.1429 | 2.9093 | 2.3198 | 1.9646 | 1.0879 | 0.14495 | 0.21128 | 1.0326
PUN J | 3.7347 | 3.9829 | 4.1715 | 4.1273 | 4.1031 | 4.2485 | 4.5976 | 8.4467 | 10.2631 | 11.9003 | 11.1352 | 12.2002 | 9.8323 | 7.9631 | 8.4513 | 9.9553 | 10.2208 | 11.673 | 12.1774 | 11.2315 | 10.1678 | 9.4423 | 6.0628 | 3.8183
PUN K | 0.7165 | 0.78849 | 0.81545 | 0.77569 | 0.8329 | 0.80694 | 0.84566 | 0.79287 | 0.78887 | 0.74823 | 0.66804 | 0.77703 | 0.70921 | 0.73455 | 0.77007 | 0.82774 | 0.862 | 0.8306 | 0.83405 | 0.87591 | 0.81219 | 0.77441 | 0.80742 | 0.74673
PUN L | 7.5495 | 7.5296 | 7.6249 | 7.698 | 7.7497 | 7.4137 | 6.8116 | 6.9607 | 6.945 | 7.121 | 6.7335 | 6.5717 | 6.2979 | 6.0261 | 6.0809 | 5.685 | 6.222 | 6.5136 | 7.0151 | 7.1245 | 7.4968 | 7.4748 | 7.6837 | 7.8561

## Slide 11: Methodology
Two of the PUNs showed significant difference between the 28-day LDFs and the 7-day LDFs.
PUN B is much more dynamic than PUN C
These two PUNs were analyzed further.
Chart: Average Absolute Difference Between 28-Day and 7-Day LDF Methodology
| HE1 | HE2 | HE3 | HE4 | HE5 | HE6 | HE7 | HE8 | HE9 | HE10 | HE11 | HE12 | HE13 | HE14 | HE15 | HE16 | HE17 | HE18 | HE19 | HE20 | HE21 | HE22 | HE23 | HE24
PUN A | 2.709 | 2.7384 | 3.852 | 3.209 | 3.1582 | 3.3086 | 3.1542 | 3.2068 | 3.374 | 3.1768 | 3.2711 | 4.2758 | 4.7188 | 4.6382 | 4.5661 | 3.5957 | 3.3771 | 3.6287 | 3.5563 | 3.5184 | 3.4888 | 3.775 | 3.9057 | 4.0108
PUN B | 38.4591 | 39.1968 | 37.7488 | 38.4884 | 40.7554 | 42.7887 | 42.7363 | 45.9522 | 46.1803 | 42.1304 | 40.8974 | 43.4508 | 45.1953 | 40.538 | 36.8672 | 35.159 | 38.213 | 36.7257 | 37.3814 | 35.4223 | 32.287 | 30.8502 | 34.1309 | 32.3376
PUN C | 7.3585 | 7.799 | 8.3135 | 7.5257 | 6.3843 | 8.6706 | 12.9907 | 15.7594 | 17.0408 | 18.3821 | 16.0951 | 13.3889 | 11.7696 | 12.9323 | 16.9434 | 15.9679 | 15.4984 | 17.9187 | 13.6019 | 16.5361 | 15.7086 | 13.0285 | 9.8026 | 6.4564
PUN D | 9.4835 | 9.5116 | 9.3541 | 9.3355 | 9.5588 | 9.3471 | 9.327 | 9.3646 | 9.8171 | 10.2213 | 10.6568 | 10.6179 | 10.8802 | 10.8735 | 11.3326 | 11.358 | 11.4931 | 11.4877 | 11.3409 | 10.9318 | 10.5254 | 10.5814 | 10.7961 | 10.8045
PUN E | 0.95777 | 0.94795 | 0.94185 | 0.94341 | 0.94146 | 0.93336 | 0.93067 | 0.94147 | 0.95907 | 0.95654 | 0.9411 | 0.93499 | 0.94142 | 0.94331 | 0.94325 | 0.94014 | 0.94299 | 0.93354 | 0.92898 | 0.93289 | 0.93544 | 0.93937 | 0.94151 | 0.94223
PUN F | 0.11423 | 0.1416 | 0.13025 | 0.044223 | 0.10439 | 0.50747 | 1.1237 | 1.4768 | 1.5789 | 1.3535 | 1.3253 | 1.3822 | 1.3576 | 1.1878 | 1.2144 | 1.1915 | 1.0097 | 0.66973 | 0.028864 | 0.17359 | 0.17707 | 0.20581 | 0.31983 | 0.34498
PUN G | 0.058929 | 1.157 | 0.095824 | 0.24284 | 0.16346 | 0.33711 | 1.1882 | 1.7745 | 0.48294 | 0.94757 | 0.4012 | 1.205 | 2.8984 | 2.7342 | 1.3114 | 0.0437 | 2.567 | 0.36342 | 0.72036 | 1.4243 | 0.3046 | 0.93776 | 1.8153 | 1.9272
PUN H | 12.2399 | 12.0232 | 12.1485 | 12.0569 | 11.8178 | 10.7235 | 10.6588 | 11.1804 | 11.7221 | 11.4548 | 11.2229 | 10.4844 | 10.2315 | 10.2716 | 10.0823 | 9.5407 | 9.1021 | 9.2951 | 10.4476 | 11.322 | 11.7487 | 11.9083 | 11.6322 | 12.1091
PUN I | 2.3561 | 2.2035 | 2.0321 | 2.0384 | 2.2395 | 2.6174 | 3.2073 | 3.7797 | 4.6429 | 6.4946 | 6.559 | 5.2723 | 5.3274 | 5.5236 | 4.1215 | 4.6974 | 4.1429 | 2.9093 | 2.3198 | 1.9646 | 1.0879 | 0.14495 | 0.21128 | 1.0326
PUN J | 3.7347 | 3.9829 | 4.1715 | 4.1273 | 4.1031 | 4.2485 | 4.5976 | 8.4467 | 10.2631 | 11.9003 | 11.1352 | 12.2002 | 9.8323 | 7.9631 | 8.4513 | 9.9553 | 10.2208 | 11.673 | 12.1774 | 11.2315 | 10.1678 | 9.4423 | 6.0628 | 3.8183
PUN K | 0.7165 | 0.78849 | 0.81545 | 0.77569 | 0.8329 | 0.80694 | 0.84566 | 0.79287 | 0.78887 | 0.74823 | 0.66804 | 0.77703 | 0.70921 | 0.73455 | 0.77007 | 0.82774 | 0.862 | 0.8306 | 0.83405 | 0.87591 | 0.81219 | 0.77441 | 0.80742 | 0.74673
PUN L | 7.5495 | 7.5296 | 7.6249 | 7.698 | 7.7497 | 7.4137 | 6.8116 | 6.9607 | 6.945 | 7.121 | 6.7335 | 6.5717 | 6.2979 | 6.0261 | 6.0809 | 5.685 | 6.222 | 6.5136 | 7.0151 | 7.1245 | 7.4968 | 7.4748 | 7.6837 | 7.8561

## Slide 12: Methodology
The performance of the three sets of LDFs (28-day, 7-day, and 1-day) was then evaluated.
For each 5 minutes, two calculations were done for each LDF:
  The difference between the LDF and the actual load.
  The absolute value of the difference between the LDF and the load.
The averages of both calculations were then computed for each LDF type (28 day, 7 day, and 1 day).
The performance of the three sets of LDFs (28-day, 7-day, and 1-day) was evaluated during Hurricane Harvey .

## Slide 13: Methodology
For the two PUNs with greater LDF variation (PUN B and PUN C), 1-day LDFs were also calculated.
The performance of the three sets of LDFs (28-day, 7-day, and 1-day) was then evaluated.
Snapshot Date

## Slide 14: Methodology
To evaluate the LDF performance, 5 minute load data from implementation date 11/3/2017 till 2/9/2018 was pulled.
The absolute difference between LDF and actual load was then calculated by every 5 minutes for all three LDF sets.
Snapshot Date
Load data from this period compared to posted LDFs
Next Snapshot Date

## Slide 15: Results
The graph below shows the performance of the three LDF sets for all four snapshot dates.
Note that the results have been normalized to the largest average difference for each PUN.
Chart: LDF Performance by Snapshot Date
| PUNB overall | PUNB 11/2 Snapshot | PUNB 12/13 Snapshot | PUNB 1/15 Snapshot | PUNB 1/18 Snapshot | PUNC overall | PUNC 11/2 Snapshot | PUNC 12/13 Snapshot | PUNC 1/15 Snapshot | PUNC 1/18 Snapshot
1-day abs average | 0.53196 | 0.53886 | 0.46564 | 0.55189 | 0.61818 | 0.40393 | 0.28345 | 0.51902 | 0.21217 | 0.48434
7-day abs average | 0.48839 | 0.31496 | 0.44425 | 0.61535 | 0.87102 | 0.40866 | 0.32719 | 0.48703 | 0.70942 | 0.40188
28-day abs average | 0.50513 | 0.28578 | 0.56549 | 1 | 0.7632 | 0.42282 | 0.27899 | 0.57159 | 1 | 0.38834

## Slide 16: Results
The exception to this trend are the 1/15, the LDF used for 3 days.
This is due to extreme cold weather.
Chart: LDF Performance by Snapshot Date
| PUNB overall | PUNB 11/2 Snapshot | PUNB 12/13 Snapshot | PUNB 1/15 Snapshot | PUNB 1/18 Snapshot | PUNC overall | PUNC 11/2 Snapshot | PUNC 12/13 Snapshot | PUNC 1/15 Snapshot | PUNC 1/18 Snapshot
1-day abs average | 0.53196 | 0.53886 | 0.46564 | 0.55189 | 0.61818 | 0.40393 | 0.28345 | 0.51902 | 0.21217 | 0.48434
7-day abs average | 0.48839 | 0.31496 | 0.44425 | 0.61535 | 0.87102 | 0.40866 | 0.32719 | 0.48703 | 0.70942 | 0.40188
28-day abs average | 0.50513 | 0.28578 | 0.56549 | 1 | 0.7632 | 0.42282 | 0.27899 | 0.57159 | 1 | 0.38834

## Slide 17: Results
The graph below shows the performance of the three LDF sets for overall study period.
The 3 LDF sets show the similar performance overall
Chart: LDF Performance by Interval Length
| PUNB overall | PUNC overall
1-day abs average | 0.53196 | 0.40393
7-day abs average | 0.48839 | 0.40866
28-day abs average | 0.50513 | 0.42282

## Slide 18: Results
Averaging across whole studying period again indicates that the 3 LDF sets show the similar performance overall
PUN B 7-day LDF is slightly better than other LDFs
PUN C 1-day LDF is slightly better than other LDFs
Note that the results have been normalized to the largest average difference for each PUN.
LDF type | PUN B Average Absolute Error | PUN C Average Absolute Error
1-day average | 0.531965 | 0.40
7-day average | 0.488385 | 0.41
28-day average | 0.50513 | 0.42

## Slide 19: Results
During period LDF <Load, error is calculated individually
Averaging across whole studying period again indicates that the 28-day method for calculating PUN LDFs produces the less negative error overall.
Note that the results have been normalized to the largest average difference for each PUN in each snapshot
LDF type | PUN B | PUN C
1-day average | 0.40 | 0.29
7-day average | 0.37 | 0.25
28-day average | 0.34 | 0.20

## Slide 20: Results
The LDF<load time over study period is listed below:
LDF type | PUN B | PUN C
1-day under LDF | 24% | 41%
7-day under LDF | 32% | 35%
28-day under LDF | 26% | 34%

## Slide 21: Results
For hurricane Harvey(8/17/2017 – 9/ 2/ 2017), period LDF <Load, error is calculated individually
Averaging across whole studying period again indicates that the for PUN B, 1-day method is best and for PUN C 28-day is best.
Note that the results have been normalized to the largest average difference for each PUN in each snapshot
LDF type | PUN B | PUN C
1-day average | 0.07 | 0.476
7-day average | 0.10 | 0.46
28-day average | 0.18 | 0.26

## Slide 22: Results
For Hurricane Harvey (8/17/2017 – 9/ 2/ 2017), 7/9 PUN LDF is used to calculate error individually
Averaging across whole studying period again indicates that the 28-day method for calculating PUN LDFs produces the less negative error overall.
Note that the results have been normalized to the largest average difference for each PUN in each snapshot
LDF type | PUN B | PUN C
1-day average | 0.37 | 0.36
7-day average | 0.34 | 0.40
28-day average | 0.26 | 0.34

## Slide 23: Results
The LDF<load time over hurricane Harvey is listed below:
LDF type | PUN B | PUN C
1-day under LDF | 16% | 65%
7-day under LDF | 19% | 75%
28-day under LDF | 40% | 42%

## Slide 24: Conclusion
For the majority of PUNs studied, the method for calculating LDFs did not result in significantly different values.
For the two PUNs with high variation in LDFs between calculation methods, additional analysis was performed.
The analysis indicated the LDFs calculated using the 28-day method showed the best performance overall when compared with load.