## Slide 1
Implementation: NPRR768 Revisions to
Real-Time On-Line Reliability Deployment Price Adder Categories
Pamela Shaw
ERCOT
March 19, 2018

## Slide 2: Implementation: NPRR768
Changes associated with DC Tie Imports and Exports
Changes associated with registered Block Load Transfers

## Slide 3: Implementation: NPRR768
Changes associated with DC Tie Imports and Exports
  6.5.7.3.1 Determination of Real-Time On-Line Reliability Deployment Price Adder
  (f) Add the MW from Real-Time DC Tie imports during an EEA to GTBD. The amount of MW is determined from the Dispatch Instruction and should continue over the duration of time specified by the ERCOT Operator.
  (g) Subtract the MW from Real-Time DC Tie exports to address emergency conditions in the receiving electric grid from GTBD. The amount of MW is determined from the Dispatch Instruction and should continue over the duration of time specified by the receiving grid operator.

## Slide 4: Implementation: NPRR768
1. The SCED shall use the UPTOMW from emergency DC Tie VDI as the dispatch instruction MW.
2. The SCED shall add the DC Tie import to the GTBD in the pricing run only if the EEA flag is active. It shall not be considered if the EEA flag is inactive. For DC Tie exports, the existence of the VDI assumes “emergency conditions in the receiving electric grid.”
3. The SCED shall sum up all the DC Tie imports and exports if multiple DC Tie import/export VDI have been issued.
4. The SCED shall have a configurable parameter for the DC Tie Import Cap. The default value is 1250MW.
5. The SCED shall apply this DC Tie Import Cap to the emergency DC Tie import when add it to the GTBD.

## Slide 5: Implementation: NPRR768
Changes associated with Registered Block Load Transfers
  6.5.7.3.1 Determination of Real-Time On-Line Reliability Deployment Price Adder
  (h) Add the MW from energy delivered to ERCOT through registered BLTs during an EEA to GTBD. The amount of MW is determined from the Dispatch Instruction and should continue over the duration of time specified by the ERCOT Operator.
  (i) Subtracted the MW from energy delivered from ERCOT to another power pool through registered BLTs during emergency conditions in the receiving electric grid from GTBD. The amount of MW is determined from the Dispatch Instruction and should continue over the duration of time specified by the receiving grid operator.

## Slide 6: Implementation: NPRR768
The SCED shall use the UPTOMW from emergency BLT VDI as the dispatch instruction MW.
The SCED shall add the BLT MW for energy delivered to ERCOT to the GTBD in the pricing run only if the EEA flag is active. It shall not be considered if the EEA flag is inactive. For BLT MW for energy delivered from ERCOT, the existence of the VDI assumes “emergency conditions in the receiving electric grid.”
The SCED shall sum up all the BLT imports and exports if multiple BLT import/export VDI have been issued.

## Slide 7: Implementation: NPRR768
Questions?