## Slide 1
ERS Deployment, Recall & Renewal Review
DSWG Meeting – April 20, 2018
Anson Lee
Notes: This presentation is about ERS deployment, Recall and Renewal.

## Slide 2: Outline
Pre ERS Deployment
Preparation
During ERS Deployment
When to deploy
When to resume normal operations
Post ERS Deployment
Obligation Exhaustion
Contract Renewal

## Slide 3: Pre ERS Deployment

## Slide 4: Know Thy Resources
Obligated time period(s)
Ramp
Unavailability/Planned Maintenance interval(s)
  Properly scheduled
  within 2% of total number of obligated intervals.
Cumulative Deployment Obligation time
  Deployment Obligation Time: The cumulative time during the Sustained Response Period of an event during which an ERS resource has an obligation
TP1
TP1
Obligation
Event 1
Event
Event 2
Deployment Obligation Time = 2 hours
Deployment Obligation Time = 3 hours
Cumulative deployment Obligation time after Event 1 = 3 hours
Cumulative deployment Obligation time after Event 2 = 5 hours
3.5 hours
2.5 hours
Day 2
Day 1
Notes: Section 3.14.3.3(2)

## Slide 5: What to expect?
Deployment
  EEA level 1
    ERS-30 resources
  EEA Level 2
    ERS-10 resources and un-deployed ERS-30 resources
Communication
  Deployment
    XML Message, followed by VDI to all-QSE hotline
    The ramp period shall begin at the completion of the VDI
  Release
    XML Message, followed by VDI to all-QSE hotline
    VDI represents the official notice of the release
Notes: Section Reference:
6.5.9.4.2(1)(a)
6.5.9.4.2(2)(a)

## Slide 6: During ERS Deployment

## Slide 7: Whether to deploy
The resource should
Deploy if
  It is contractually committed to provide the ERS service type deployed during the ERS Time Period that includes all or any part of the first interval of the Sustained Response Period, with the following exceptions:
    Properly scheduled unavailability, planned maintenance within the 2% limit
    10-hour-recovery period from a previous deployment
Not required to deploy if
  It does not have an obligation for any part of the first interval of the Sustained
  Response Period.
Deploy if obligated during any part of the first interval
Notes: Section Reference:
3.14.3.3 (1)

## Slide 8: Knowledge Checkpoint 1

## Slide 9: Scenario 1: Should Resource 1 deploy?
Obligated
hours
Time
VDI
Starts
VDI
Stops
First Interval
Sustained
Response Period
Sustained Response Period
Starts
Deploy!
If ERCOT deploys ERS, any ERS Resource that is contractually committed to provide the ERS service type deployed during the ERS Time Period that includes all or any part of the first interval of the Sustained Response Period must deploy.
Notes: Section Reference:
3.14.3.3 (1)

## Slide 10: Scenario 2: Should Resource 2 deploy?
Obligated
hours
Time
First Interval
Sustained
Response Period
Deploy!
If ERCOT deploys ERS, any ERS Resource that is contractually committed to provide the ERS service type deployed during the ERS Time Period that includes all or any part of the first interval of the Sustained Response Period must deploy
VDI
Starts
VDI
Stops
Sustained Response Period
Starts
Notes: Section Reference:
3.14.3.3 (1)

## Slide 11: Scenario 3: Should Resource 3 deploy?
Obligated
hours
Time
VDI
Starts
VDI
Stops
First Interval
Sustained Response
Period
Sustained Response Period
Starts
Not required to deploy.
If an ERS Resource does not have an obligation for any part of the first interval of the Sustained Response Period, the ERS Resource is not required to deploy at any time during the Sustained Response Period.
Obligated
hours
Notes: Section Reference:
3.14.3.3 (1)

## Slide 12: Scenario 4: Should Resource 4 deploy?
Obligated
hours
Time
VDI
Starts
VDI
Stops
First Interval
Sustained
Response Period
Sustained Response Period
Starts
Deploy!
If ERCOT deploys ERS, any ERS Resource that is contractually committed to provide the ERS service type deployed during the ERS Time Period that includes all or any part of the first interval of the Sustained Response Period must deploy.
Notes: Section Reference:
3.14.3.3 (1)

## Slide 13: Deployment Obligation
An ERS Resource shall not return to normal operations
  until released to do so by ERCOT or
  until the ERS Resource has reached its maximum deployment obligation time
  whichever occurs first.
Notes: Section Reference:
Section 3.14.3.3 (5)(b)

## Slide 14: Deployment Obligation
2 If an ERS deployment is still in effect when the Weather-Sensitive ERS Resource’s cumulative deployment obligation time equals or exceeds eight hours, the ERS Resource must continue to meet its event performance requirements until the three-hour maximum deployment obligation time for that event is met or ERCOT releases the ERS Load, whichever comes first.
1 For a Non-Weather-Sensitive ERS Resource, if an ERS deployment is still in effect when the ERS Resource’s cumulative deployment obligation time equals or exceeds eight hours, the ERS Resource must continue to meet its event performance requirements for the next four hours or until ERCOT releases the ERS Resource, whichever comes first.
Notes: Section Reference:
Non-Weather-Sensitive: Section 3.14.3.3 (3)(a)
Weather-Sensitive: Section 3.14.3.3 (3)(b)

## Slide 15: Knowledge Checkpoint 2

## Slide 16: During ERS Deployment Non-Weather-Sensitive (Non-WS)
Scenario 5
Resource 5 (Non-Weather-Sensitive) has a 30 minute ramp, a TP1 (6:00 AM - 8:00 AM) obligation of 10 MW, a TP2 (8:00 AM - 1:00 PM) obligation of 10 MW, a TP3 (1:00 PM - 4:00 PM) obligation of 10 MW and a TP4 (4:00 PM - 7:00 PM) obligation of 10 MW .The deployment instruction is issued at 5:30AM on a weekday. Resource 5 started deploying at 6AM.
(a) At 2PM, the cumulative deployment time reaches 8 hours. Can Resource 5 resume its normal operation after 2PM, if recall was never issued?
(b) If the recall was never issued at 6PM, can Resource 5 resume its normal operation after 6PM?

## Slide 17: Scenario 5: Resource 5 (ERS-30) No event prior to this event
2. Sustained Response Period started at 6am and Resource 5 deployed
1. VDI issued at 5.30am
3. Resource 5 has deployed for 8 hours at 2pm
Question 1:
Can they resume normal operation at 2pm?
Question 2:
Can they resume normal operation at 6pm if recall has not yet been issued?
Yes
No
Obligated in all time periods
Notes: Scenario 5
Resource 5 (Non-Weather-Sensitive) has a 30 minute ramp, a TP1 (6:00 AM - 8:00 AM) obligation of 10 MW, a TP2 (8:00 AM - 1:00 PM) obligation of 10 MW, a TP3 (1:00 PM - 4:00 PM) obligation of 10 MW and a TP4 (4:00 PM - 7:00 PM) obligation of 10 MW .The deployment instruction is issued at 5:30AM on a weekday. Resource 5 started deploying at 6AM.
(a) At 2PM, the cumulative deployment time reaches 8 hours. Can Resource 5 resume its normal operation after 2PM, if recall was never issued?
(b) If the recall was never issued at 6PM, can Resource 5 resume its normal operation after 6PM?
Reference Section: Section 3.14.3.3 (3)(a)
if an ERS deployment is still in effect when the ERS Resource’s cumulative deployment obligation time equals or exceeds eight hours, the ERS Resource must continue to meet its event performance requirements for the next four hours or until ERCOT releases the ERS Resource, whichever comes first.

## Slide 18: During ERS Deployment Weather-Sensitive
Scenario 6
Resource 6 (Weather Sensitive) has a 30 minute ramp, a TP3 (1:00 PM - 4:00 PM) obligation of 10 MW and a TP4 (4:00 PM - 7:00 PM) obligation of 10 MW. The deployment instruction is issued at 12.30 PM on a weekday. Resource 6 deployed at 1PM. Prior to the event, Resource 6 has a cumulative deployment time of 7 hours.
(a) If the recall was never issued, when can Resource 6 resumes its normal operation without affecting its event performance?

## Slide 19: Scenario 6: Resource 6 (ERS-30 WS) Cumulatively deployed for 7 hours before the event
2. Sustained Response Period started at 1pm and Resource 6 deployed
1. VDI issued at 12.30pm
3. Cumulative deployment obligation time reached 8 hours at 2pm
Question 3:
When is the earliest time Resource 6 can resume its normal operation if recall has not yet been issued?
4pm
Because the maximum event deployment obligation time for Weather Sensitive
is 3 hours
Obligated in TP3
(1pm-4pm)
and TP4
(4pm -7pm)
Event reached 3 hours at 4pm
Notes: Scenario 6
Resource 6 (Weather Sensitive) has a 30 minute ramp, a TP3 (1:00 PM - 4:00 PM) obligation of 10 MW and a TP4 (4:00 PM - 7:00 PM) obligation of 10 MW. The deployment instruction is issued at 12.30 PM on a weekday. Resource 6 deployed at 1PM. Prior to the event, Resource 6 has a cumulative deployment time of 7 hours.
(a) When is the earliest time Resource 6 can resume its normal operation if recall has not yet been issued?
4pm
Because the maximum event deployment obligation time for Weather Sensitive
is 3 hours
Reference Section: Section 3.14.3.3(3)(b)(iii)
If an ERS deployment is still in effect when the Weather-Sensitive ERS Resource’s cumulative deployment obligation time equals or exceeds eight hours, the ERS Resource must continue to meet its event performance requirements until the three-hour maximum deployment obligation time for that event is met or ERCOT releases the ERS Load, whichever comes first.

## Slide 20: Post ERS Deployment

## Slide 21: Post ERS deployment
ERCOT will communicate the official VDI times (both deployment and release) for the event.
Keep track on cumulative deployment obligation time for each of your resources
  Use official VDI time for both deployment and release
Determine which resource has exhausted its obligation
  When Cumulative Deployment Obligation time reached 8 hours

## Slide 22: Three possible outcomes
None of the resources exhausted its obligation
At least one of the resources exhausted its obligation and ERCOT decided to renew
At least one of the resources exhausted its obligation and ERCOT decided not to renew
Note: if ERS resource(s) migrates to a Must-Run Alternative contract, the contract would be renewed as well.

## Slide 23: If none of the resources exhausted its obligation,
ERS SCT continues
Cumulative Deployment Obligation time is calculated for each resource.
24
During event
5 hours
Cumulative
Deployment Obligation Time
= 5 hours
Deployed
After Event
Contract period
Cumulative
Deployment Obligation Time
= 0 hours
Before Event
Notes: Protocol References:
3.14.3.1(16)(a)
3.14.3.1(18)(b)

## Slide 24: If at least one of the resources exhausted its obligation and ERCOT decided not to renew,
All the resources that exhausted their obligation in a previous contract period are no longer obligated in the new contract period.
A new contract period will begin
24
1st contract period
5 hours
Cumulative
Deployment Obligation Time = 5 hours
Deployed
Standard Contract Term
2nd contract period
Did not exhaust
No obligation
Standard Contract Term
Exhausted but not renewed
1st contract period
8 hours
Deployed
2nd contract period
For all resources that did not exhaust their obligation in a previous contract period, Cumulative Deployment Obligation time is rolled over from previous contract period for each resource.
Notes: Protocol References:
3.14.3.1(16)(b)
3.14.3.1(18)(b)

## Slide 25: If at least one of the resources exhausted its obligation and ERCOT decided to renew,
A new contract period will begin.
24
1st contract period
5 hours
Cumulative Deployment Obligation Time = 5 hours
Deployed
Standard Contract Term
2nd contract period
Did not exhaust
Cumulative Deployment Obligation Time = 0 hours
Standard Contract Term
Exhausted but renewed
1st contract period
8 hours
Deployed
2nd contract period
For all the resources that exhausted their obligation in a previous contract period, their Cumulative Deployment Obligation time will be reset to zero.
For all resources that did not exhaust their obligation in a previous contract period, Cumulative Deployment Obligation time is rolled over from previous contract period for each resource.
Notes: Protocol References:
3.14.3.1(16)(c)
3.14.3.1(18)(b)

## Slide 26: Contract Renewal
Only exhausted resources which opted for renewal will be considered for renewal
ERCOT will determine which service-type(s) and time-period(s) to renew
By the end of the 2nd business day of renewed contract, QSE may revoke the renewal opt-in status for future contract periods
By the end of the 3rd Business Day in any ERS Contract Period (other than the first), ERCOT shall communicate to QSEs a confirmation of the terms of participation for all of their committed resources.
24
Notes: Protocol References:
3.14.3.1(18)(c)

## Slide 27: Remarks
Deploy if you are not sure.
If you are not sure when to resume normal operation, wait until the official release notice from ERCOT before you do.