## Slide 1
Virtual Transactions at Certain Generation Resource Nodes within PUN sites
OBDRR003/SCR796
Carrie Bivens
Manager, Forward Markets
April 30, 2018

## Slide 2: History
At the February 12 CMWG, ERCOT discussed issues related to virtual transactions flowing over unsecured (i.e., limits not enforced) transmission equipment, which were implicated in late DAM publishing times.
On March 9, ERCOT secured a subset of step-up transformers in DAM and subsequent CRR auctions.
  More time was needed to create a proposal for handling transmission equipment within PUN sites.

## Slide 3: Problem statement
Based on current practice of both allowing virtual transactions within some PUN sites and also not securing transmission equipment within PUN sites:
Power flow divergence can occur in DAM on unsecured equipment, leading to issues solving in a timely manner.
Overselling can occur which could potentially impact RENA.

## Slide 4: Proposed Resolution
Modify where financial/virtual transactions (Energy Bids, Energy Only Offers, PTP Obligation bids, and CRRs) can occur (see next slide for details).
Because only physical flows would be occurring within the PUN site, the PUN transmission equipment can remain unsecured. The approach of having certain nodes biddable and others not is analogous to how Logical Combined Cycle Resource Nodes are handled.
Note that there are NO changes to real-time in OBDRR003/SCR796.

## Slide 5: Proposed Resolution (cont’d)
  Continue to allow virtual transactions at PUN Resource Nodes (XXXXXX_PUN1).
  Continue to allow virtual transactions at generator Resource Nodes in PUN stations where there are no constrainable elements between the Generation Resource Node (GRN) and the meter.
  Disallow virtual transactions at generator Resource Nodes in PUN stations where there ARE constrainable elements between the GRN and the meter.
    Based on the current model, there are 81 generator Resource Nodes in PUNs.
      Of those, 37 would remain biddable and 44 would be non-biddable.

## Slide 6: When is a PUN GRN biddable?
According to the rules proposed in OBDRR003, PUN GRNs would be considered biddable if they are located in the same power flow bus as one or more of the EPS meters designated for that PUN site.
If there is at least one constrainable transmission element (transformer/line/series device) between a PUN GRN and each of the EPS meters for that PUN site, the PUN GRN will be precluded from virtual transactions (EOOs/EBs/PTPs/CRRs).

## Slide 7: Example 1 – PUN GRN behind a Transformer
G1_RN
Consider PUN Station A below.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
EPS_G1
EPS_G2
A_PUN1

## Slide 8: Example 1 – PUN GRN behind a Transformer
G1_RN
Consider PUN Station A below. There are two generators and two Points of Interconnection(POI).
~
PUN Station A
G1
~
G2
ERCOT Equipment
PUN Equipment
Point of Interconnection(POI)
G2_RN
A_PUN1
EPS_G1
EPS_G2

## Slide 9: Example 1 – PUN GRN behind a Transformer
G1_RN
Consider PUN Station A below. There are two generators and two Points of Interconnection(POI).
PUN GRN, G1_RN, is adjacent to the POI at EPS meter, EPS_G1.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
EPS_G1
EPS_G2
A_PUN1

## Slide 10: Example 1 – PUN GRN behind a Transformer
G1_RN
Consider PUN Station A below. There are two generators and two Points of Interconnection(POI).
PUN GRN, G1_RN, is adjacent to the POI at EPS meter, EPS_G1.
PUN GRN, G2_RN, is placed on the low side of its generator’s step up transformers.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
EPS_G1
EPS_G2
A_PUN1

## Slide 11: Example 1 – PUN GRN behind a Transformer
G1_RN
The power flow buses are split by lines and transformers.
~
PUN Station A
G1
~
G2
EPS_G1
G2_RN
ERCOT Equipment
PUN Equipment
Power Flow Buses
EPS_G2
A_PUN1

## Slide 12: Example 1 – PUN GRN behind a Transformer
Biddable
G1_RN
The power flow buses are split by lines and transformers.
In this example, G1_RN is biddable because it is in the same power flow bus as an EPS meter for the PUN site.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
EPS_G1
EPS_G2
A_PUN1

## Slide 13: Example 1 – PUN GRN behind a Transformer
Biddable
G1_RN
The power flow buses are split by lines and transformers.
In this example, G1_RN is biddable because it is in the same power flow bus as an EPS meter for the PUN site.
G2_RN is not biddable because there exists constrainable equipment between it and the EPS meters for the PUN site.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
Not Biddable
EPS_G1
EPS_G2
A_PUN1

## Slide 14: Example 1 – PUN GRN behind a Transformer
G1_RN
PUN Resource Nodes will always remain biddable.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
Not Biddable
EPS_G1
EPS_G2
Biddable
A_PUN1

## Slide 15: Example 2a – EPS Meter Outside PUN Station
G2_RN
G1_RN
Consider the example below where the POIs are outside PUN Station A.
~
PUN Station A
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
Station B
EPS_G1

## Slide 16: Example 2a – EPS Meter Outside PUN Station
G2_RN
G1_RN
Consider the example below where the POIs are outside PUN Station A.
The PUN GRNs are outside the PUN station as well.
~
PUN Station A
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
EPS_G1
Station B

## Slide 17: Example 2a – EPS Meter Outside PUN Station
G2_RN
G1_RN
Consider the example below where the POIs are outside PUN Station A.
The PUN GRNs are outside the PUN station as well.
The power flow buses are split by lines and transformers.
~
PUN Station A
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
Power Flow Buses
EPS_G1
Station B

## Slide 18: Example 2a – EPS Meter Outside PUN Station
G2_RN
G1_RN
In this example, G1_RN and G2_RN are in the same power flow bus as an EPS meter for the PUN site.
~
PUN Station A
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
EPS_G1
Station B

## Slide 19: Example 2a – EPS Meter Outside PUN Station
Biddable
G2_RN
G1_RN
In this example, G1_RN and G2_RN are in the same power flow bus as an EPS meter for the PUN site.
G1_RN and G2_RN are biddable.
~
PUN Station A
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
EPS_G1
Station B

## Slide 20: Example 2b – EPS Meter Outside PUN Station
G2_RN
PUN Station A
G1_RN
Consider another example where the POI is outside PUN Station A.
~
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
Station B
EPS_G1
A_PUN1
A_PUN2

## Slide 21: Example 2b – EPS Meter Outside PUN Station
G1_RN
Consider another example where the POI is outside PUN Station A.
This time the PUN GRNs are placed inside PUN Station A, and the PUN Resource nodes are placed at the POI.
~
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
G2_RN
Station B
PUN Station A
EPS_G1
A_PUN1
A_PUN2

## Slide 22: Example 2b – EPS Meter Outside PUN Station
G1_RN
Consider another example where the POI is outside PUN Station A.
This time the PUN GRNs are placed inside PUN Station A, and the PUN Resource nodes are placed at the POI.
The power flow buses separated by lines and transformers.
~
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
G2_RN
Power Flow Buses
Station B
PUN Station A
EPS_G1
A_PUN1
A_PUN2

## Slide 23: Example 2b – EPS Meter Outside PUN Station
G1_RN
The PUN GRNs are not in the same power flow bus as the EPS meters for this PUN site.
~
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
G2_RN
Station B
PUN Station A
EPS_G1
A_PUN1
A_PUN2

## Slide 24: Example 2b – EPS Meter Outside PUN Station
G1_RN
The PUN GRNs are not in the same power flow bus as the EPS meters for this PUN site.
G1_RN and G2_RN are not biddable.
~
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
G2_RN
Not Biddable
Station B
PUN Station A
EPS_G1
A_PUN1
A_PUN2

## Slide 25: Example 2b – EPS Meter Outside PUN Station
A_PUN1
A_PUN2
Biddable
G1_RN
The PUN GRNs are not in the same power flow bus as the EPS meters for this PUN site.
G1_RN and G2_RN are not biddable.
The PUN Resource Nodes are biddable.
~
G1
~
G2
EPS_G2
ERCOT Equipment
PUN Equipment
G2_RN
Not Biddable
Station B
PUN Station A
EPS_G1