## Slide 1
Interaction of LCAP, VOLL, and ORDC
Wholesale Market Subcommittee (WMS)
ERCOT
May 2, 2018

## Slide 2: Introduction
There have been some questions regarding the interactions between the low system-wide offer cap (LCAP), the Value of Lost Load (VOLL), and the Operating Reserve Demand Curve (ORDC) and we wanted to discuss the topic with WMS.
The interactions and potential issues described in this presentation are relevant only if the cumulative Peaker Net Margin (PNM) exceeds $315,000/MW-year.
  The highest historical PNM of ~$125,000/MW-year occurred in 2011.

## Slide 3: Agenda
Scarcity pricing mechanism
ORDC and System-Wide Offer Cap (SWOC) interaction – Brattle
VOLL and ORDC interaction
VOLL and LCAP interaction
DAM Ancillary Service Offers

## Slide 4: Scarcity Pricing Mechanism
Directed by PUCT Substantive rule
  Chapter 25, Subchapter S
  Paragraph (g) Scarcity Pricing Mechanism
  Peaker Net Margin (PNM) Threshold = 3 x CONE
  Cost of New Entry (CONE) = $105,000 $/MW-year
  PNM Threshold = $315,000 $/MW-year
  SWOC is equal to HCAP ($9,000 $/MWh) until PNM Threshold reached; then
  SWOC = LCAP
  LCAP = greater of $2,000 per $/MWh or 50 x FIP in $/MWh (Houston Ship Channel)

## Slide 5: LCAP and ORDC
Brattle EORM study 2014
http://files.brattle.com/system/publications/pdfs/000/004/978/original/estimating_the_economically_optimal_reserve_margin_in_ercot_revised.pdf?1395159117 page 29
“Consistent with current market rules, we tabulate the Peaker Net Margin (PNM) over the calendar year and reduce the System-Wide Offer Cap (SWOC) to the Low System-Wide Offer Cap (LCAP) of $2,000/MWh after the PNM threshold is exceeded. However, we stress that this mechanism will have much less impact on the market than it has previously because the LCAP now only affects the Power Balance Penalty Curve (PBPC) and suppliers’ offers, but does not affect the Operating Reserves Demand Curve (ORDC). Therefore, prices will still rise gradually to the VOLL of $9,000 in shortage conditions even after the PNM threshold is exceeded, thereby rendering the LCAP far less important.”

## Slide 6: VOLL and ORDC
From the Methodology for Implementing ORDC to Calculate Real-Time Reserve Price Adders:
2.3. Determination of Price Adders (RTORPA and RTOFFPA)
Once PBMCL is determined, the Real-Time On-Line Reserve Price Adder (RTORPA) and Real-Time Off-Line Reserve Price Adder (RTOFFPA) for each SCED interval can be calculated. RTORPA (a.k.a. PS) and RTOFFPA (a.k.a. PNS) are functions of the PBMCL at various levels of Real-Time reserves, the net value of Load curtailment, and time duration during which the reserves are available. RTORPA and RTOFFPA are determined as follows:
Where v represents the net value of Load curtailment and is calculated as the VOLL minus the SCED System Lambda. System Lambda is subtracted from VOLL to reflect the scarcity value of the marginal dispatch capacity and to ensure that the final cost of energy does not go above the VOLL. The Off-Line Available Reserves (RTOFFCAP) will be set to zero when the SCED snapshot of the PRC is equal to or below the PRC MW at which EEA Level 1 is initiated.
Notes: PBMCL = probability of reserves falling below the minimum contingency level

## Slide 7: VOLL and LCAP
Issue: If VOLL is $9,000/MWh and LCAP is only $2,000/MWh then System Lambda will not be greater than $2,000/MWh; however the RTORPA could rise to $7,000. What are repercussions? Is any action needed?
  We have precedent on this issue. When ORDC was implemented in 2014 the VOLL was at $9,000/MWh and the SWOC was at $7,000/MWh. There did not appear to be any concerns raised at that time.
  One concern that comes to mind is questioning if Resources will offer to provide Ancillary Services in the DAM if the SWOC is $2,000/MWh, since they run the risk that the combined price will potentially rise to $9,000/MWh (RTORPA = $7k/MWh + $2k/MWh System Lambda) in Real-Time.

## Slide 8: Insufficient AS Offers in DAM
  IF this happened (not enough offers), what is ERCOT’s Ancillary Service procurement process?
    4.5.2 Ancillary Service Insufficiency
    (2) ERCOT shall procure the difference in capacity between the Day-Ahead Ancillary Service Plan and the DAM-reduced Ancillary Service Plan amounts using the
    1. Supplemental Ancillary Service Market (SASM) process in accordance with Section 6.4.9.2.2, SASM Clearing Process.
    2. If the SASM process is insufficient, then ERCOT may acquire the insufficient amount of Ancillary Services from Hourly Reliability Unit Commitment (HRUC) Resources that are qualified to provide the needed Ancillary Service.
    3. ERCOT may also issue a Watch and procure Ancillary Services in accordance with Section 6.5.9.3.3.
    6.5.9.3.3 Watch
    (c) If the insufficiency arose due to insufficient Ancillary Service Offers received in the DAM or ERCOT needs to increase the Ancillary Service requirements after DAM clearing, ERCOT may assign the insufficient amounts of Ancillary Service(s) to QSEs with planned On-Line Resources qualified to provide the insufficient Ancillary Service(s), even if there are no existing Ancillary Service Offers for those QSEs’ Resources.

## Slide 9
Next Steps?