## Slide 1
Nodal Pricing for Non-Modeled Generators & Distributed Generation Registered with ERCOT for Settlements
ERCOT Staff
WMS Meeting
May 2, 2018

## Slide 2: Background
From Section 2 of the ERCOT Nodal Protocols:
Non-Modeled Generator
A generator that is:
(a) Capable of providing net output of energy to the ERCOT System;
(b) Ten MW or less in size; or greater than ten MW and registered with the PUCT according to P.U.C. Subst. R. 25.109, Registration of Power Generation Companies and Self-Generators, as a self-generator; and
Registered with ERCOT as a Non-Modeled Generator, which means that the generator may not participate in the Ancillary Service or energy markets, RUC, or SCED.
This NPRR would also affect Distributed Generation registered with ERCOT pursuant to Section 16.5
  Registration is required for units >1 MW that inject to the grid
  Registration is optional for smaller units

## Slide 3: Distributed Generation affected by this proposal
Registered DG | No. of Units | MW
Renewable | 125 | 451
Non-Renewable | 45 | 244
TOTALS | 170 | 694
Chart: ACCUMULATED COUNT Registered DGs, Q409 – Q218 (as of 4/26/2018)
| 2009-Q4 | 2010-Q1 | 2010-Q2 | 2010-Q3 | 2010-Q4 | 2011-Q1 | 2011-Q2 | 2011-Q3 | 2011-Q4 | 2012-Q1 | 2012-Q2 | 2012-Q3 | 2012-Q4 | 2013-Q1 | 2013-Q2 | 2013-Q3 | 2013-Q4 | 2014-Q1 | 2014-Q2 | 2014-Q3 | 2014-Q4 | 2015-Q1 | 2015-Q2 | 2015-Q3 | 2015-Q4 | 2016-Q1 | 2016-Q2 | 2016-Q3 | 2016-Q4 | 2017-Q1 | 2017-Q2 | 2017-Q3 | 2017-Q4 | 2018-Q1 | 2018-Q2
ACCUMULATED COUNT | 16 | 17 | 17 | 19 | 20 | 21 | 21 | 23 | 23 | 26 | 32 | 32 | 32 | 32 | 48 | 50 | 51 | 55 | 56 | 57 | 59 | 62 | 66 | 67 | 68 | 71 | 73 | 75 | 82 | 94 | 114 | 125 | 141 | 154 | 170
(Numbers don’t add up due to rounding of fractions)

## Slide 4: Benefits of Nodal Pricing
Non-Modeled Generators and registered DGs have always been settled at the applicable Load Zone price
Nodal (instead of zonal) pricing would provide proper incentives for Non-Modeled Generators and registered DG in transmission-constrained areas, such as:
  Generation pockets where Generation Resources are receiving negative LMPs due to transmission constraints, but the zonal price remains positive. In such cases, positive zonal price signals provide perverse incentives for Non-Modeled Generators to continue producing or even increase production.
  Load pockets where Generation Resources are receiving LMPs that are much higher than the zonal price due to transmission constraints. In such cases the diluted zonal prices fail to provide Non-Modeled Generators and DG registered with ERCOT with the incentive to produce and thus help to resolve the constraint.

## Slide 5: High-level description of pricing proposal
ERCOT’s draft NPRR proposes to extend applicable nodal pricing to Non-Modeled Generators and registered DGs
  This would enable operation and production consistent with Nodal market design and the reliability needs of the ERCOT system
The NPRR would establish nodal pricing as follows:
  For Non-Modeled Generators that are already modeled, the time-weighted price at the electrical bus determined by ERCOT in review of the meter location in the Model
  In the Real-Time Market, a nodal price is currently being calculated for each CIM Load every 5 minutes
  Registered DG units would receive the price at the CIM Load to which the unit is mapped, per NPRR 866

## Slide 6: Precursor to Nodal Pricing
NPRR 866, currently pending (tabled at PRS), will create a methodology for mapping registered DG units to the transmission grid
  Mapping is not the same as modeling
A mapped registered DG unit would be associated with a Load point in the Common Information Model (CIM Load)

## Slide 7: What the NPRR will NOT do:
This NPRR:
  Would NOT create new Resource Nodes
  Would NOT introduce new Settlement Points
  Would NOT affect the CRR Markets
The NPRR would not apply to unregistered DG (e.g., residential/commercial rooftop solar PV)
The NPRR will not propose to address Wholesale Storage Load treatment for a storage facility in which the re-generated energy is provided by a Non-Modeled Generator or registered DG
  This may need to be addressed in a subsequent NPRR

## Slide 8: Terminology notes
The term ‘Non-Modeled Generator’ is proposed to be eliminated and replaced by other, more descriptive terms
  Under active discussion at Resource Definition Task Force (RTF)
Framework for proposed definition modifications can be viewed at: http://www.ercot.com/calendar/2018/3/26/149862-RTF
Until the term is retired, we will continue to use it

## Slide 9
Questions?