## Slide 1
Day-Ahead Market Price Corrections (NPRR807)
Carrie Bivens
Manager, Forward Markets
May 2, 2018

## Slide 2: Status Quo
Protocol section 4.5.3(4) requires ERCOT to correct DAM prices if accurate prices can be determined when (a) a market solution is invalid, or (b) invalid prices has been identified in a valid market solution. Certain data input errors, software errors, and inconsistency with the Protocols and/or PUC rules can cause an invalid market solution or invalid prices.
Implications:
Would require ERCOT to rerun DAM with the error corrected, obtaining new prices.
  When you rerun a DAM, changes can occur that are unrelated to the original error due to solution parameters (MIP gap).

## Slide 3: Status Quo
Implications (cont’d):
Those new prices may be inconsistent with the original award.
  Example: Energy Bid of 50 MW for $50 at LZ_NORTH. Original DAM award was 50 MW with a clearing price of $50. New DAM price after rerunning DAM is $60. ERCOT corrects the price to $60 and uses that price for DAM settlements.
  Would likely lead to many disputes.
Real-time commitment decisions and external transactions were initiated based on original prices.

## Slide 4: Another option
If stakeholders prefer to retain the price correction concept, another implementation could be full resettlement with new prices AND new awards.
Implications:
Errors are corrected.
Change both prices and awards.
  Resettle DAM with that new data, then adjust/resettle real-time based on new energy imbalances.
  Again, changes can occur that are unrelated to the original error due to solution parameters (MIP gap).
Commitment decisions and initiation of trades occurred based on initial solution, so some QSEs might find themselves unexpectedly unhedged after-the-fact.
Ancillary Services awards could change after the service is provided

## Slide 5: ERCOT proposal in NPRR807
NPRR807 states that DAM prices won’t be corrected if the price correction would lead to price/dispatch inconsistency based on the original MWs. Price validation process occurs prior to publishing (uses same inputs as DAM).
Implications:
Awards and prices are consistent.
Price certainty for resource commitment decisions, provision of Ancillary Services, and external ERCOT activity, reducing risk of post hoc changes.
Errors in past solutions are unmodified. Could cause lost opportunity if an error caused something not to be awarded.

## Slide 6: Hypothetical Scenario
Consider the following illustrative example:
Say ERCOT staff makes an error inputting a manual contingency into MMS and that incorrect contingency ends up binding in the published DAM solution. Because many Resource Nodes have shift factors to that contingency, prices for those Resource Nodes are affected. Redispatch due to that contingency constraint occurred as well. ERCOT identifies the error within current protocol price correction timelines.
What should be the response to this ERCOT error, if any?