## Slide 1
Virtual Transactions at Certain Generation Resource Nodes within PUN sites
SCR796/OBDRR003
Carrie Bivens
Manager, Forward Markets
May 2, 2018

## Slide 2: Problem statement
Based on current practice of both allowing virtual transactions within some PUN sites and also not securing transmission equipment within PUN sites (i.e., enforcing limits):
Power flow divergence can occur in DAM on unsecured equipment, leading to issues solving in a timely manner.
Overselling can occur which could potentially impact RENA.

## Slide 3: Proposed Resolution
Modify where financial/virtual transactions (Energy Bids, Energy Only Offers, PTP Obligation bids, and CRRs) can occur (see next slide for details).
Because only physical flows would be occurring within the PUN site, the PUN transmission equipment can remain unsecured. The approach of having certain nodes biddable and others not is analogous to how Logical Combined Cycle Resource Nodes are handled.
Note that there are NO changes to real-time in OBDRR003/SCR796.

## Slide 4: Proposed Resolution (cont’d)
  Continue to allow virtual transactions at PUN Resource Nodes (XXXXXX_PUN1).
  Continue to allow virtual transactions at generator Resource Nodes in PUN stations where there are no constrainable elements between the Generation Resource Node (GRN) and the meter.
  Disallow virtual transactions at generator Resource Nodes in PUN stations where there ARE constrainable elements between the GRN and the meter.
    Based on the current model, there are 82 generator Resource Nodes in PUNs.
      Of those, 37 would remain biddable and 45 would be non-biddable.

## Slide 5: When is a PUN GRN biddable?
According to the rules proposed in OBDRR003, PUN GRNs would be considered biddable if they are located in the same power flow bus as one or more of the EPS meters designated for that PUN site.
If there is at least one constrainable transmission element (transformer/line/series device) between a PUN GRN and each of the EPS meters for that PUN site, the PUN GRN will be precluded from virtual transactions (EOOs/EBs/PTPs/CRRs).

## Slide 6: Example 1 – PUN GRN behind a Transformer
G1_RN
Consider PUN Station A below.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
EPS_G1
EPS_G2
A_PUN1

## Slide 7: Example 1 – PUN GRN behind a Transformer
G1_RN
Consider PUN Station A below. There are two generators and two Points of Interconnection(POI).
~
PUN Station A
G1
~
G2
ERCOT Equipment
PUN Equipment
Point of Interconnection(POI)
G2_RN
A_PUN1
EPS_G1
EPS_G2

## Slide 8: Example 1 – PUN GRN behind a Transformer
G1_RN
Consider PUN Station A below. There are two generators and two Points of Interconnection(POI).
PUN GRN, G1_RN, is adjacent to the POI at EPS meter, EPS_G1.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
EPS_G1
EPS_G2
A_PUN1

## Slide 9: Example 1 – PUN GRN behind a Transformer
G1_RN
Consider PUN Station A below. There are two generators and two Points of Interconnection(POI).
PUN GRN, G1_RN, is adjacent to the POI at EPS meter, EPS_G1.
PUN GRN, G2_RN, is placed on the low side of its generator’s step up transformers.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
EPS_G1
EPS_G2
A_PUN1

## Slide 10: Example 1 – PUN GRN behind a Transformer
G1_RN
The power flow buses are split by lines and transformers.
~
PUN Station A
G1
~
G2
EPS_G1
G2_RN
ERCOT Equipment
PUN Equipment
Power Flow Buses
EPS_G2
A_PUN1

## Slide 11: Example 1 – PUN GRN behind a Transformer
Biddable
G1_RN
The power flow buses are split by lines and transformers.
In this example, G1_RN is biddable because it is in the same power flow bus as an EPS meter for the PUN site.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
EPS_G1
EPS_G2
A_PUN1

## Slide 12: Example 1 – PUN GRN behind a Transformer
Biddable
G1_RN
The power flow buses are split by lines and transformers.
In this example, G1_RN is biddable because it is in the same power flow bus as an EPS meter for the PUN site.
G2_RN is not biddable because there exists constrainable equipment between it and the EPS meters for the PUN site.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
Not Biddable
EPS_G1
EPS_G2
A_PUN1

## Slide 13: Example 1 – PUN GRN behind a Transformer
G1_RN
PUN Resource Nodes will always remain biddable.
~
PUN Station A
G1
~
G2
G2_RN
ERCOT Equipment
PUN Equipment
Not Biddable
EPS_G1
EPS_G2
Biddable
A_PUN1

## Slide 14: Example 2a – EPS Meter Outside PUN Station
EPS_G2
EPS_G1
G2_RN
G1_RN
Consider the example below where the POIs are outside PUN Station A.
~
PUN Station A
G1
~
G2
ERCOT Equipment
PUN Equipment
Station B

## Slide 15: Example 2a – EPS Meter Outside PUN Station
Consider the example below where the POIs are outside PUN Station A.
The PUN GRNs are outside the PUN station as well.
PUN Station A
ERCOT Equipment
PUN Equipment
Station B
G2_RN
G1_RN
EPS_G2
EPS_G1
~
G1
~
G2

## Slide 16: Example 2a – EPS Meter Outside PUN Station
Consider the example below where the POIs are outside PUN Station A.
The PUN GRNs are outside the PUN station as well.
The power flow buses are split by lines and transformers.
PUN Station A
ERCOT Equipment
PUN Equipment
Power Flow Buses
Station B
G2_RN
G1_RN
EPS_G2
EPS_G1
~
G1
~
G2

## Slide 17: Example 2a – EPS Meter Outside PUN Station
In this example, G1_RN and G2_RN are in the same power flow bus as an EPS meter for the PUN site.
PUN Station A
ERCOT Equipment
PUN Equipment
Station B
G2_RN
G1_RN
EPS_G2
EPS_G1
~
G1
~
G2

## Slide 18: Example 2a – EPS Meter Outside PUN Station
G2_RN
Biddable
In this example, G1_RN and G2_RN are in the same power flow bus as an EPS meter for the PUN site.
G1_RN and G2_RN are biddable.
PUN Station A
ERCOT Equipment
PUN Equipment
Station B
G1_RN
EPS_G2
EPS_G1
~
G1
~
G2

## Slide 19: Example 2b – EPS Meter Outside PUN Station
G2_RN
PUN Station A
G1_RN
Consider another example where the POI is outside PUN Station A.
ERCOT Equipment
PUN Equipment
Station B
A_PUN1
A_PUN2
EPS_G2
EPS_G1
~
G1
~
G2

## Slide 20: Example 2b – EPS Meter Outside PUN Station
G1_RN
G2_RN
Consider another example where the POI is outside PUN Station A.
This time the PUN GRNs are placed inside PUN Station A, and the PUN Resource nodes are placed at the POI.
ERCOT Equipment
PUN Equipment
Station B
PUN Station A
A_PUN1
A_PUN2
EPS_G2
EPS_G1
~
G1
~
G2

## Slide 21: Example 2b – EPS Meter Outside PUN Station
Consider another example where the POI is outside PUN Station A.
This time the PUN GRNs are placed inside PUN Station A, and the PUN Resource nodes are placed at the POI.
The power flow buses separated by lines and transformers.
ERCOT Equipment
PUN Equipment
Power Flow Buses
Station B
PUN Station A
G2_RN
G1_RN
A_PUN1
A_PUN2
EPS_G2
EPS_G1
~
G1
~
G2

## Slide 22: Example 2b – EPS Meter Outside PUN Station
The PUN GRNs are not in the same power flow bus as the EPS meters for this PUN site.
ERCOT Equipment
PUN Equipment
Station B
PUN Station A
G2_RN
G1_RN
A_PUN1
A_PUN2
EPS_G2
EPS_G1
~
G1
~
G2

## Slide 23: Example 2b – EPS Meter Outside PUN Station
The PUN GRNs are not in the same power flow bus as the EPS meters for this PUN site.
G1_RN and G2_RN are not biddable.
ERCOT Equipment
PUN Equipment
Station B
PUN Station A
G2_RN
G1_RN
A_PUN1
A_PUN2
EPS_G2
EPS_G1
~
G1
~
G2
Not Biddable

## Slide 24: Example 2b – EPS Meter Outside PUN Station
A_PUN1
Biddable
EPS_G2
EPS_G1
The PUN GRNs are not in the same power flow bus as the EPS meters for this PUN site.
G1_RN and G2_RN are not biddable.
The PUN Resource Nodes are biddable.
ERCOT Equipment
PUN Equipment
Station B
PUN Station A
Not Biddable
G2_RN
G1_RN
A_PUN2
~
G1
~
G2

## Slide 25: Process
OBDRR003 contains some redlines that would be implemented immediately and some greyboxed for SCR796 system implementation.
  In the interim between approval of OBDRR003 and implementation of SCR796, ERCOT will have the ability to secured PUN equipment in DAM “only when it is necessary for DAM to reach a solution.”
    Once SCR796 is implemented, that language will be replaced by language stating that ERCOT will not secure PUN equipment.
Request that WMS approve OBDRR003 once SCR796 is approved by the Board, since it contains greyboxed language that is implicitly dependent on that approval.