## Slide 1
Potential Options to Allow for the Use of Actual Data in the ERCOT Initial Settlement
RMS
May 8, 2018

## Slide 2: Intended Purpose of Discussion
The purpose of this discussion is to introduce some options that allow for the use of actual meter data while performing the initial settlement of an operating day. ERCOT has not consulted with any other MPs while developing these options and understands there may be more options that arise as a result of continued market discussion. These options were developed to provide a starting point for future discussions that are expected to take place as part of an RMS workshop/working group.

## Slide 3: Option 1 – TDSP Submits Daily 867_03 Data
System Impacts
Current TDSP process does not support daily reads
Would daily reads need to be flagged non-billing to allow a subsequent monthly billing file?
Would ERCOT need to replace the daily reads with the monthly billing data?

## Slide 4: Option 2 – Change IDR Meter Requirement to IDR Requirement
The basis of this proposal is to modify protocol language 18.6.1 in a manner that requires Interval Data Recorders (AMS or IDR Meters) for premises >700kW or transmission connected instead of requiring IDR Meters.
18.6 Installation and Use of Interval Data Recorders Meters
18.6.1 Interval Data Recorder Meter Mandatory Installation Requirements
(1) Interval Data Recorders (IDRs) Meters are required and shall be installed and utilized for Settlement of Premises having either:
(a) A peak Demand greater than 700 kW (or 700kVA in CenterPoint Energy’s service territory); or
(b) Service provided at transmission voltage (above 60 kV).

## Slide 5: Option 2 – System Impacts
System Changes Would Be Required for ERCOT & TDSPs
  ERCOT impact is small
    would need to change IDR Requirement reporting to only check NIDRs
Requires TDSP capability of applying 4CP demand billing to non-BUSIDRRQ premises
Allows for DG identification and negative load treatment if AMS meter type
REP System Impacts Unknown
  Do REPs use “BUSIDRRQ” to determine who is on 4CP demand billing?

## Slide 6: Option 3 – .lse File Submittal
Add new option for IDR Meter data submittal as .lse format
TDSP defines ERCOT Settlement data file submittal format for a premise with an IDR Meter based on their setting of the AMS Flag in ERCOT Systems
  If TDSP sets AMS Flag to “AMSR or AMSM”
    Data submittal for Settlements is .lse file format

## Slide 7: Option 3 - What Remains Intact
IDR Meter Definition
  An IDR where the ESI ID is required to be assigned a BUSIDRRQ Load Profile Type code and data is submitted in accordance with Section 10.3.3.3, Submission of Settlement Quality Meter Data to ERCOT.
Requirement of BUSIDRRQ Profile Type for an IDR Meter
Transaction used by the TDSP to set the AMS Flag in ERCOT Systems
Data extracts
  All IDR Meter data included in the IDR Supplemental Extract (ERCOT loads the data in the same location regardless of submittal format)
TDSP continues submitting monthly 867_03 files for all BUSIDRRQ Profiles
  ERCOT will only load the monthly 867_03s for the meters where the AMS flag is “NULL”

## Slide 8: Option 3 - Potential Protocol Language (1)
10.3.3.3 Submission of Settlement Quality Meter Data to ERCOT
(1) Settlement Quality Meter Data shall be submitted to ERCOT on a periodic cycle, but no later than monthly:
(a) For provisioned Advanced Meters, Settlement Quality Meter Data will be submitted using an ERCOT specified file format for the interval data only, which will be used for Settlement.
(i) The monthly non-interval total consumption and demand (if applicable) values for these ESI IDs shall be provided to ERCOT and Load Serving Entities (LSEs) using the appropriate Texas Standard Electronic Transactions (TX SETs) in order to:
(A) Effectuate the registration transactions outlined in Section 15, Customer Registration; and
(B) Determine if a Premise has become subject to the IDR Meter Mandatory Installation Requirements.
(ii) These non-interval total consumption and demand values will not be used for Settlement.

## Slide 9: Option 3 - Potential Protocol Language (2)
(b) For NIDRall other meters, Settlement Quality Meter Data will be submitted using the appropriate TX SET.
(c) For IDR Meters, Settlement Quality Meter Data will be submitted in one of the following methods:
(i) For locations with a BUSIDRRQ profile type where the TDSP has set the AMS Flag to “AMSR or AMSM” in the ERCOT registration system, Settlement Quality Meter Data must be provided in the ERCOT specified file format in accordance with Retail Market Guide Section 7.15, Advanced Meter Interval Data File Format and Submission, which will be used for Settlement. In addition, the TDSP shall send the appropriate TX SETs to effectuate the registration transactions outlined in Section 15, Customer Registration.
(ii) For locations with a BUSIDRRQ profile type where the TDSP has set the AMS Flag to “NULL” in the ERCOT registration system, Settlement Quality Meter Data will be submitted using the appropriate TX SETs.

## Slide 10: Option 3 – System Impacts
System Changes Would Be Required for ERCOT & TDSPs
REP System Impacts Unknown
  Will REPs consume daily IDR Meter data

## Slide 11: Option 4 – Do Any Combination of the Three Options
Provides a more robust solution than only doing one
If the combination includes option 3, would not require TDSP capability of applying 4CP demand billing to non-BUSIDRRQ premises