## Slide 1
Proposed Change to the Generic Maximum Shadow Price for Base Case Constraints
OBDRR005
David Maggio
Technical Advisory Committee
May 24th, 2018

## Slide 2: Introduction
ERCOT identified a concern with the current generic maximum shadow price for base case transmission constraints and discussed it with the Congestion Management Working Group (CMWG) and Wholesale Market Subcommittee (WMS).
At their May meeting, the WMS endorsed the concept that is reflected in Other Binding Document Revision Request (OBDRR) 005
  The proposed revision is to the Methodology for Setting Maximum Shadow Prices for Network and Power Balance Constraints.

## Slide 3: Generic Shadow Prices Caps for Transmission Constraints
The vast majority of shadow price caps for transmission constraints are driven by the generic values defined in section 3.5 of the methodology:
  Base Case Violation: $5,000/MWh
    Base Case violations include Generic Transmission Constraints (GTCs)
  N-1 Constraint Violation
    345 kV: $4,500/MWh
    138 kV: $3,500/MWh
    69 kV: $2,800/MWh
These values have been the same since Nodal go-live.

## Slide 4: Potential Concerns with the Panhandle GTC
The concern arose out of thinking about the Panhandle GTC and interactions with the System-Wide Offer Cap (SWCAP) of $9,000/MWh.
  The Panhandle GTC currently has a shadow price cap of $5,000/MWh.
If the Panhandle GTC needed to be managed in a case in which real-time energy prices outside the Panhandle rose to values above ~$5,000/MWh, economic dispatch would no longer be managing the constraint on its own.
  Exceeding the GTC’s limits could have a significant impact on the stability of the entire Panhandle region.
  The prices above $5,000/MWh could be for a short or long period.
  Manual actions would be needed to continue managing the constraint.
This same situation exists for all base case constraints, although the impact may not be the same.

## Slide 5: Panhandle Wind Curtailments for 2018
Chart: MWs of Panhandle Wind Curtailment for 1/1/18 - 4/18/18 Intervals in which the Panhandle GTC was Binding
| 0-100 | 100-200 | 200-300 | 300-400 | 400-500 | 500-600 | 600-700 | 700-800 | 800-900 | 900-1000 | 1000-1100 | 1100-1200
 | 64.5844 | 83.8592 | 94.4642 | 112.1694 | 123.2939 | 128.2833 | 121.6206 | 110.14 | 65.8928 | 49.8267 | 9.1914 | 0.91444
~964 total hours
This graph provides an indication of the amount of MWs of overloading on the Panhandle GTC that could occur in the scenario being described.

## Slide 6: Historical Intervals with Base Case Constraints at the Shadow Price Cap
It’s uncommon for base case constraints to be at the shadow price cap.
  Less that 40 hours total since Nodal Go-Live
We’ve not yet observed cases in which system lambda was above $5,000/MWh and a base constraint was active.

## Slide 7: Proposed Change and Next Steps
The proposed change is to make the generic value $9,251/MWh for all base case violations, as opposed to $5,000/MWh.
  The “251” in the value is intended to account for energy offer curves which may be as low as the system-wide offer floor.
The OBDRR includes minor changes to section 3.5 of the methodology, both the generic value itself and the associated analysis and examples.
ERCOT is asking the Technical Advisory Committee (TAC) to recommend the proposed revisions and pass along OBDRR005 to the Board.
Assuming approval of the OBDRR, the proposed implementation date is Operating Day June 20th, 2018.