## Slide 1
Analysis of Load Reductions Associated with 4-CP Transmission Charges and Price Responsive Load/Retail DR
Carl L Raish
Principal Load Profiling and Modeling
WMS – June 6, 2018

## Slide 2: Overview
  4CP Analysis
    Methodology Improvement
    Results in Competitive and NOIE Areas
  Price Response and Retail DR
    Block and Index Pricing (BI)
    Other Load Control (OLC)
    Other Voluntary DR (OTH)
    Peak Rebate (PR)
    Real Time Pricing (RTP)
    Time-of-Use Pricing (TOU)
      Analysis not available
    DG Price Response
  NOIE Price Response

## Slide 3: Methodology (in brief)
    Identify 4CP Days (stored in ERCOT Data)
    Identify Days with high price events (4 consecutive intervals >$200
      Track and take into consideration at ESID level
    Identify Near-CP days … significant load reduction on other than 4CP days
      Old method was to look at total load of competitive ESIIDs (~600) served at transmission voltage and identify summer days with 100 MW reduction
      New method to limit the look to transmission ESIIDs (~160) that actually reduced in the prior year
      Lowered detection threshold to 100 MW or 5%
      General outcome was to identify more Near-CP days
    Develop baselines for each ESIID … excluding high price days and other 4CP/Near CP days
    Using those baselines:
      Identify ESIIDs that respond frequently and significantly during 4CP/NearCP events for the three year period before, during and after the year being analyzed.
      Estimate 4CP/Near CP reductions for these ESIIDs

## Slide 4: Competitive 4 CP Days - 2017
CP Reduce = 1,205 MW
CP Reduce = 502 MW
CP Reduce = 1,082 MW
CP Reduce = 999 MW

## Slide 5: NOIE 4 CP Days - 2017
CP Reduce = 149 MW
CP Reduce = 186 MW
CP Reduce = 733 MW
CP Reduce = 283 MW

## Slide 6: Competitive + NOIE 4 CP Days - 2017
CP Reduce = 1,353 MW
CP Reduce = 689 MW
CP Reduce = 1,815 MW
CP Reduce = 1,282 MW

## Slide 7: 4CP and NearCP Hour Ending 17:00 Reductions
2015
2017
2016

## Slide 8: NOIE Hour Ending 17:00 Response
2015
2017
2016

## Slide 9: 2012 – 2017 Pricing Events
For this analysis a High Price Event has been defined as a day with a Load zone price > $200 for 4 consecutive 15-minute intervals
For the 2012 – 2017 years,194 days were identified with high price events in one or more load zones
  AEN – 66 days
  CPS – 58 days
  Houston – 73 days
  LCRA – 67 days
  North – 46 days
  Raybn – 49 days
  South – 89 days
  West – 116 days
119 days had high price events in only 1 load zone
40 days had high price events in all 8 load zones
13 of the 40 days with high price events in all 8 load zones occurred during a summer month (June – September)

## Slide 10: Number of Reporting REPs & Unique ESIIDs By Year
Individual REPs
2013 – 21
2014 – 33
2015 – 32
2016 – 35
2017 – 38
Related REPs (by DUNs) are
Combined into a single REP
REP Families
2013 – 19
2014 – 23
2015 – 25
2016 – 27
2017 – 29
Unique ESIIDs
2013 – 179,195
2014 – 763,445
2015 – 847,574
2016 – 906,646
2017 – 975,716

## Slide 11: Block and Index Participation
REPs
ESIIDs

## Slide 12: 2017 Block & Index Analysis
Houston
May 19, 2017
36.2 MW Reduce
21 Reps; 18,886 Bus customers; 193.9 MW; 19 event days
North
Oct 4, 2017
88.6 MW Reduce
South
April 3, 2017
35.8 MW Reduce
West
Dec 7, 2017
33.3 MW Reduce

## Slide 13: Other Load Control Participation
REPs
ESIIDs
Business
Residential

## Slide 14: 2017 OLC Analysis
2.2 MW Reduce
2 Reps reported 15 deployments in 2017 affecting 2,345 Res customers
One composite graph shown combining day with each REP’s largest reduction

## Slide 15: 2017 Other Voluntary DR Analysis
Aug 1, 2017
10.9 MW Reduce
3 Reps reported 23 deployments in 2017 affecting 56,276 customers
Program same description as 2016
Reductions ranged from 0 – 26.7 MW
Aug 2, 2017
26.7 MW Reduce
Aug 21, 2017
13.5 MW Reduce
Aug 17, 2017
9.4 MW Reduce

## Slide 16: Peak Rebate Participation
REPs
ESIIDs
Business
Residential

## Slide 17: 2017 Peak Rebate Analysis
2 Reps reported 3 deployments in 2017 affecting 39,942 customers
No days with deployments by both REPs
Composite Deployment 2017
13.4 MW Reduce

## Slide 18: Real Time Pricing Participation
REPs
ESIIDs
Business
Residential

## Slide 19: 2017 Real Time Pricing Analysis
Houston
May 19, 2017
8.4 MW Reduce
14 Reps; 14,769 customers; 24.5 MW; 19 event days
North
Oct 4, 2017
12.9 MW Reduce
South
May 19, 2017
1.2 MW Reduce
West
May 30, 2017
2.1 MW Reduce

## Slide 20: 2017 NOIE Price Response Analysis
10 NOIEs identified as responding to high prices; 257.1 MW; 17 event days
Composite Deployment 2017
257.1 MW Reduce

## Slide 21: 2017 DG Price Response Analysis
Houston
April 28, 2017
63.4 MW Increase
61 Registered and Unregistered DGs; 181.1 MW; 19 event days
Renewable fuel DG not included
North
Oct 4, 2017
3.2 MW Increase
South
Oct 9, 2017
61.7 MW Increase
West
May 30, 2017
52.8 MW Increase

## Slide 22: Demand/Price Response Totals

## Slide 23: Questions?
ON
OFF
craish@ercot.com 512/248-3876