## Slide 1: Settlement Corrections for Price Sensitive Loads
Demand Side Working Group
Floyd J. Trefny
June 15, 2018

## Slide 2: Background from April 20, 2018
Interval Data Recorders (IDR) meters measure retail load on 15-minute intervals
Load Zone Settlement Point Prices from ERCOT that retail consumers pay are based on 15-minute intervals.
  Calculated for each bus’s load weighted average of 5-minute bus LMPs from each SCED executed during the 15-minute period
  These 5-minute averages are further weighted by the change in system load over the 15 minute period
Retail Loads pay metered kWh multiplied by the 15-minute settlement point price
  Loads that have significant differences in demand during the 15 minute interval are not settled correctly
  Discourages demand response behavior

## Slide 3: Background from April 20, 2018
Generators are not settled the same way as load
  Protocol section 6.6.3.1, Real-Time Energy Imbalance Payment or Charge at a Resource Node, addressed a similar problem with generation settlements
  ERCOT uses Generation Base Points typically different every 5 minutes to adjust 15-minute energy data into 5 minute data for settlement purposes
Structure of Load settlement equations make it difficult to easily change calculations for individual loads
  Loads are summed up individually for each QSE by LZ and then pricing is applied to result in a charge to a QSE
Need a way to correct settlements of load for those consumers who desire such

## Slide 4: A Concept
Talked off line with ERCOT staff
Best approach may be to use method similar to that done for “wholesale storage load”
Require any load desiring this correction to have installed telemetry operating with scans every 2 seconds
  Telemetry would be sent to ERCOT via the TSP
  Load telemetry would also improve the visibility of these loads to ERCOT’s State Estimator

## Slide 5: A Concept (cont)
No changes to the current 15 minute settlement calculation for QSE’s load
ERCOT would integrate the load’s telemetry signal for power to produce 5 minute energy usage
  The 5 minute energy would be prorated to add up to the same total energy measured in the 15 minute interval
Each 5 minute energy would be multiplied by the load zone LMP from SCED for that interval and totaled for the 15 minute interval
The difference between the 15 minute settlement and the corrected 5 minute settlement would create a credit or charge and is added to the QSE’s settlement
Credit or charge would be applied to the ERCOT Balancing account (RENA)

## Slide 6: Next Steps
Verify with the PUC staff that such a correction is allowed under current rules
  Similar to that already approved for wholesale storage load
Validate that TSPs are willing to send load power data to ERCOT via telemetry
ERCOT to review the concept and make any recommendations to DSWG
Seek comments from other stakeholders