## Slide 1
Dispatch and Price for the Resource Disconnected by Contingency
Jian Chen
Market Analysis and Validation
QMWG
July 9th, 2018

## Slide 2: Resource Node and Resource
2
G
Station A
Station B
Station C
Station D
EPS Meter
RN for UNIT_G1
UNIT_G1

## Slide 3: Contingency Definition and Constraint
G
Station A
Station B
Station C
line contingency for LN A-B-2
Station D
Overloading LN A-B-1
Notes: Although here

## Slide 4: Contingency Definition and Constraint
G
Station A
Station B
Station C
line contingency for LN A-D
Station D
Overloading LN A-B-1

## Slide 5: Constraint Shift Factors and Downstream Applications
For the real-time market, shift factors are calculated from EMS and then transferred to MMS for resource dispatch and price calculations.
SCED Optimization
Resource SF
Resource Base Point,
Resource LMP (ICCP)
Electric Bus SF
System Lambda, Constraint Shadow Price
Post Process
RN Price, Meter Price
EMS RTCA

## Slide 6: Pick-up Effect for Generation Loss
Under a generation loss scenario, the shift factor of the disconnected resource is NOT exactly 0, due to the consideration of the “pick-up” effect.
The “pick-up” assumption is, in the case of a contingency involving generation loss, some of the other generators have to pick up the lost generation. Therefore, the MW carried by the disconnected resource will have some impact on the posting-contingency constraint.
The shift factor of Electrical Bus associated with Settlement Point or Meter, however, does not consider pick-up effect. The shift factor for any Electric Bus disconnected by contingency is set to 0.

## Slide 7: “Pick-up” Effect
G
Station A
Station B
Station C
Station D
Overloading LN A-B-1
SF for RN = 0
UNIT_G1
Gen | MWBC | PF | MWPC | SF
G1 | 20 | NA | 0 | 0.1
G2 | 50 | 0.25 | 55 | 0.2
G3 | 50 | 0.5 | 60 | 0.2
G4 | 50 | 0 | 50 | 0.1
G5 | 50 | 0.25 | 55 | -0.2
“Pick-up” SF for G1:
G
G
G
G2
G3
G4
G
G5

## Slide 8: Shift Factors and Price Calculation
The difference between resource SF(none-zero) and Electric Bus SF (zero) will lead to different Resource LMP and RN price.
SCED Optimization
Resource SF
Electric Bus SF
System Lambda, Constraint Shadow Price
Post Process
RN Price, Meter Price
EMS RTCA
Assuming positive SF after “pick-up” effect
Curtailment and lower Resource LMP due to positive resource SF
0
Higher RN and Meter price
Resource Base Point,
Resource LMP (ICCP)

## Slide 9: NPRR833 - Modify PTP Obligation Bid Clearing Change
The approved NPRR 833 will fix the modeling of PTPs in the DAM. With the NPRR, ERCOT will update the DAM optimization engine to address the situation where a contingency disconnects a Resource Node. The DAM Settlement Point Price will include that “pick-up” shift factor in the price calculation for the Resource Node.
As part of the NPRR 833 project, ERCOT will also update the Real-Time Market so that the RT Settlement Point Price for the Resource Node will also include the pick-up effect.
As currently being envisioned, the pick-up shift factor would not be applied to the real-time meter price under NPRR 833.
  This is due in at least part to the potential “many-to-many” relationship between resources and real-time meter prices.

## Slide 10: Other Factors related to Resource/RN LMP difference
When resource and RN are both dead in base case, the dead bus logic for off-line resources shift factor is looking for the next active node, and the Heuristic rule for RN LMP calculation is based on Protocol 6.6.1 (1)
The shift factor calculation for combine cycle logic resource is RT MW weighted, while the LMP calculation for combine cycle logic RN is HRL weighted
Constraint element could be located between the resource and the RN
Certain unit contingency could open the resource but not the RN