## Slide 1
Draft NPRR RT HUB LMP Calculation Change
July 9, 2018

## Slide 2: Introduction
This draft NPRR changes the Real-Time HUB LMP calculation to match the methodology used in DAM/CRR Auctions
  This is a follow-up to NPRR 868, As-Built Hub and Load Zone Calculation for DAM/CRR Auctions
    http://www.ercot.com/content/wcm/key_documents_lists/138531/07.__WMS_Feb_2018_DAM_Hub_Buses_v2.pptx
RT HUB LMP calculation will be based on Shift Factor Aggregation at Power Flow Buses instead of the current use of LMP at Electrical Buses
  Hub Bus Shift Factor calculation will give equal weightage to the Shift Factors of constituent Power Flow Buses
  Hub Bus LMP will be calculated based on the aggregated HUB Shift Factor and corresponding Transmission Constraint Shadow Prices and the Power Balance Penalty Shadow Price
Looking for stakeholder feedback on pursuing this NPRR

## Slide 3: Current HUB LMP Calculation: Real-Time vs DAM/CRR
LMP Aggregation
Shift Factor Aggregation
Real-Time HUB LMP Calculation
Day-Ahead HUB LMP Calculation (NPRR 868)
eb2
PF2
eb3
eb1
PF1
PF3
Hub
1/3
Hub Bus 3
1/3
Hub Bus 2
1/3
Hub Bus 1
1/3
2/3
0
eb2
PF2
eb3
eb1
PF1
PF3
Hub
1/3
Hub Bus 3
1/3
Hub Bus 2
1/3
Hub Bus 1
1/3
1/3
1/3

## Slide 4: Expected System Changes
NMMS: Automate process to designate all 345 KV nodes in a Hub Bus as Electrical Buses
EMS: Modify Electrical Bus Shift Factor data transfer to MMS to include Power Flow Bus information
MMS: Modify RT HUB LMP calculations as per new formula