| NPRR Number | DRAFT | NPRR Title | Change to the Calculation of Real-Time Hub Prices |
| --- | --- | --- | --- |
| Date Posted | TBD |
| Requested Resolution | Normal |
| Nodal Protocol Sections Requiring Revision | 2.1, Definitions 3.5.2.1, North 345 kV Hub (North 345) 3.5.2.2, South 345 kV Hub (South 345) 3.5.2.3, Houston 345 kV Hub (Houston 345) 3.5.2.4, West 345 kV Hub (West 345) 3.5.2.6, ERCOT Bus Average 345 kV Hub (ERCOT 345 Bus) 6.6.1.5, Hub LMPs |
| Related Documents Requiring Revision/Related Revision Requests | None |
| Revision Description | This Nodal Protocol Revision Request (NPRR) is submitted as a follow-up to NPRR868, As-Built Hub and Load Zone Calculation. Whereas NPRR868 modified definitions and price calculations for the Day-Ahead Market (DAM) and Congestion Revenue Right (CRR) Auctions to ensure alignment between system logic and Protocol language, this NPRR proposes to change both systems and language regarding the calculations of Hub price calculations for the Real-Time Market (RTM). To accommodate the calculations, a change to the definition of Electrical Bus is proposed which would require that all 345 KV nodes in a Hub Bus be designated as an Electrical Bus. |
| Reason for Revision | Addresses current operational issues. Meets Strategic goals (tied to the ERCOT Strategic Plan or directed by the ERCOT Board). Market efficiencies or enhancements Administrative Regulatory requirements Other: (explain) (please select all that apply) |
| Business Case | Implementation this NPRR will result in a consistent methodology for calculating Hub prices across the Real-Time Market, DAM, and CRR Auctions. |

| Sponsor |
| --- |
| Name | David Maggio |
| E-mail Address | David.Maggio@ercot.com |
| Company | ERCOT |
| Phone Number | 512-248-6998 |
| Cell Number | 773-458-3215 |
| Market Segment | N/A |

| Market Rules Staff Contact |
| --- |
| Name | Brittney Albracht |
| E-Mail Address | Brittney.Albracht@ercot.com |
| Phone Number | 512-225-7027 |

Proposed Protocol Language Revision

## DEFINITIONS

Electrical Bus

(1)	A physical transmission element defined in the Network Operations Model that connects, using breakers and switches, one or more:

(a)	Loads;

(b)	Lines;

(c)	Transformers;

(d)	Generators;

(e)	Capacitors;

(f)	Reactors;

(g)	Phase shifters; or

(h)	Other reactive control devices to the ERCOT Transmission Grid where there is negligible impedance between the connected Transmission Elements.

(2)	All Electrical Buses are designated by ERCOT and TSPs for modeling the electrical topology of the ERCOT Transmission Grid.

(3)	All 345 KV nodes in a Hub Bus shall be designated as an Electrical Bus.

Hub Bus

(1)	An energized power flow bus or group of energized power flow buses are defined as a single element in the Hub definition.  The Locational Marginal Price (LMP) of the Hub Bus is the simple average of the LMPs assigned to each energized power flow bus in the Hub Bus.  If all power flow buses within a Hub Bus are de-energized, the LMP of the Hub does not include the de-energized Hub Bus.  If power flow buses within a Hub Bus are de-energized under contingency, the disconnected MWs are redistributed among remaining energized power flow buses. This is used solely for calculating the prices of existing Hub Buses defined in Section 3.5.2, Hub Definitions;

3.5.2.1	North 345 kV Hub (North 345)

(1)	The North 345 kV Hub is composed of the following Hub Buses:

|  | ERCOT Operations |  |
| --- | --- | --- |
| No. | Hub Bus | kV | Hub |
| 1 | ANASW | 345 | NORTH |
| 2 | CN345 | 345 | NORTH |
| 3 | WLSH | 345 | NORTH |
| 4 | FMRVL | 345 | NORTH |
| 5 | LPCCS | 345 | NORTH |
| 6 | MNSES | 345 | NORTH |
| 7 | PRSSW | 345 | NORTH |
| 8 | SSPSW | 345 | NORTH |
| 9 | VLSES | 345 | NORTH |
| 10 | ALNSW | 345 | NORTH |
| 11 | ALLNC | 345 | NORTH |
| 12 | BNDVS | 345 | NORTH |
| 13 | BNBSW | 345 | NORTH |
| 14 | BBSES | 345 | NORTH |
| 15 | BOSQUESW | 345 | NORTH |
| 16 | CDHSW | 345 | NORTH |
| 17 | CNTRY | 345 | NORTH |
| 18 | CRLNW | 345 | NORTH |
| 19 | CMNSW | 345 | NORTH |
| 20 | CNRSW | 345 | NORTH |
| 21 | CRTLD | 345 | NORTH |
| 22 | DCSES | 345 | NORTH |
| 23 | EMSES | 345 | NORTH |
| 24 | ELKTN | 345 | NORTH |
| 25 | ELMOT | 345 | NORTH |
| 26 | EVRSW | 345 | NORTH |
| 27 | KWASS | 345 | NORTH |
| 28 | FGRSW | 345 | NORTH |
| 29 | FORSW | 345 | NORTH |
| 30 | FRNYPP | 345 | NORTH |
| 31 | GIBCRK | 345 | NORTH |
| 32 | HKBRY | 345 | NORTH |
| 33 | VLYRN | 345 | NORTH |
| 34 | JEWET | 345 | NORTH |
| 35 | KNEDL | 345 | NORTH |
| 36 | KLNSW | 345 | NORTH |
| 37 | LCSES | 345 | NORTH |
| 38 | LIGSW | 345 | NORTH |
| 39 | LEG | 345 | NORTH |
| 40 | LFKSW | 345 | NORTH |
| 41 | LWSSW | 345 | NORTH |
| 42 | MLSES | 345 | NORTH |
| 43 | MCCREE | 345 | NORTH |
| 44 | MDANP | 345 | NORTH |
| 45 | ENTPR | 345 | NORTH |
| 46 | NCDSE | 345 | NORTH |
| 47 | NORSW | 345 | NORTH |
| 48 | NUCOR | 345 | NORTH |
| 49 | PKRSW | 345 | NORTH |
| 50 | KMCHI | 345 | NORTH |
| 51 | PTENN | 345 | NORTH |
| 52 | RENSW | 345 | NORTH |
| 53 | RCHBR | 345 | NORTH |
| 54 | RNKSW | 345 | NORTH |
| 55 | RKCRK | 345 | NORTH |
| 56 | RYSSW | 345 | NORTH |
| 57 | SGVSW | 345 | NORTH |
| 58 | SHBSW | 345 | NORTH |
| 59 | SHRSW | 345 | NORTH |
| 60 | SCSES | 345 | NORTH |
| 61 | SYCRK | 345 | NORTH |
| 62 | THSES | 345 | NORTH |
| 63 | TMPSW | 345 | NORTH |
| 64 | TNP_ONE | 345 | NORTH |
| 65 | TRCNR | 345 | NORTH |
| 66 | TRSES | 345 | NORTH |
| 67 | TOKSW | 345 | NORTH |
| 68 | VENSW | 345 | NORTH |
| 69 | WLVEE | 345 | NORTH |
| 70 | W_DENT | 345 | NORTH |
| 71 | WTRML | 345 | NORTH |
| 72 | WCSWS | 345 | NORTH |
| 73 | WEBB | 345 | NORTH |
| 74 | WHTNY | 345 | NORTH |
| 75 | WCPP | 345 | NORTH |

(2)	The North 345 kV Hub Price uses the aggregated Shift Factors of the Hub Buses for each hour of the Settlement Interval of the Day-Ahead Market (DAM) in the Day-Ahead and is the simple average of the time-weighted Hub Bus prices for each 15-minute Settlement Interval in Real-Time, for each Hub Bus included in this Hub.

(3)	The Day-Ahead Settlement Point Price of the Hub for a given Operating Hour is calculated as follows:

DASPP North345 =	DASL – (DAHUBSF North345, c * DASP c),

if HBBC North345≠0

DASPP North345 =	DASPPERCOT345Bus, if HBBC North345=0

Where:

DAHUBSF North345, c	=	(HUBDF hb, North345, c * DAHBSF hb, North345, c)

DAHBSF hb, North345, c	=	(HBDF pb, hb, North345, c * DASF pb, hb, North345, c)

HUBDF hb, North345, c	=	IF(HB North345, c=0, 0, 1 / HB North345, c)

HBDF pb, hb, North345, c	=	IF(PB hb, North345, c=0, 0, 1 / PB hb, North345, c)

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| DASPP North345 | $/MWh | Day-Ahead Settlement Point Price(The DAM Settlement Point Price at the Hub, for the hour. |
| DASL | $/MWh | Day-Ahead System Lambda(The DAM Shadow Price for the system power balance constraint for the hour. |
| DASP c | $/MWh | Day-Ahead Shadow Price for a binding transmission constraint(The DAM Shadow Price for the constraint c for the hour. |
| DAHUBSF North345,c | none | Day-Ahead Shift Factor of the Hub (The DAM aggregated Shift Factor of a Hub for the constraint c for the hour. |
| DAHBSF hb,North345,c | none | Day-Ahead Shift Factor of the Hub Bus(The DAM aggregated Shift Factor of a Hub Bus hb for the constraint c for the hour. |
| DASF pb,hb,North345,c | none | Day-Ahead Shift Factor of the power flow bus(The DAM Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| HUBDF hb, North345,c | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the hour. |
| HBDF pb, hb, North345,c | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c. |
| PB hb, North345,c | none | The total number of energized power flow buses in Hub Bus hb for the constraint c. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c. |
| HBBC North345 | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case. |
| HB North345,c | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c. |
| c | none | A DAM binding transmission constraint for the hour caused by either base case or a contingency. |

(4)	The Real-Time Settlement Point Price of the Hub for a given 15-minute Settlement Interval is calculated as follows:

RTSPP North345	=	Max [-$251, (RTRSVPOR + RTRDP +

(RNWFy * HUBLMPNorth345,y))]

Where:

RTRSVPOR 		=	(RNWF  y * RTORPA y)

RTRDP                       =           (RNWFy  * RTORDPAy)

RNWF y		=	TLMP y / TLMP y

HUBLMPNorth345,y  =  RTSLy –(RTHUBSF North345, c,y * RTSPc,y),  if HBBC North345,y≠0

HUBLMPNorth345,y 	= 	HUBLMPERCOT345Bus,y, if HBBC North345,y=0

RTHUBSFNorth345,c,y	=	(HUBDF hb,North345,c,y * RTHBSF hb,North345,c,y)

RTHBSF hb,North345,c,y	=	(HBDF pb, hb,North345,c,y * RTSF pb, hb,North345 c,y)

HUBDF hb,North345,c,y	=	IF(HB North345,c,y=0, 0, 1 / HBNorth345,c,y)

HBDF pb, hb,North345,c,y	=	IF(PB hb, North345,c,y=0, 0, 1 / PB hb,North345,c,y)

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| RTSPP North345 | $/MWh | Real-Time Settlement Point Price(The Real-Time Settlement Point Price at the Hub, for the 15-minute Settlement Interval. |
| RTSL y | $/MWh | Real-Time System Lambda(The Real-Time Shadow Price for the system power balance constraint for the SCED interval y. |
| RTSP c, y | $/MWh | Real-Time Shadow Price for a binding transmission constraint(The Real-Time Shadow Price for the constraint c for the SCED interval y. |
| RTRSVPOR | $/MWh | Real-Time Reserve Price for On-Line Reserves(The Real-Time Reserve Price for On-Line Reserves for the 15-minute Settlement Interval. |
| RTORPA y | $/MWh | Real-Time On-Line Reserve Price Adder per interval(The Real-Time price adder for On-Line Reserves for the SCED interval y. |
| RTRDP | $/MWh | Real-Time On-Line Reliability Deployment Price(The Real-Time price for the 15-minute Settlement Interval, reflecting the impact of reliability deployments on energy prices that are calculated from the Real-Time On-Line Reliability Deployment Price Adder. |
| RTORDPA y | $/MWh | Real-Time On-Line Reliability Deployment Price Adder(The Real-Time price adder that captures the impact of reliability deployments on energy prices for the SCED interval y. |
| RNWF y | none | Resource Node Weighting Factor per interval(The weight used in the Resource Node Settlement Point Price calculation for the portion of the SCED interval y within the Settlement Interval. |
| TLMP y | second | Duration of SCED interval per interval(The duration of the portion of the SCED interval y within the 15-minute Settlement Interval |
| HUBLMPNorth345,y | $/MWh | Real-Time Hub Locational Marginal Price (The Real-Time Hub LMP for the Hub for the SCED interval y. |
| RTHUBSF North345,c,y | none | Real-Time Shift Factor of the Hub (The Real-Time aggregated Shift Factor of a Hub for the constraint c for the SCED interval y. |
| RTHBSF hb,North345,c,y | none | Real-Time Shift Factor of the Hub Bus(The Real-Time aggregated Shift Factor of a Hub Bus hb for the constraint c for the SCED interval y. |
| RTSF pb,hb,North345,c,y | none | Real-Time Shift Factor of the power flow bus(The Real-Time Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| HUBDF hb, North345,c,y | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the SCED interval y. |
| HBDF pb, hb, North345,c,y | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| y | none | A SCED interval in the 15-minute Settlement Interval. The summation is over the total number of SCED runs that cover the 15-minute Settlement Interval. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c for the SCED interval y. |
| PB hb, North345,c,y | none | The total number of energized power flow buses in Hub Bus hb for the constraint c for the SCED interval y. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c for the SCED interval y. |
| HBBC North345,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case for the SCED interval y. |
| HB North345,c,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c for the SCED interval y. |
| c | none | A Real-Time binding transmission constraint for the SCED interval y caused by either base case or a contingency. |

3.5.2.2	South 345 kV Hub (South 345)

(1)	The South 345 kV Hub is composed of the following Hub Buses:

|  | ERCOT Operations |  |
| --- | --- | --- |
| No. | Hub Bus | kV | Hub |
| 1 | AUSTRO | 345 | SOUTH |
| 2 | BLESSING | 345 | SOUTH |
| 3 | CAGNON | 345 | SOUTH |
| 4 | COLETO | 345 | SOUTH |
| 5 | CLEASP | 345 | SOUTH |
| 6 | NEDIN | 345 | SOUTH |
| 7 | FAYETT | 345 | SOUTH |
| 8 | FPPYD1 | 345 | SOUTH |
| 9 | FPPYD2 | 345 | SOUTH |
| 10 | GARFIE | 345 | SOUTH |
| 11 | GUADG | 345 | SOUTH |
| 12 | HAYSEN | 345 | SOUTH |
| 13 | HILLCTRY | 345 | SOUTH |
| 14 | HOLMAN | 345 | SOUTH |
| 15 | KENDAL | 345 | SOUTH |
| 16 | LA_PALMA | 345 | SOUTH |
| 17 | LON_HILL | 345 | SOUTH |
| 18 | LOSTPI | 345 | SOUTH |
| 19 | LYTTON_S | 345 | SOUTH |
| 20 | MARION | 345 | SOUTH |
| 21 | PAWNEE | 345 | SOUTH |
| 22 | RIOHONDO | 345 | SOUTH |
| 23 | RIONOG | 345 | SOUTH |
| 24 | SALEM | 345 | SOUTH |
| 25 | SANMIGL | 345 | SOUTH |
| 26 | SKYLINE | 345 | SOUTH |
| 27 | STP | 345 | SOUTH |
| 28 | CALAVERS | 345 | SOUTH |
| 29 | BRAUNIG | 345 | SOUTH |
| 30 | WHITE_PT | 345 | SOUTH |
| 31 | ZORN | 345 | SOUTH |

(2)	The South 345 kV Hub Price uses the aggregated Shift Factors of the Hub Buses for each hour of the Settlement Interval of the DAM in the Day-Ahead and is the simple average of the time-weighted Hub Bus prices for each 15-minute Settlement Interval in Real-Time, for each Hub Bus included in this Hub.

(3)	The Day-Ahead Settlement Point Price of the Hub for a given Operating Hour is calculated as follows:

DASPP South345 =	DASL – (DAHUBSF South345, c * DASP c),

if HBBC South345≠0

DASPP South345 =		DASPPERCOT345Bus, if HBBC South345=0

Where:

DAHUBSF South345, c	=	(HUBDF hb, South345, c * DAHBSF hb, South345, c)

DAHBSF hb, South345, c	=	(HBDF pb, hb, South345, c * DASF pb, hb, South345, c)

HUBDF hb, South345, c	=	IF(HB South345, c=0, 0, 1 / HB South345, c)

HBDF pb, hb, South345, c	=	IF(PB hb, South345, c=0, 0, 1 / PB hb, South345, c)

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| DASPP South345 | $/MWh | Day-Ahead Settlement Point Price(The DAM Settlement Point Price at the Hub, for the hour. |
| DASL | $/MWh | Day-Ahead System Lambda(The DAM Shadow Price for the system power balance constraint for the hour. |
| DASP c | $/MWh | Day-Ahead Shadow Price for a binding transmission constraint(The DAM Shadow Price for the constraint c for the hour. |
| DAHUBSF South345,c | none | Day-Ahead Shift Factor of the Hub (The DAM aggregated Shift Factor of a Hub for the constraint c for the hour. |
| DAHBSF hb,South345,c | none | Day-Ahead Shift Factor of the Hub Bus(The DAM aggregated Shift Factor of a Hub Bus hb for the constraint c for the hour. |
| DASF pb,hb,South345,c | none | Day-Ahead Shift Factor of the power flow bus(The DAM Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| HUBDF hb, South345,c | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the hour. |
| HBDF pb, hb, South345,c | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c. |
| PB hb, South345,c | none | The total number of energized power flow buses in Hub Bus hb for the constraint c. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c. |
| HBBC South345 | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case. |
| HB South345,c | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c. |
| c | none | A DAM binding transmission constraint for the hour caused by either base case or a contingency. |

(4)	The Real-Time Settlement Point Price of the Hub for a given 15-minute Settlement Interval is calculated as follows:

RTSPP South345	=	Max [-$251, (RTRSVPOR + RTRDP +

(RNWFy * HUBLMPSouth345,y))]

Where:

RTRSVPOR 		=	(RNWF  y * RTORPA y)

RTRDP                                =              ( RNWFy  * RTORDPAy)

RNWF y		=	TLMP y / TLMP y

HUBLMPSouth345,y  =  RTSLy –(RTHUBSF South345, c,y * RTSPc,y),  if HBBC South345,y≠0

HUBLMP South345,y 	= 	HUBLMPERCOT345Bus,y, if HBBC South345,y=0

RTHUBSF South345,c,y	=	(HUBDF hb, South345,c,y * RTHBSF hb, South345,c,y)

RTHBSF hb, South345,c,y	=	(HBDF pb, hb, South345,c,y * RTSF pb, hb, South345 c,y)

HUBDF hb, South345,c,y	=	IF(HB South345,c,y=0, 0, 1 / HB South345,c,y)

HBDF pb, hb, South345,c,y	=	IF(PB hb, South345,c,y=0, 0, 1 / PB hb, South345,c,y)

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| RTSPP South345 | $/MWh | Real-Time Settlement Point Price(The Real-Time Settlement Point Price at the Hub, for the 15-minute Settlement Interval. |
| RTSL y | $/MWh | Real-Time System Lambda(The Real-Time Shadow Price for the system power balance constraint for the SCED interval y. |
| RTSP c, y | $/MWh | Real-Time Shadow Price for a binding transmission constraint(The Real-Time Shadow Price for the constraint c for the SCED interval y. |
| RTRSVPOR | $/MWh | Real-Time Reserve Price for On-Line Reserves(The Real-Time Reserve Price for On-Line Reserves for the 15-minute Settlement Interval. |
| RTORPA y | $/MWh | Real-Time On-Line Reserve Price Adder per interval(The Real-Time On-Line Reserve Price Adder for the SCED interval y. |
| RTRDP | $/MWh | Real-Time On-Line Reliability Deployment Price-(The Real-Time price for the 15-minute Settlement Interval, reflecting the impact of reliability deployments on energy prices that are calculated from the Real-Time On-Line Reliability Deployment Price Adder. |
| RTORDPA y | $/MWh | Real-Time On-Line Reliability Deployment Price Adder –The Real-Time price adder that captures the impact of reliability deployments on energy prices for the SCED interval y. |
| RNWF y | none | Resource Node Weighting Factor per interval(The weight used in the Resource Node Settlement Point Price calculation for the portion of the SCED interval y within the Settlement Interval. |
| TLMP y | second | Duration of SCED interval per interval(The duration of the portion of the SCED interval y within the 15-minute Settlement Interval. |
| HUBLMPSouth345,y | $/MWh | Real-Time Hub Locational Marginal Price (The Real-Time Hub LMP for the Hub for the SCED interval y. |
| RTHUBSF South345,c,y | none | Real-Time Shift Factor of the Hub (The Real-Time aggregated Shift Factor of a Hub for the constraint c for the SCED interval y. |
| RTHBSF hb,South345,c,y | none | Real-Time Shift Factor of the Hub Bus(The Real-Time aggregated Shift Factor of a Hub Bus hb for the constraint c for the SCED interval y. |
| RTSF pb,hb,South345,c,y | none | Real-Time Shift Factor of the power flow bus(The Real-Time Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| HUBDF hb, South345,c,y | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the SCED interval y. |
| HBDF pb, hb, South345,c,y | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| y | none | A SCED interval in the 15-minute Settlement Interval. The summation is over the total number of SCED runs that cover the 15-minute Settlement Interval. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c for the SCED interval y. |
| PB hb, South345 | none | The total number of energized power flow busesin Hub Bus hb for the constraint c for the SCED interval y. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c for the SCED interval y. |
| HBBCSouth345,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case for the SCED interval y. |
| HB South345,c,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c for the SCED interval y. |
| c | none | A Real-Time binding transmission constraint for the SCED interval y caused by either base case or a contingency. |

3.5.2.3	Houston 345 kV Hub (Houston 345)

(1)	The Houston 345 kV Hub is composed of the following listed Hub Buses:

|  | ERCOT Operations |  |
| --- | --- | --- |
| No. | Hub Bus | kV | Hub |
| 1 | ADK | 345 | HOUSTON |
| 2 | _BI | 345 | HOUSTON |
| 3 | CBY | 345 | HOUSTON |
| 4 | CTR | 345 | HOUSTON |
| 5 | CHB | 345 | HOUSTON |
| 6 | DPW | 345 | HOUSTON |
| 7 | DOW | 345 | HOUSTON |
| 8 | RNS | 345 | HOUSTON |
| 9 | GBY | 345 | HOUSTON |
| 10 | _JN | 345 | HOUSTON |
| 11 | _KG | 345 | HOUSTON |
| 12 | KDL | 345 | HOUSTON |
| 13 | _NB | 345 | HOUSTON |
| 14 | _OB | 345 | HOUSTON |
| 15 | PHR | 345 | HOUSTON |
| 16 | SDN | 345 | HOUSTON |
| 17 | SMITHERS | 345 | HOUSTON |
| 18 | THW | 345 | HOUSTON |
| 19 | WAP | 345 | HOUSTON |
| 20 | _WO | 345 | HOUSTON |

(2)	The Houston 345 kV Hub Price uses the aggregated Shift Factors of the Hub Buses for each hour of the Settlement Interval of the DAM in the Day-Ahead and is the simple average of the time-weighted Hub Bus prices for each 15-minute Settlement Interval in Real-Time, for each Hub Bus included in this Hub.

(3)	The Day-Ahead Settlement Point Price of the Hub for a given Operating Hour is calculated as follows:

DASPP Houston345 =	DASL – (DAHUBSF Houston345, c * DASP c),

if HBBC Houston345≠0

DASPP Houston345 =	DASPPERCOT345Bus, if HBBC Houston345=0

Where:

DAHUBSF Houston345, c	=	(HUBDF hb, Houston345, c * DAHBSF hb, Houston345, c)

DAHBSF hb, Houston345, c	=	(HBDF pb, hb, Houston345, c * DASF pb, hb, Houston345, c)

HUBDF hb, Houston345, c	=	IF(HB Houston345, c=0, 0, 1 / HB Houston345, c)

HBDF pb, hb, Houston345, c	=	IF(PB hb, Houston345, c=0, 0, 1 / PB hb, Houston345, c)

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| DASPP Houston345 | $/MWh | Day-Ahead Settlement Point Price(The DAM Settlement Point Price at the Hub, for the hour. |
| DASL | $/MWh | Day-Ahead System Lambda(The DAM Shadow Price for the system power balance constraint for the hour. |
| DASP c | $/MWh | Day-Ahead Shadow Price for a binding transmission constraint(The DAM Shadow Price for the constraint c for the hour. |
| DAHUBSF Houston345,c | none | Day-Ahead Shift Factor of the Hub (The DAM aggregated Shift Factor of a Hub for the constraint c for the hour. |
| DAHBSF hb,Houston345,c | none | Day-Ahead Shift Factor of the Hub Bus(The DAM aggregated Shift Factor of a Hub Bus hb for the constraint c for the hour. |
| DASF pb,hb,Houston345,c | none | Day-Ahead Shift Factor of the power flow bus(The DAM Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| HUBDF hb, Houston345,c | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the hour. |
| HBDF pb, hb, Houston345,c | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c. |
| PB hb, Houston345,c | none | The total number of energized power flow buses in Hub Bus hb for the constraint c. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c. |
| HBBC Houston345 | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case. |
| HB Houston345,c | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c. |
| c | none | A DAM binding transmission constraint for the hour caused by either base case or a contingency. |

(4)	The Real-Time Settlement Point Price of the Hub for a given 15-minute Settlement Interval is calculated as follows:

RTSPP Houston345	   =	Max [-$251, (RTRSVPOR + RTRDP +

(RNWFy * HUBLMPHouston345,y))]

Where:

RTRSVPOR 		=	(RNWF  y * RTORPA y)

RTRDP                       		=           (RNWFy  * RTORDPAy)

RNWF y		=	TLMP y / TLMP y

HUBLMPHouston345,y  =  RTSLy –(RTHUBSF Houston345, c,y * RTSPc,y),  if HBBC Houston345,y≠0

HUBLMP Houston345,y 	= 	HUBLMPERCOT345Bus,y, if HBBC Houston345,y=0

RTHUBSF Houston345,c,y	=	(HUBDF hb, Houston345,c,y * RTHBSF hb, Houston345,c,y)

RTHBSF hb, Houston345,c,y	=	(HBDF pb, hb, Houston345,c,y * RTSF pb, hb, Houston345 c,y)

HUBDF hb, Houston345,c,y	=	IF(HB Houston345,c,y=0, 0, 1 / HB Houston345,c,y)

HBDF pb, hb, Houston345,c,y	=	IF(PB hb, Houston345,c,y=0, 0, 1 / PB hb, Houston345,c,y)

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| RTSPP Houston345 | $/MWh | Real-Time Settlement Point Price(The Real-Time Settlement Point Price at the Hub, for the 15-minute Settlement Interval. |
| RTSL y | $/MWh | Real-Time System Lambda(The Real-Time Shadow Price for the system power balance constraint for the SCED interval y. |
| RTSP c, y | $/MWh | Real-Time Shadow Price for a binding transmission constraint(The Real-Time Shadow Price for the constraint c for the SCED interval y. |
| RTRSVPOR | $/MWh | Real-Time Reserve Price for On-Line Reserves(The Real-Time Reserve Price for On-Line Reserves for the 15-minute Settlement Interval. |
| RTORPA y | $/MWh | Real-Time On-Line Reserve Price Adder per interval(The Real-Time On-Line Reserve Price Adder for the SCED interval y. |
| RTRDP | $/MWh | Real-Time On-Line Reliability Deployment Price(The Real-Time price for the 15-minute Settlement Interval, reflecting the impact of reliability deployments on energy prices that are calculated from the Real-Time On-Line Reliability Deployment Price Adder. |
| RTORDPA y | $/MWh | Real-Time On-Line Reliability Deployment Price Adder(The Real-Time price adder that captures the impact of reliability deployments on energy prices for the SCED interval y. |
| RNWF y | none | Resource Node Weighting Factor per interval(The weight used in the Resource Node Settlement Point Price calculation for the portion of the SCED interval y within the Settlement Interval. |
| TLMP y | second | Duration of SCED interval per interval(The duration of the portion of the SCED interval y within the 15-minute Settlement Interval |
| HUBLMPHouston345,y | $/MWh | Real-Time Hub Locational Marginal Price (The Real-Time Hub LMP for the Hub for the SCED interval y. |
| RTHUBSF Houston345,c,y | none | Real-Time Shift Factor of the Hub (The Real-Time aggregated Shift Factor of a Hub for the constraint c for the SCED interval y. |
| RTHBSF hb,Houston345,c,y | none | Real-Time Shift Factor of the Hub Bus(The Real-Time aggregated Shift Factor of a Hub Bus hb for the constraint c for the SCED interval y. |
| RTSF pb,hb,Houston345,c,y | none | Real-Time Shift Factor of the power flow bus(The Real-Time Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| HUBDF hb, Houston345,c,y | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the SCED interval y. |
| HBDF pb, hb, Houston345,c,y | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| y | none | A SCED interval in the 15-minute Settlement Interval. The summation is over the total number of SCED runs that cover the 15-minute Settlement Interval. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c for the SCED interval y. |
| PB hb, Houston345,c,y | none | The total number of energized power flow buses in Hub Bus hb for the constraint c for the SCED interval y. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c for the SCED interval y. |
| HBBC Houston345,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case for the SCED interval y. |
| HB Houston345,c,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c for the SCED interval y. |
| c | none | A Real-Time binding transmission constraint for the SCED interval y caused by either base case or a contingency. |

3.5.2.4	West 345 kV Hub (West 345)

(1)	The West 345 kV Hub is composed of the following listed Hub Buses:

|  | ERCOT Operations |  |
| --- | --- | --- |
| No. | Hub Bus | kV | Hub |
| 1 | ABMB | 345 | WEST |
| 2 | BOMSW | 345 | WEST |
| 3 | OECCS | 345 | WEST |
| 4 | BTRCK | 345 | WEST |
| 5 | FSHSW | 345 | WEST |
| 6 | FLCNS | 345 | WEST |
| 7 | GRSES | 345 | WEST |
| 8 | JCKSW | 345 | WEST |
| 9 | MDLNE | 345 | WEST |
| 10 | MOSSW | 345 | WEST |
| 11 | MGSES | 345 | WEST |
| 12 | DCTM | 345 | WEST |
| 13 | ODEHV | 345 | WEST |
| 14 | OKLA | 345 | WEST |
| 15 | SARC | 345 | WEST |
| 16 | SWESW | 345 | WEST |
| 17 | TWINBUTE | 345 | WEST |

(2)	The West 345 kV Hub Price uses the aggregated Shift Factors of the Hub Buses for each hour of the Settlement Interval of the DAM in the Day-Ahead and is the simple average of the time weighted Hub Bus prices for each 15-minute Settlement Interval in Real-Time, for each Hub Bus included in this Hub.

(3)	The Day-Ahead Settlement Point Price of the Hub for a given Operating Hour is calculated as follows:

DASPP West345 =		DASL – (DAHUBSF West345, c * DASP c),

if HBBC West345≠0

DASPP West345 =		DASPPERCOT345Bus, if HBBC West345=0

Where:

DAHUBSF West345, c	=	(HUBDF hb, West345, c * DAHBSF hb, West345, c)

DAHBSF hb, West345, c	=	(HBDF pb, hb, West345, c * DASF pb, hb, West345, c)

HUBDF hb, West345, c	=	IF(HB West345, c=0, 0, 1 / HB West345, c)

HBDF pb, hb, West345, c	=	IF(PB hb, West345, c=0, 0, 1 / PB hb, West345, c)

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| DASPP West345 | $/MWh | Day-Ahead Settlement Point Price(The DAM Settlement Point Price at the Hub, for the hour. |
| DASL | $/MWh | Day-Ahead System Lambda(The DAM Shadow Price for the system power balance constraint for the hour. |
| DASP c | $/MWh | Day-Ahead Shadow Price for a binding transmission constraint(The DAM Shadow Price for the constraint c for the hour. |
| DAHUBSF West345,c | none | Day-Ahead Shift Factor of the Hub (The DAM aggregated Shift Factor of a Hub for the constraint c for the hour. |
| DAHBSF hb,West345,c | none | Day-Ahead Shift Factor of the Hub Bus(The DAM aggregated Shift Factor of a Hub Bus hb for the constraint c for the hour. |
| DASF pb,hb,West345,c | none | Day-Ahead Shift Factor of the power flow bus(The DAM Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| HUBDF hb, West345,c | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the hour. |
| HBDF pb, hb, West345,c | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c. |
| PB hb, West345,c | none | The total number of energized power flow buses in Hub Bus hb for the constraint c. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c. |
| HBBC West345 | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case. |
| HB West345,c | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c. |
| C | none | A DAM binding transmission constraint for the hour caused by either base case or a contingency. |

(4)	The Real-Time Settlement Point Price of the Hub for a given 15-minute Settlement Interval is calculated as follows:

RTSPP West345	=	Max [-$251, (RTRSVPOR + RTRDP +

(RNWFy * HUBLMPWest345,y))]

Where:

RTRSVPOR 		=	(RNWF  y * RTORPA y)

RTRDP                      		=           (RNWFy  * RTORDPAy)

RNWF y		=	TLMP y / TLMP y

HUBLMPWest345,y  =  RTSLy –(RTHUBSF West345, c,y * RTSPc,y),  if HBBC West345,y≠0

HUBLMP West345,y 	= 	HUBLMPERCOT345Bus,y, if HBBC West345,y=0

RTHUBSF West345,c,y	=	(HUBDF hb, West345,c,y * RTHBSF hb, West345,c,y)

RTHBSF hb, West345,c,y	=	(HBDF pb, hb, West345,c,y * RTSF pb, hb, West345 c,y)

HUBDF hb, West345,c,y	=	IF(HB West345,c,y=0, 0, 1 / HB West345,c,y)

HBDF pb, hb, West345,c,y	=	IF(PB hb, West345,c,y=0, 0, 1 / PB hb, West345,c,y)

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| RTSPP West345 | $/MWh | Real-Time Settlement Point Price(The Real-Time Settlement Point Price at the Hub, for the 15-minute Settlement Interval. |
| RTRSVPOR | $/MWh | Real-Time Reserve Price for On-Line Reserves(The Real-Time Reserve Price for On-Line Reserves for the 15-minute Settlement Interval. |
| RTORPA y | $/MWh | Real-Time On-Line Reserve Price Adder per interval(The Real-Time On-Line Reserve Price Adder for the SCED interval y. |
| RTRDP | $/MWh | Real-Time On-Line Reliability Deployment Price(The Real-Time price for the 15-minute Settlement Interval, reflecting the impact of reliability deployments on energy prices that are calculated from the Real-Time On-Line Reliability Deployment Price Adder. |
| RTORDPA y | $/MWh | Real-Time On-Line Reliability Deployment Price Adder(The Real-Time price adder that captures the impact of reliability deployments on energy prices for the SCED interval y. |
| RNWF y | none | Resource Node Weighting Factor per interval(The weight used in the Resource Node Settlement Point Price calculation for the portion of the SCED interval y within the Settlement Interval. |
| RTSL y | $/MWh | Real-Time System Lambda(The Real-Time Shadow Price for the system power balance constraint for the SCED interval y. |
| RTSP c, y | $/MWh | Real-Time Shadow Price for a binding transmission constraint(The Real-Time Shadow Price for the constraint c for the SCED interval y. |
| TLMP y | second | Duration of SCED interval per interval(The duration of the portion of the SCED interval y within the 15-minute Settlement Interval. |
| HUBLMPWest345,y | $/MWh | Real-Time Hub Locational Marginal Price (The Real-Time Hub LMP for the Hub for the SCED interval y. |
| RTHUBSF West345,c,y | none | Real-Time Shift Factor of the Hub (The Real-Time aggregated Shift Factor of a Hub for the constraint c for the SCED interval y. |
| RTHBSF hb,West345,c,y | none | Real-Time Shift Factor of the Hub Bus(The Real-Time aggregated Shift Factor of a Hub Bus hb for the constraint c for the SCED interval y. |
| RTSF pb,hb,West345,c,y | none | Real-Time Shift Factor of the power flow bus(The Real-Time Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| HUBDF hb, West345,c,y | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the SCED interval y. |
| HBDF pb, hb, West345,c,y | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| y | none | A SCED interval in the 15-minute Settlement Interval. The summation is over the total number of SCED runs that cover the 15-minute Settlement Interval. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c for the SCED interval y. |
| PB hb, West345 | none | The total number of energized power flow buses in Hub Bus hb for the constraint c for the SCED interval y. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c for the SCED interval y. |
| HBBC West345,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case for the SCED interval y. |
| HB West345,c,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c for the SCED interval y. |
| c | none | A Real-Time binding transmission constraint for the SCED interval y caused by either base case or a contingency. |

[NPRR817: Insert Section 3.5.2.5 below upon system implementation and renumber accordingly:] 3.5.2.5 Panhandle 345 kV Hub (Pan 345) (1) The Panhandle 345 kV Hub is composed of the following listed Hub Buses: ERCOT Operations No. Hub Bus kV Hub 1 ABERNATH 345 PAN 2 AJ_SWOPE 345 PAN 3 ALIBATES 345 PAN 4 CTT_CROS 345 PAN 5 CTT_GRAY 345 PAN 6 OGALLALA 345 PAN 7 RAILHEAD 345 PAN 8 TESLA 345 PAN 9 TULECNYN 345 PAN 10 W_CW_345 345 PAN 11 WHIT_RVR 345 PAN 12 WINDMILL 345 PAN (2) The Panhandle 345 kV Hub Price uses the aggregated Shift Factors of the Hub Buses for each hour of the Settlement Interval of the DAM in the Day-Ahead and is the simple average of the time weighted Hub Bus prices for each 15-minute Settlement Interval in Real-Time, for each Hub Bus included in this Hub. (3) The Day-Ahead Settlement Point Price of the Hub for a given Operating Hour is calculated as follows: DASPP Pan345 = DASL – (DAHUBSF Pan345, c * DASP c), if HBBC Pan345≠0 DASPP Pan345 = DASPPERCOT345Bus, if HBBC Pan345=0 Where: DAHUBSF Pan345, c = (HUBDF hb, Pan345, c * DAHBSF hb, Pan345, c) DAHBSF hb, Pan345, c = (HBDF pb, hb, Pan345, c * DASF pb, hb, Pan345, c) HUBDF hb, Pan345, c = IF(HB Pan345, c=0, 0, 1 / HB Pan345, c) HBDF pb, hb, Pan345, c = IF(PB hb, Pan345, c=0, 0, 1 / PB hb, Pan345, c) The above variables are defined as follows: Variable Unit Definition DASPP Pan345 $/MWh Day-Ahead Settlement Point Price(The DAM Settlement Point Price at the Hub, for the hour. DASL $/MWh Day-Ahead System Lambda(The DAM Shadow Price for the system power balance constraint for the hour. DASP c $/MWh Day-Ahead Shadow Price for a binding transmission constraint(The DAM Shadow Price for the constraint c for the hour. DAHUBSF Pan345,c none Day-Ahead Shift Factor of the Hub (The DAM aggregated Shift Factor of a Hub for the constraint c for the hour. DAHBSF hb,Pan345,c none Day-Ahead Shift Factor of the Hub Bus(The DAM aggregated Shift Factor of a Hub Bus hb for the constraint c for the hour. DASF pb,hb,Pan345,c none Day-Ahead Shift Factor of the power flow bus(The DAM Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. HUBDF hb, Pan345,c none Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the hour. HBDF pb, hb, Pan345,c none Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. pb none An energized power flow bus that is a component of a Hub Bus for the constraint c. PB hb, Pan345,c none The total number of energized power flow buses in Hub Bus hb for the constraint c. hb none A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c. HBBC Pan345 none The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case. HB Pan345,c none The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c. c none A DAM binding transmission constraint for the hour caused by either base case or a contingency. (4) The Real-Time Settlement Point Price of the Hub for a given 15-minute Settlement Interval is calculated as follows: RTSPP Pan345 = Max [-$251, (RTRSVPOR + RTRDP + (RNWFy * HUBLMPPan345,y))] Where: RTRSVPOR = (RNWF y * RTORPA y) RTRDP = (RNWF y * RTORDPA y) RNWF y = TLMP y / TLMP y HUBLMPPan345,y = RTSLy –(RTHUBSF Pan345, c,y * RTSPc,y), if HBBC Pan345,y≠0 HUBLMP Pan345,y = HUBLMPERCOT345Bus,y, if HBBC Pan345,y=0 RTHUBSF Pan345,c,y = (HUBDF hb, Pan345,c,y * RTHBSF hb, Pan345,c,y) RTHBSF hb, Pan345,c,y = (HBDF pb, hb, Pan345,c,y * RTSF pb, hb, Pan345 c,y) HUBDF hb, Pan345,c,y = IF(HB Pan345,c,y=0, 0, 1 / HB Pan345,c,y) HBDF pb, hb, Pan345,c,y = IF(PB hb, Pan345,c,y=0, 0, 1 / PB hb, Pan345,c,y)The above variables are defined as follows: Variable Unit Description RTSPP Pan345 $/MWh Real-Time Settlement Point Price(The Real-Time Settlement Point Price at the Hub for the 15-minute Settlement Interval. RTRSVPOR $/MWh Real-Time Reserve Price for On-Line Reserves(The Real-Time Reserve Price for On-Line Reserves for the 15-minute Settlement Interval. RTORPA y $/MWh Real-Time On-Line Reserve Price Adder per interval(The Real-Time On-Line Reserve Price Adder for the SCED interval y. RTRDP $/MWh Real-Time On-Line Reliability Deployment Price(The Real-Time price for the 15-minute Settlement Interval, reflecting the impact of reliability deployments on energy prices that are calculated from the Real-Time On-Line Reliability Deployment Price Adder. RTORDPA y $/MWh Real-Time On-Line Reliability Deployment Price Adder(The Real-Time price adder that captures the impact of reliability deployments on energy prices for the SCED interval y. RNWF y none Resource Node Weighting Factor per interval(The weight used in the Resource Node Settlement Point Price calculation for the portion of the SCED interval y within the Settlement Interval. RTSL y $/MWh Real-Time System Lambda(The Real-Time Shadow Price for the system power balance constraint for the SCED interval y. RTSP c, y $/MWh Real-Time Shadow Price for a binding transmission constraint(The Real-Time Shadow Price for the constraint c for the SCED interval y. TLMP y second Duration of SCED interval per interval(The duration of the portion of the SCED interval y within the 15-minute Settlement Interval. HUBLMPPan345,y $/MWh Real-Time Hub Locational Marginal Price (The Real-Time Hub LMP for the Hub for the SCED interval y. RTHUBSF Pan345,c,y none Real-Time Shift Factor of the Hub (The Real-Time aggregated Shift Factor of a Hub for the constraint c for the SCED interval y. RTHBSF hb,Pan345,c,y none Real-Time Shift Factor of the Hub Bus(The Real-Time aggregated Shift Factor of a Hub Bus hb for the constraint c for the SCED interval y. RTSF pb,hb,Pan345,c,y none Real-Time Shift Factor of the power flow bus(The Real-Time Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. HUBDF hb, Pan345,c,y none Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the SCED interval y. HBDF b, hb, Pan345,c,y none Hub Bus Distribution Factor per power flow bus of Hub Bus(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. y none A SCED interval in the 15-minute Settlement Interval. The summation is over the total number of SCED runs that cover the 15-minute Settlement Interval. pb none An energized power flow bus that is a component of a Hub Bus for the constraint c for the SCED interval y. PB hb, Pan345 none The total number of energized power flow buses in Hub Bus hb for the constraint c for the SCED interval y. hb none A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c for the SCED interval y. HBBC Pan345,y none The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case for the SCED interval y. HB Pan345,c,y none The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c for the SCED interval y. c none A Real-Time binding transmission constraint for the SCED interval y caused by either base case or a contingency.

3.5.2.6	ERCOT Bus Average 345 kV Hub (ERCOT 345 Bus)

(1)	The ERCOT Bus Average 345 kV Hub is composed of the Hub Buses listed in Section 3.5.2.1, North 345 kV Hub (North 345); Section 3.5.2.2, South 345 kV Hub (South 345); Section 3.5.2.3, Houston 345 kV Hub (Houston 345); and Section 3.5.2.4,West 345 kV Hub (West 345).

[NPRR817: Replace paragraph (1) above with the following upon system implementation:] (1) The ERCOT Bus Average 345 kV Hub is composed of the Hub Buses listed in Section 3.5.2.1, North 345 kV Hub (North 345); Section 3.5.2.2, South 345 kV Hub (South 345); Section 3.5.2.3, Houston 345 kV Hub (Houston 345); and Section 3.5.2.4,West 345 kV Hub (West 345). The Panhandle 345 kV Hub is not included in the ERCOT Bus Average 345 kV Hub price.

(2)	The ERCOT Bus Average 345 kV Hub uses the aggregated Shift Factors of the Hub Buses for each hour of the Settlement Interval of the DAM in the Day-Ahead and is the simple average of the time weighted Hub Bus prices for each 15-minute Settlement Interval in Real-Time, for each Hub Bus included in this Hub.

(3)	The Day-Ahead Settlement Point Price of the Hub for a given Operating Hour is calculated as follows:

DASPP ERCOT345Bus =	DASL – (DAHUBSF ERCOT345Bus, c * DASP c),

if HBBC ERCOT345Bus≠0

DASPP ERCOT345Bus =	0, if HBBC ERCOT345Bus=0

Where:

DAHUBSF ERCOT345Bus, c   =	(HUBDF hb, ERCOT345Bus, c * DAHBSF hb, ERCOT345Bus, c)

DAHBSF hb, ERCOT345Bus, c  =	(HBDF pb, hb, ERCOT345Bus, c * DASF pb, hb, ERCOT345Bus, c)

HUBDF hb, ERCOT345Bus, c	=	IF(HB ERCOT345Bus, c=0, 0, 1 / HB ERCOT345Bus, c)

HBDF pb, hb, ERCOT345Bus, c	=	IF(PB hb, ERCOT345Bus, c=0, 0, 1 / PB hb, ERCOT345Bus, c)

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| DASPP ERCOT345Bus | $/MWh | Day-Ahead Settlement Point Price(The DAM Settlement Point Price at the Hub, for the hour. |
| DASL | $/MWh | Day-Ahead System Lambda(The DAM Shadow Price for the system power balance constraint for the hour. |
| DASP c | $/MWh | Day-Ahead Shadow Price for a binding transmission constraint(The DAM Shadow Price for the constraint c for the hour. |
| DAHUBSF ERCOT345Bus,c | none | Day-Ahead Shift Factor of the Hub (The DAM aggregated Shift Factor of a Hub for the constraint c for the hour. |
| DAHBSF hb,ERCOT345Bus,c | none | Day-Ahead Shift Factor of the Hub Bus(The DAM aggregated Shift Factor of a Hub Bus hb for the constraint c for the hour. |
| DASF pb,hb,ERCOT345Bus,c | none | Day-Ahead Shift Factor of the power flow bus(The DAM Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| HUBDF hb,ERCOT345Bus,c | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the hour. |
| HBDF pb, hb, ERCOT345Bus,c | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the hour. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c. |
| PB hb, ERCOT345Bus,c | none | The total number of energized power flow buses in Hub Bus hb for the constraint c. |
| hb | none | A Hub Bus that is a component of the ERCOT Bus Average 345 kV Hub (ERCOT 345 Bus) with at least one energized power flow bus for the constraint c. The Hub “ERCOT 345 Bus” includes any Hub Bus defined in the Hub “North 345”, “South 345”, “Houston 345” and “West 345”. |
| HBBC ERCOT345Bus | none | The total number of Hub Buses in the ERCOT Bus Average 345 kV Hub (ERCOT 345 Bus) with at least one energized component in each Hub Bus in base case. The Hub “ERCOT 345 Bus” includes any Hub Bus defined in the Hub “North 345”, “South 345”, “Houston 345” and “West 345”. |
| HB ERCOT345Bus,c | none | The total number of Hub Buses in the ERCOT Bus Average 345 kV Hub (ERCOT 345 Bus) with at least one energized component in each Hub Bus for the constraint c. The Hub “ERCOT 345 Bus” includes any Hub Bus defined in the Hub “North 345”, “South 345”, “Houston 345” and “West 345”. |
| c | none | A DAM binding transmission constraint for the hour caused by either base case or a contingency. |

(4)	The Real-Time Settlement Point Price of the Hub for a given 15-minute Settlement Interval is calculated as follows:

RTSPP ERCOT345Bus	=	Max [-$251, (RTRSVPOR + RTRDP +

(RNWFy * HUBLMPERCOT345Bus,y))]

Where:

RTRSVPOR 	=	(RNWF  y * RTORPA y)

RTRDP                      	 =           (RNWF y  * RTORDPA y)

RNWF y		=	TLMP y / TLMP y

HUBLMPERCOT34Bus,y  =  RTSLy –(RTHUBSF ERCOT345Bus, c,y * RTSPc,y),  if HBBC ERCOT345Bus,y≠0

HUBLMPERCOT345Bus,y 	= 	0, if HBBC ERCOT345Bus,y=0

RTHUBSF ERCOT345Bus,c,y	=	(HUBDF hb, ERCOT345Bus,c,y * RTHBSF hb, ERCOT345Bus,c,y)

RTHBSF hb, ERCOT345Bus,c,y	=	(HBDF pb, hb, ERCOT345Bus,c,y * RTSF pb, hb, ERCOT345Bus,c,y)

HUBDF hb, ERCOT345Bus,c,y	=	IF(HB ERCOT345Bus,c,y=0, 0, 1 / HB ERCOT345Bus,c,y)

HBDF pb, hb, ERCOT345Bus,c,y	=	IF(PB hb, ERCOT345Bus,c,y=0, 0, 1 / PB hb, ERCOT345Bus,c,y)

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| RTSPP ERCOT345Bus | $/MWh | Real-Time Settlement Point Price(The Real-Time Settlement Point Price at the Hub, for the 15-minute Settlement Interval. |
| RTRSVPOR | $/MWh | Real-Time Reserve Price for On-Line Reserves(The Real-Time Reserve Price for On-Line Reserves for the 15-minute Settlement Interval. |
| RTORPA y | $/MWh | Real-Time On-Line Reserve Price Adder per interval(The Real-Time On-Line Reserve Price Adder for the SCED interval y. |
| RTRDP | $/MWh | Real-Time On-Line Reliability Deployment Price(The Real-Time price for the 15-minute Settlement Interval, reflecting the impact of reliability deployments on energy prices that are calculated from the Real-Time On-Line Reliability Deployment Price Adder. |
| RTORDPA y | $/MWh | Real-Time On-Line Reliability Deployment Price Adder(The Real-Time price adder that captures the impact of reliability deployments on energy prices for the SCED interval y. |
| RNWF y | none | Resource Node Weighting Factor per interval(The weight used in the Resource Node Settlement Point Price calculation for the portion of the SCED interval y within the Settlement Interval. |
| RTSL y | $/MWh | Real-Time System Lambda(The Real-Time Shadow Price for the system power balance constraint for the SCED interval y. |
| RTSP c, y | $/MWh | Real-Time Shadow Price for a binding transmission constraint(The Real-Time Shadow Price for the constraint c for the SCED interval y. |
| TLMP y | second | Duration of SCED interval per interval(The duration of the portion of the SCED interval y within the 15-minute Settlement Interval. |
| HUBLMPERCOT345Bus,y | $/MWh | Real-Time Hub Locational Marginal Price (The Real-Time Hub LMP for the Hub for the SCED interval y. |
| RTHUBSF ERCOT345Bus,c,y | none | Real-Time Shift Factor of the Hub (The Real-Time aggregated Shift Factor of a Hub for the constraint c for the SCED interval y. |
| RTHBSF hb, ERCOT345Bus,c,y | none | Real-Time Shift Factor of the Hub Bus(The Real-Time aggregated Shift Factor of a Hub Bus hb for the constraint c for the SCED interval y. |
| RTSF pb,hb, ERCOT345Bus,c,y | none | Real-Time Shift Factor of the power flow bus(The Real-Time Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| HUBDF hb, ERCOT345Bus,c,y | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the SCED interval y. |
| HBDF b, hb, ERCOT345Bus,c,y | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| y | none | A SCED interval in the 15-minute Settlement Interval. The summation is over the total number of SCED runs that cover the 15-minute Settlement Interval. |
| pb | none | An energized Electrical Bus that is a component of a Hub Bus for the constraint c for the SCED interval y.. |
| PB hb, ERCOT345Bus,c,y | none | The total number of energized power flow bus in Hub Bus hb that is a component of the union of “North 345”, “South345”, Houston345”, and “West345” Hubs for the constraint c for the SCED interval y. |
| hb | none | A Hub Bus that is a component of the ERCOT345Bus Hub with at least one energized power flow bus for the constraint c for the SCED interval y. |
| HBBC ERCOT345Bus,y | none | The total number of Hub Buses in the ERCOT345Bus Hub (union of “North345”, “South345”, Houston345”, and “West345” Hub buses ) with at least one energized component in each Hub Bus in base case for the SCED interval y. |
| HB ERCOT345Bus,c,y | none | The total number of Hub Buses from the union of “North345”, “South345”, Houston345”, and “West345” Hubs with at least one energized component in each Hub Bus for the constraint c for the SCED interval y. |
| c | none | A Real-Time binding transmission constraint for the SCED interval y caused by either base case or a contingency. |

6.6.1.5		Hub LMPs

(1)	The Hub LMPs shall be posted on the MIS Public Area.

(2)	For each defined Hub except for the ERCOT Hub Average 345 kV Hub, the Hub LMP is the arithmetic average of the Real-Time LMPs of the Hub Buses included in the Hub.  The Hub LMP for a SCED Interval is calculated as follows:

HUBLMP Hub, y	=RTSLy –(RTHUBSF Hub, c,y * RTSPc,y),  if HBBC Hub,y≠0

HUBLMP Hub, y	=	HUBLMPERCOT345Bus,y,  if HBBC Hub,y=0

Where:

RTHUBSF Hub,c,y	=	(HUBDF hb, Hub,c,y * RTHBSF hb, Hub,c,y)

RTHBSF hb, Hub,c,y	=	(HBDF pb, hb,Hub,c,y * RTSF pb, hb, Hub,c,y)

HUBDF hb, Hub,c,y	=	IF(HB Hub,c,y=0, 0, 1 / HB Hub,c,y)

HBDF pb, hb, Hub,c,y	=	IF(PB hb, Hub,c,y=0, 0, 1 / PB hb, Hub,c,y)

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| HUBLMP Hub, y | $/MWh | Hub Locational Marginal Price(The Hub LMP for the Hub for the SCED Interval y. |
| RTHUBSF Hub,c,y | none | Real-Time Shift Factor of the Hub (The Real-Time aggregated Shift Factor of a Hub for the constraint c for the SCED interval y. |
| RTHBSF hb,Hub,c,y | none | Real-Time Shift Factor of the Hub Bus(The Real-Time aggregated Shift Factor of a Hub Bus hb for the constraint c for the SCED interval y. |
| RTSL y | $/MWh | Real-Time System Lambda(The Real-Time Shadow Price for the system power balance constraint for the SCED interval y. |
| RTSF pb,hb,Hub,c,y | none | Real-Time Shift Factor of the power flow bus(The Real-Time Shift Factor of a power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| HUBDF hb, Hub,c,y | none | Hub Distribution Factor per Hub Bus in a constraint(The distribution factor of Hub Bus hb for the constraint c for the SCED interval y. |
| HBDF pb, hb, Hub,c,y | none | Hub Bus Distribution Factor per power flow bus of Hub Bus in a constraint(The distribution factor of power flow bus pb that is a component of Hub Bus hb for the constraint c for the SCED interval y. |
| y | none | A SCED interval. |
| pb | none | An energized power flow bus that is a component of a Hub Bus for the constraint c for the SCED interval y. |
| PB hb, Hub,c,y | none | The total number of energized power flow buses in Hub Bus hb for the constraint c for the SCED interval y. |
| hb | none | A Hub Bus that is a component of the Hub with at least one energized power flow bus for the constraint c for the SCED interval y. |
| HBBC Hub,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus in base case for the SCED interval y. |
| HB Hub,c,y | none | The total number of Hub Buses in the Hub with at least one energized component in each Hub Bus for the constraint c for the SCED interval y. |
| c | none | A Real-Time binding transmission constraint for the SCED interval y caused by either base case or a contingency. |
| Hub | none | One of the following Hubs: ERCOT Bus Average 345 kV Hub, North 345 kV Hub, South 345 kV Hub, Houston 345 kV Hub, or the West 345 kV Hub |

(3)	The Hub LMP for the ERCOT Hub Average 345 kV Hub (ERCOT 345) for a SCED Interval is calculated as follows:

HUBLMP ERCOT345, y	=	(HUBLMPNORTH345, y + HUBLMPSOUTH345, y + HUBLMPHOUSTON345, y  + HUBLMPWEST345, y) / 4

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| HUBLMPERCOT345, y | $/MWh | Hub Locational Marginal Price for the ERCOT345(The Hub LMP for the ERCOT Hub Average 345 kV Hub (ERCOT 345), for the SCED Interval y. |
| HUBLMPNORTH345, y | $/MWh | Hub Locational Marginal Price for the NORTH345(The Hub LMP for the North 345 kV Hub (NORTH 345), for the SCED Interval y. |
| HUBLMPSOUTH345, y | $/MWh | Hub Locational Marginal Price for the SOUTH345(The Hub LMP for the South 345 kV Hub (SOUTH 345), for the SCED Interval y. |
| HUBLMPHOUSTON345, y | $/MWh | Hub Locational Marginal Price for the HOUSTON345(The Hub LMP for the Houston 345 kV Hub (HOUSTON 345), for the SCED Interval y. |
| HUBLMPWEST345, y | $/MWh | Hub Locational Marginal Price for the WEST345(The Hub LMP for the West 345 kV Hub (WEST 345), for the SCED Interval y. |

# Comments

Instead of repeat the HUBLMP for every Hub, can we just refer it to Section 6.6.1.5.

Also the RTSPP formula is also repeated for every Hub and is redundant.