## Slide 1
Refresher on NPRR826, Mitigated Offer Caps for RMR Resources
David Maggio
Manager, Market Analysis and Validation
August 13th, 2018

## Slide 2: Introduction
During the July WMS meeting, there was discussion on QMWG restarting the review of NPRR826.
To facilitate that restart, it was requested that ERCOT provide a refresher on the NPRR and where discussions left off.
The latest version of the NPRR is from August ‘17 following that month’s PRS meeting.
A few entities had submitted comments in the month or so leading up to this PRS meeting, however, the language has been static as of ERCOT comments submitted on June 23rd, 2017.

## Slide 3: Overview of the Process Currently Captured in the NPRR
Under the current language:
  Analysis would be performed by ERCOT to determine a single heat rate that would be applied across the full dispatchable range of the RMR Resource.
  The single heat rate would be separately calculated for each RMR Resource and would be determined using the following steps and used for the RMR Resource’s MOC curve:
    For each non-RMR Resource for each analyzed SCED interval and constraint, calculate a value = (Price at HSL from the Step 2 EOC for that Resource)/Abs(Shift factor for that Resource for the specified constraint)
    For each SCED interval and constraint, identify the largest value that is less than the maximum Shadow Price for the constraint
      Call this value “X”
      Results in ignoring Resources that could not have been dispatched up to HSL to help resolve the congestion.

## Slide 4: Overview of the Process Currently Captured in the NPRR cont.
    For each SCED interval and constraint, determine a value “Y” = the minimum of:
      X + $50/MWh; and
      The maximum Shadow Price of the constraint - $1/MWh
      Results in ignoring Resources that could not have been dispatched up to HSL to help resolve the congestion.
      If X is null, then it is assumed that “b.” would be the minimum
    For each SCED interval and constraint, determine a value “Z” that is = Y * Abs(Shift factor for the RMR Resource for the specified constraint) / FIP for the Operating Day of the SCED interval.
      For SCED intervals where multiple constraints are analyzed, used the largest Z for the interval.
    Set the single heat rate of the RMR Resource as the 99th percentile of all the Z values determined for each SCED interval in the study period.

## Slide 5: Overview of the Process Currently Captured in the NPRR cont.
  The study period consists of the most recent 60 calendar months up until the date of the analysis.
  The transmission constraints considered will be based on the constraints identified in the RMR final assessment.
  The initial analysis is performed as soon as practicable and updates are performed ahead of each contract month.
  Other cost variables for the MOC curve of the RMR Resource will be set to 0 and the capacity factor for the Resource will be set to 1.
    This will result is the MOC curve simply being the product of the single heat rate calculated and the FIP for the given Operating Day.
  The IMM can suspend this process.

## Slide 6: Simple Example with 2 Resources
Assume the following:
  2 Resources - A is an RMR Resource and B is a non-RMR Resource
  There is only one constraint being analyzed and the same input values apply to all SCED intervals in the study period.
  For Resource B:
    The price at HSL from the Step 2 EOC is $100/MWh
    The shift factor to the constraint is -10%
  For Resource A, the shift factor to the constraint is -20%
  The maximum Shadow Price for the constraint is $3,500/MWh
  FIP is $3/MMBtu

## Slide 7: Simple Example with 2 Resources cont.
$100/MWh / Abs(-10%) = $1,000/MWh
X is set to $1,000/MWh
  There is only 1 non-RMR Resource, the value from the previous step is $1,000/MWh, and this value is less than $3,500/MWh
Y = minimum ($1,000/MWh + $50/MWh, $3,500/MWh - $1/MWh) = $1,050/MWh
Z = $1,050/MWh * Abs(-20%) / $3/MMBtu = 70 MMBtu/MWh
The 99th percentile of several values all equal to 70 MMBtu/MWh would mean the single heat rate for the RMR Resource’s MOC curve is 70 MMBtu/MWh across its entire operating range.

## Slide 8: Points of Discussion following the August ‘17 PRS Meeting
In the months following the August ‘17 PRS meeting, some stakeholders had reached out to ERCOT to discuss the following concepts and questions:
  Incorporate a form of steps 1 through 4 of the previously described process into the two-step SCED process and have the MOC curve based on a price for the SCED interval, as opposed to being based on a periodic analysis of historical offers.
    The calculation could occur between steps 1 and 2, immediately after the Step 2 EOCs are determined for all of the non-RMR Resources.
  Only go through the effort of the calculation when the RMR is flagged for mitigation, in order to limit computational impacts.
  Consider the application of shift factor cutoffs when determining which non-RMR Resources to include in the analysis.
  Reconsider how to handle the case in which multiple constraints are being analyzed for a given SCED interval.

## Slide 9: Points of Discussion following the August ‘17 PRS Meeting cont.
  The current process only considers the congestion component of the LMP. If we’re doing these calculations as part of the SCED process in real-time, can we potentially consider both the congestion and power balance components of the LMP?
    Because System Lambda is an output of step 2 of SCED, we would have to use a proxy value (E.g., the System Lambda from step 1 or the System Lambda from the previous SCED execution).
  For SCED CCT, once mitigation has been applied to a Resource for a SCED interval, the Resource continues to be flagged for mitigation for the remainder of the hour. Due to the scenario of the applicable constraints being deactivated mid-hour, we need to consider how to manage this process for an RMR Resources
    E.g., have the persistence logic not apply RMR Resources.

## Slide 10: Questions