## Slide 1
2017 Real-Time Co-optimization Backcast
Steve Reedy
Deputy Director, ERCOT IMM
sreedy@potomaceconomics.com
512-225-7139
Austin Electricity Conference
September 6, 2018

## Slide 2: What is Real-Time Co-optimization (of Energy and Reserves)?
Co-optimization of Energy and Reserves: Awarding the least cost providers of energy and reserves
Current Market Design
  Awards co-optimized reserves and energy in the Day-Ahead Market
  QSEs can redistribute reserve awards within their fleet (or trade with other QSEs)
  Final provision of reserves is not optimized by ERCOT.
Real-Time Co-optimization Design
  Awards co-optimized reserves and energy in both Day-Ahead and Real-Time markets
  Final provision of reserves is optimized by ERCOT

## Slide 3: IMM Real-Time Co-optimization Study
“Backcast” of 2017
Uses 2017 data for:
  Commitment status of resources (ON, OFF, etc.)
  Energy offers
  Ramp Rates
  Network Conditions (binding constraints, shift factors)
Every 15 minutes
  Data published in 60 day SCED reports
Not “Sequential”
  The results of the simulation of 12:15 do not affect the input the simulation of 12:30
  Sequential simulation would:
    Require assumptions of market behavior (to what extent do generators follow their basepoints)
    Reduce the accuracy of the simulation inputs(binding constraints, shift factors, ramp rates, loss factors, etc. valid for actual system conditions, not necessarily for different input conditions)
    Increase the simulation time (impossible to run simulation with several computers in parallel, would increase run time by at least 30x)

## Slide 4: What the simulation tool does
Takes all inputs and re-runs SCED
  Confirms validity of inputs (Results of simulation close to actual SCED results?)
    In the few instances where this happened results were discarded
  Enables comparison of a simulation to a simulation
Linearizes offer curves and determines best RRS awards using a Mixed Integer Program (MIPCL-PY)
  If a resource provides RRS and has some NFRC (non-frequency responsive capacity) then the NFRC has to be subtracted from the High Limit. This binary behavior requires a special solving algorithm (MIP).
Takes RRS awards from Step 2 and all inputs and determines energy and reserve awards and prices with a Quadratic Program (QP).
Publishes detailed and summary results files for each day.

## Slide 5: Key Assumptions and Likely Effects
Assumes that commitment remains constant. i.e. everyone would have had the exact same units on for the exact same times in a Real-Time Co-optimized world.
  It would be likely that generator owners would respond to lower prices by not turning on as many units. This would tend to raise production cost savings and raise energy and reserve prices.
  This can be simulated by turning units “OFF” in 60d_SCED input file and redistributing missing MWs to other units.

## Slide 6: Key Assumptions and Likely Effects (2)
Assumes that offers for reserves would be $0/MWh.
  Raising the offer price would tend to raise reserve prices.
  This can be simulated by:
    Modifying the Objective Function in the MIP portion of the code, and
    Modifying the q vector in the QP portion of the code
The results of one interval do not effect the next (Non-Sequential)
  Modeling sequential effects would tend to increase the production cost savings and reduce the energy and reserve prices.
  This can be simulated by:
    Producing a set of input files for the next interval with each simulation run
    Would require simulating every five minutes (instead of published 15 minutes)

## Slide 7: Key Findings
$11.6M reduction in production costs (likely a floor due to commitment assumptions)
$4.3M improvement in system reliability (likely a floor due to non-sequential nature of model)
$155M reduction in reserve costs (likely a ceiling due to commitment assumptions)
$1.6B reduction in energy costs (likely a ceiling due to commitment assumptions)