## Slide 1
QSE Impacts From RTC
Sai Moorty
Principal, Market Design and Analysis
Technical Workshop on IMM and ERCOT Reports Concerning Impacts of Real-Time Co-Optimization and Marginal Losses
September 6, 2018

## Slide 2: Introduction
RTC concept paper posted to the Sept. 18, 2017 SAWG meeting web page:
http://www.ercot.com/content/wcm/key_documents_lists/131797/RT_Co-optimization_Scope_UPDATED_09292017.docx
RTC examples posted to the July 14, 2017 SAWG meeting web page:
http://www.ercot.com/content/wcm/key_documents_lists/122875/RT_Co-Optimization_Scenario_Automated.xlsm

## Slide 3: Introduction
RTC replaces current SCED & ORDC mechanism to value energy and operating reserves
  RTC is the process of simultaneously procuring, in real time, energy (Base Points) and reserves to meet real-time system demand and Ancillary Services (AS)
    Resource Specific Base Points and AS awards for all the AS types determined - nominally every 5 minutes
    LMPs and AS MCPCs will automatically incorporate the value of operating reserve shortages (no ORDC price adders required)
  Different AS products (i.e., RegUp, RegDown, RRS, Non-Spin) will have their respective individual demand curves to value the different types of operating reserves

## Slide 4: QSE Impact: AS Product Set
Under RTC, the AS product set may change.
  One option being considered is to split Non-Spin between On-Line and Off-Line Resources.
    On-Line Non-Spin  Spinning Operating Reserves (SOR)
    Off-Line Non-Spin  Non-Spinning Operating Reserves (NSOR)
  Location/region-based AS product
    The functionality to have locational AS product requirements is expected to be included in any ERCOT system changes.
    Whether this product is required and how the requirements would be estimated has not yet been determined.

## Slide 5: QSE Impact: Management of Energy and AS Offers
There will be a different offer cap for energy and a different offer cap for AS
  As an example,
    Value Of Lost Load (VOLL) = 9,000 $/MWh
    Max Value on Power Balance Penalty Curve = 9,001 $/MWh
    Energy Offer Cap = 2,000 $/MWh
    AS Offer Cap = 7,000 $/MWh
AS offer submittal/modification and timeline rules may change (subject to stakeholder decisions); i.e., proxy AS offers used when no AS offer submitted by QSE
  Analogous to energy offers submittal and timeline rules currently in real time

## Slide 6: QSE Impact: Management of energy and AS Offers
New telemetry point from QSE to ERCOT indicating status of ability to provide AS in real time
  Resource specific
  By AS type if resource qualifies
Energy offer floor for Non-Spin capacity will no longer be required

## Slide 7: QSE Impact: Management of RTC Awards for AS
RTC will consider all capacity (HSL) as available for procurement of energy (Base Point) and AS
  “HASL” free
  Ramp rate, NFRC, ability to provide AS, etc. still considered
After completion of RTC, ERCOT will transfer via ICCP to QSEs
  Resource specific AS awards by AS type
  AS MCPC by AS type
Due to latency of data transfer/processing, QSE expected to respond to AS deployment upon ERCOT instructions
  QSE may receive regulation deployment instructions before QSE has processed the latest RTC awards to QSE for Regulation Service
  No “handshaking” between ERCOT and QSE for receipt of AS awards (similar to Base Points)

## Slide 8: QSE Impact: Other Telemetry Changes
QSE will not send following telemetry for Generation Resources and Controllable Load Resources
  AS responsibility
  AS schedule
If LFC is changed to issue regulation deployments on a resource specific basis, then QSE will not send Regulation Participation Factor telemetry to ERCOT
  If LFC regulation instructions are at QSE level, then QSE will still be required to send resource specific Regulation Participation Factors for performance measurement purposes
  This would be a future design discussion with stakeholders

## Slide 9: QSE Impact: Load Resources with UFR (for RRS)
Business as usual for Load Resources with UFR providing RRS
Load Resources with UFR providing RRS
  QSE will continue to send current telemetry
  RTC will consider Load Resource providing RRS as price taker
    Effectively, the Real-Time RRS responsibility will be the same as the Day-Ahead awards
  Deployment procedures remain the same

## Slide 10: QSE Impact: MIS Posting
New posting of resource specific AS awards by AS type (confidential)
New posting of AS MCPCs by AS type (public)
60-day report for AS offers in real time and other potential disclosure report changes

## Slide 11: QSE Impact: RUC and SASM
RUC would be modified to have the ability to coordinate the provision of energy and AS among resources to meet energy demand, as well as AS requirements
  Resource COP HSL, instead of COP HASL, considered by RUC
  RUC objective changed to have resource available to meet energy demand and total AS requirements, while managing forecasted transmission congestion
  RUC commitment could be for AS (new)
Current thinking is that SASM would no longer be needed
  RUC ensures sufficient capacity looking forward, to meet energy demand and AS requirements
  RTC will procure the actual energy and AS from resources

## Slide 12: QSE Impact: Settlements
Conceptually, AS procured in real time will be settled in a similar fashion as Real-Time Energy Imbalance Settlement
  There will be an AS imbalance settlement for each AS type
  Similar approach is currently used to settle ORDC payments for operating reserves (Protocol 6.7.5)
Proposed RTC framework does not create any NEW make-whole payment to resources and corresponding uplift to load
QSE Shadow Settlements

## Slide 13
Questions?