## Slide 1: Texas Standard Electronic Transactions
Introduction to TX SET

## Slide 2: Protocol Disclaimer
This presentation provides a general overview of Retail Transaction Processing and is not intended to be a substitute for the ERCOT Protocols, as amended from time to time. If any conflict exists between this presentation and the ERCOT Protocols, the ERCOT Protocols shall control in all respects.
For more information, please visit:
http://www.ercot.com/mktrules/nprotocols/

## Slide 3: Housekeeping
Restrooms
Refreshments
Attendance sheet
Questions
  Please silence smart phones & other electronics

## Slide 4: Antitrust Admonition
To avoid raising concerns about antitrust liability, participants in ERCOT activities should refrain from proposing any action or measure that would exceed ERCOT’s authority under federal or state law. For additional information, stakeholders should consult the Statement of Position on Antitrust Issues for Members of ERCOT Committees, Subcommittees, and Working Groups, which is posted on the ERCOT website.

## Slide 5: Course Objectives
What is TX SET?
Where do I find Tools/References?
How does TX SET work?
How is TX SET managed?
Notes: The term Texas SET can refer to two different things.
TX SET (Standard Electronic Transactions) are a set of ANSI EDI transaction guidelines customized by the TX SET Working Group for the ERCOT Retail Market.
These standardized transactions support retail processes as documented in the various ERCOT Market rules.
TX SET is an ERCOT Working group comprised of stakeholders participating in the development and maintenance of TX SET EDI transactions .
The Working Group reports to the Retail Market Subcommittee (RMS) and analyzes the need for new electronic transactions or modifications to existing electronic transactions based upon changes that occur within the retail electric market that affect EDI (electronic data interchange) transaction processing.

## Slide 6: Agenda
Introduction
Governing Documents
Transactions
Transaction Process Flow
MIS Portal
TXSET Working Group
Appendix

## Slide 7: Introduction

## Slide 8: What is TX SET?
Texas Standard Electronic Transactions
Set of ANSI EDI transaction guidelines
Facilitates retail business processes
Maintained by TX SET working group
Notes: The term Texas SET can refer to two different things.
TX SET (Standard Electronic Transactions) are a set of ANSI EDI transaction guidelines customized by the TX SET Working Group for the ERCOT Retail Market.
These standardized transactions support retail processes as documented in the various ERCOT Market rules.
TX SET is an ERCOT Working group comprised of stakeholders participating in the development and maintenance of TX SET EDI transactions .
The Working Group reports to the Retail Market Subcommittee (RMS) and analyzes the need for new electronic transactions or modifications to existing electronic transactions based upon changes that occur within the retail electric market that affect EDI (electronic data interchange) transaction processing.

## Slide 9: Benefits of TX SET
    Standardization of automated processes
    Improves data quality and efficiency
    Greater transparency
    Improved security
    Allows reporting flexibility
    Increased cost savings
Notes: Why do we have it?
  Can you imagine the volumes of transactions per day? (Average daily volume for ERCOT, inbound and outbound, is in excess of 150,000)
Standardization is key!

## Slide 10: When are TX SET used?
To execute Retail market processes
  Move In
  Move Out
  Switch
  Disconnects
  Reconnects
  Updates to premise information
  Updates to customer information
Notes: TX SET transactions should be used when needing to execute a Retail Market
Process supported by TX SET EDI.
In the event a process cannot be supported by TX SET EDI transactions, the
Market standard method should be used. Please consult the ERCOT Retail Market Guide.
Some of these processes include:
The Safety Net Spreadsheet
MarkeTrak

## Slide 11: How are TX SET Delivered?
NAESB EDM v1.6
North American Energy Standards Board
Electronic Delivery Mechanism
  Version 1.6 is a National Standard
  Secured computer to computer data protocol
  Modified to fit ERCOT Market
Notes: TX SET EDI Transactions are securely transmitted through
servers from sender to receiver with the NAESB EDM (Electronic Delivery Mechanism) v1.6 Protocol installed on each server.
This is a protocol with specialized technical enhancements modified to fit the ERCOT retail market.
The NAESB EDM v1.6 is a National Standard maintained by the North American Energy Standards Board.
The ERCOT NAESB EDM v1.6 guideline is managed by the ERCOT Working Group TDTMS (Texas Data Transport and MarkeTrak System).

## Slide 12: Transaction Flows
REP’s Customer Information System
TDSP’s Customer Information System
Notes: TX SET Transactions could potentially follow two paths.
Point to point (REP – TDSP)
Flow through ERCOT

## Slide 13: Acronyms
TX SET – Texas Standard Electronic Transactions
PURA – Public Utilities Regulatory Act
PUCT – Public Utility Commission of Texas
ERCOT – Electric Reliability Council of Texas
NAESB – North American Energy Standards Board
MP – Market Participant
ESI ID – Electric Service Identifier

## Slide 14: Acronyms
LSE
Load Serving Entity
REP
Retail Electric Provider
ROR
REP of Record
CR Competitive Retailer
MOU/EC
Municipal/Coop
TDSP Transmission & Distribution Service Provider
TDU Transmission & Distribution Utility

## Slide 15: Governing Documents

## Slide 16: Hierarchy of Rules
PUCT Substantive Rules
Public Utility Regulatory Act (PURA)
ERCOT Protocols

## Slide 17: ERCOT Protocols
Rules/Policies/Standards that govern the ERCOT market
  Created through collaborative efforts
  Define procedures used by ERCOT and Market Participants (MPs)
  MPs, ERCOT and Independent Market Monitor (IMM) bound by Protocols
Notes: The Electric Reliability Council of Texas (ERCOT) Protocols, created through the collaborative efforts of representatives of all segments of Market Participants, as amended from time to time, that contains the scheduling, operating, planning, reliability, and Settlement (including Customer registration) policies, rules, guidelines, procedures, standards, and criteria of ERCOT.
These Protocols outline the procedures and processes used by ERCOT and Market Participants for the orderly functioning of the ERCOT system and nodal market.
Market Participants, the Independent Market Monitor (IMM), and ERCOT shall abide by these Protocols.

## Slide 18: ERCOT Protocols

## Slide 19: Relevant ERCOT Protocol Sections
Section 2 – Definitions and Acronyms
Section 9 – Settlements and Billing
Section 10 – Metering
Section 12 – Market Information System
Section 15 – Customer Registration
Section 18 – Load Profiling
Section 19 – Texas Standard Electronic Transaction
Section 21 – Revision Request Process
Section 24 – Retail Point to Point Communications

## Slide 20: Section 15 - Customer Registration
ERCOT is the Registration Agent for the Retail Electric Market
ERCOT maintains the Registration Database of all ESI IDs
All Competitive Retailers operating in ERCOT register their customers via TX SET
Notes: This section provides Market Participants and ERCOT with the market rules and transactional timing when operating in ERCOT’s Retail Electric Market and providing Customer Choice, for example:
  ERCOT shall maintain a registration database of all metered and unmetered Electric Service Identifiers (ESI IDs) in Texas for Customer Choice.
  All Customer registration processes will be conducted using the appropriate Texas Standard Electronic Transactions (TX SETs). Definitions of all TX SET codes referenced in this Section can be found in Section 19, Texas Standard Electronic Transaction.
  All CRs with Customers in Texas, whether operating inside the ERCOT Region or not, shall be required to register their Customers in accordance with this Section.

## Slide 21: Section 19 – Texas Standard Electronic Transaction
Transactions between Competitive Retailers (CRs), ERCOT, and Transmission and Distribution Service Providers (TDSPs)
Validation process
TX SET change control process
Retail market testing process
Notes: Provides the mechanism that enables and facilitates the retail business processes in the deregulated Texas electric market. The Texas SET Implementation Guides shall serve as the standard for the applicable TX SETs among all Market Participants and ERCOT.
This Section shall cover:
  Transactions between Transmission and/or Distribution Service Providers (TDSPs) (refers to all TDSPs unless otherwise specified), Competitive Retailers (CRs) and ERCOT;
  Technical Advisory Committee (TAC) subcommittee and ERCOT responsibilities; and
  Texas SET Change Control process.

## Slide 22: Section 24 – Retail Point to Point Communications
Transactions that do not flow through ERCOT
Transactions that flow between CRs and TDSPs
  Disconnect/Reconnect
  Suspension of delivery
  Remittance information
  TDSP Invoice
Notes: Point to point communications include transactions flowing directly between Competitive Retailers (CRs), and Transmission and/or Distribution Service Providers (TDSPs) and do not flow through ERCOT. These point to point transactions may be Customer requested service orders and CR/TDSP invoicing and remittance advise transactions.

## Slide 23: ERCOT Market Guides
ERCOT
Market Guides
ERCOT Protocols
Other Binding Documents (OBDs)

## Slide 24: ERCOT Market Guides

## Slide 25: ERCOT Retail Market Guide
Section 1 – Purpose
Section 2 – Definitions and Acronyms
Section 3 – Retail Market Guide Revision Process
Section 4 – Public Utility Commission of Texas
Section 5 – Electric Reliability Council of Texas
Section 6 – Retail Market Subcommittee Working Group
Section 7 – Market Processes
Section 8 – Municipally Owned Utilities and Electric Cooperatives
Section 9 – Appendices
Section 10 – Competitive Metering
Section 11 – Solution to Stacking

## Slide 26: Section 7 – Market Processes
Section 7.3 – Inadvertent Gain Process
Section 7.4 – Safety Nets
Section 7.5 – Standard Historical Usage Requests
Section 7.6 – Disconnect and Reconnect for Non-Payment Process
Section 7.7 – Transaction Timing Matrix
Section 7.16 – Business Processes and Communications Related to Meter Tampering
Section 7.15 - Advanced Meter Interval Data File Format and Submission
Section 7.17 – Business Processes and Communications for Switch Holds Related to Deferred Payment

## Slide 27: Appendices
Section 9 Appendix D1 – Transaction Timing Matrix
Section 9 Appendix D3 – TDSP’s Discretionary Service Timelines Matrix
Section 9 Appendix G – ERCOT Specified File Format for Submission of Interval Data for Advanced Metering Systems
Notes: Reference protocals section 15

## Slide 28: Section 11- Solution to Stacking
  Section 11.1 - Overview of Solution to Stacking
  Section 11.2 - ERCOT Operating Rules
  Section 11.2.2 - Cancellation Rules
  Section 11.2.3 - Concurrent Processing Rules
  Section 11.2.4 - Pending Transaction Rules
  Section 11.3 - Transmission and/or Distribution Service Provider Operating Rules
  Section 11.4 - Retail Electric Provider Operating Rules
Notes:   Section 11.1 - Overview of Solution to Stacking
    This Section 11, Solution to Stacking, provides the processes and guidelines for Market Participants operating in the Texas retail market to handle multiple non-sequential Texas Standard Electronic Transactions (TX SETs) on a single Electric Service Identifier (ESI ID).
  Section 11.2 - ERCOT Operating Rules
    The ERCOT Operating Rules describe the process and guidelines utilized by ERCOT to process multiple, non-sequential transactions concurrently on a single Electric Service Identifier (ESI ID).
  Section 11.2.2 - Cancellation Rules
    These rules detail the circumstances under which ERCOT will cancel existing orders.
  Section 11.2.3 - Concurrent Processing Rules
    The concurrent processing rules detail the circumstances in which transactions are allowed to complete after being processed concurrently.
Section 11.2.4 - Pending Transaction Rules
  These rules detail the methods used for Pending REP Notification Transactions. These rules were developed to ensure that these transactions are sent only when the appropriate recipient can be positively identified.
Section 11.3 - Transmission and/or Distribution Service Provider
Operating Rules
  The business rules Transmission and/or Distribution Service Providers (TDSPs) will follow in order to process multiple, non-sequential transactions concurrently on a single Electric Service Identifier (ESI ID).
Section 11.4 - Retail Electric Provider Operating Rules
  Retail Electric Providers (REPs), like the Transmission and/or Distribution Service Providers (TDSPs) and ERCOT, will be required to handle multiple, non-sequential transactions on an Electric Service Identifier (ESI ID).

## Slide 29: TX SET Guides
Notes: But for quick reference, there is also a Transaction Name Inventory posted on ERCOT.com, complete with a handy pocket card. We printed and laminated pocket cards to give you here today. We hope that you will find them as useful as we do. We also hope that you will use them in the upcoming class scenarios!

## Slide 30: Texas SET Swimlanes
Texas Standard Electronic Transaction (SET) swimlanes are reference documents that outline the business process lifecycle for transactions used in the competitive retail electric market in Texas.
http://ercot.com/mktrules/guides/txset/sw

## Slide 31: TX SET Swimlanes

## Slide 32: Texas SET Implementation Guides (IG)
TX SET Implementation Guides provide technical details contained within the electronic transactions used in the competitive retail electric market in Texas.
Current Version 4.0 supports PUC Substantive Rules and market process revisions
http://ercot.com/mktrules/guides/txset/current

## Slide 33: Transactions

## Slide 34: Overview of transaction flow
650
TDSP
CR
810
824
820
814
824
867
814
824
867
824 – Rejects
867 – Usage
814 – ESIID info and relationships
820 – Remittance advice
650 – Service Orders
810 – Invoice
814 PC/PD only
Notes: Moved up two slides

## Slide 35: Texas Standard Electronic Transactions (TX SET)
Many transactions involve ERCOT
Transaction Type | Use
814 –ESI ID info and Relationships (Many flavors) | Enrollments; Switch requests; Move-Ins; Move-Outs; ESI ID Maintenance
867 – Premise Usage | Initial Meter Read; Historical/Monthly Usage; Final Usage
824 – Reject Notification | Invoice or Usage Reject Notification

## Slide 36: Texas Standard Electronic Transactions (TX SET)
Some transactions may not involve ERCOT
Transaction Type | Use
810 – Invoice | Bills for Charges between Market Participants
820 – Payments | Payments between Market Participants
650 –Service Order Requests | Disconnects for Non-Pay; Reconnects; Switch Hold and Switch Hold Removal; Planned Outage Notification
824 – Reject Notification | Invoice or Usage Reject Notification
These are called Point-to-Point transactions and flow between TDSPs and REPs

## Slide 37: Transaction Names
TX SET Version 4.0 – Transaction Names Inventory
Refer to handout
Defines the transaction name for each transaction
Describes how the transaction flows
Found on the ERCOT website at http://www.ercot.com/mktrules/guides/txset

## Slide 38: Transaction Names – 650_01 Service Orders
There are 80 REF segments to identify the purpose of the 650 Service Order based on the above 11 codes
From 650_01 Implementation guide.

## Slide 39: MVI vs SWI – 814_16 vs 814_01
 | Move In – 814_16 | Switch – 814_01
Definition | Customer requesting service connected in their name at either a new or an existing premise. | The process by which the current Customer makes a request to change their REP of Record for their ESI ID(s).
Timing & Costs | Move In fees and potential delays could be encountered | No fees (Standard Switch, if applicable) Allows for same day request and completion
Occupant Permit | Required for some municipalities/cities | Not required
Critical Care and Chronic Condition | Designation will be terminated due to New Customer MVI Critical Care and Chronic Condition status’ are associated to the Customer and not the Premise | No change to status
Billing Demand Reset | Demand Ratchet resets | No impact to Billing Demand
4CP (Coincident Peak) | 4CP demand resets | No change to 4CP demand
Non-standard Metering Premise | Meter is replaced with Standard meter and additional charge(s) to Customer if requested to re-install non-standard meter | No change

## Slide 40: Transactions Initiating Business Process Instance
Initiating Business Process Instance (BPI)
    Move In 814_16
    Switch 814_01
    Move Out 814_24
The business processes listed above will start or end a REP’s relationship with their customer.

## Slide 41: Transactions Initiating Business Process Instance
Business process instances may be closed as Completed or Cancelled.
Cancelled transactions may be a result of:
    Cancel Request 814_08
    Complete Unexecutable 814_28 CU

## Slide 42: Checkpoint Questions
True or False: Response transactions can only be Rejects.
FALSE
True or False: A point-to-point transaction is sent only to ERCOT.
FALSE

## Slide 43: Checkpoint Questions
What transaction is used to determine the actual start date for a customer?
814_04
814_16
867_04
814_01

## Slide 44: Transaction Process Flow

## Slide 45: Move In (MVI) – Reject
ERCOT
New CR
814_16 (MVI)
1
814_17 (only a reject)
2

## Slide 46: Move In – Accept
TDSP
ERCOT
New CR
814_16
1
814_03
2
814_04
3
4
814_05
867_02
5
867_02
6
867_04
7
867_04
8

## Slide 47: Move In w/ Permit Required – New Installation
TDSP
ERCOT
New CR
814_16
1
4
814_28
814_03
2
814_28
3
814_04
5
814_05
6
867_04
7
867_04
8
Customer sends permit to TDSP

## Slide 48: Move In w/ Permit Not Received
Customer does not send permit to TDSP within 20 days
814_08
5
814_08
7
814_09
6
TDSP
ERCOT
New CR
814_16
1
4
814_28
814_03
2
814_28
3

## Slide 49: Move In w/ Cancel
TDSP
ERCOT
New CR
814_16
1
814_03
2
814_04
3
814_05
4
867_02
5
867_02
6
814_08
7
814_08
8
814_09
9
814_09
10
Customer cancels MVI

## Slide 50: Move In w/ Date Change
TDSP
ERCOT
New CR
Current CR
814_16
1
814_03
2
814_04
3
814_05
4
867_02
5
867_02
6
814_12
7
814_12
8
814_13
9
814_13
10
814_06
11
867_03F
14
810_02
16
867_04
12
867_04
13
867_03F
15
Customer changes MVI date

## Slide 51: Checkpoint Questions
Yes or No: If a MVI order is submitted and an 814_28 PR is received, does it cancel the original MVI order if the permit is received within 20 days?
NO
Yes or No: If a MVI order is submitted and an 814_28 PR is received and then later an 814_08 is received, should the CR receive an 867_04?
NO
Yes or No: Based on the scenario in the previous question, should the CR expect this customer to be with the submitting CR?
NO

## Slide 52: Switch – Rejected
814_01
1
814_02
2
TDSP
ERCOT
New CR
Current CR

## Slide 53: Switch – Accept
TDSP
ERCOT
New CR
Current CR
814_01
1
867_02
6
814_05
4
867_02
7
867_04
9
814_03
2
814_04
3
867_04
8
867_03F
10
810_02
12
867_03F
11
814_06
5

## Slide 54: Switch Hold – Add – Deferred Payment Plan (DPP)
TDSP
ERCOT
Current CR
650_01 (add)
1
814_20
4
814_21
5
814_20
3
650_02 (acknowledgement)
2

## Slide 55: Switch Hold – Add - Tampering
814_20
2
814_21
3
814_20
1
810_02 (tampering)
4
TDSP
ERCOT
Current CR

## Slide 56: Switch Hold – Remove – DPP / Tampering
650_01 (remove)
1
814_20
4
814_21
5
814_20
3
650_02 (acknowledgement)
2
TDSP
ERCOT
Current CR

## Slide 57: Switch w/ Switch Hold
TDSP
ERCOT
New CR
814_01
1
814_03
2
814_04R
3
814_05R
4
Same result for MVI

## Slide 58: Checkpoint Questions
What transaction does the TDSP receive when an 814_01 or 814_16 is initiated?
867_04
814_03
867_03
814_04

## Slide 59: Checkpoint Questions
A Customer Loss (814_06) transaction is sent to which entity?
Current REP of Record
TDSP
ERCOT
New CR
True or False: The 814_04 / 814_05 provides premise attributes and scheduling.
TRUE

## Slide 60: Move Out (MVO) – Reject
TDSP
ERCOT
Current CR
814_24
1
814_25R
4

## Slide 61: Move Out – Accept
814_24
1
814_24
2
814_25
3
814_25
4
867_03F
5
867_03F
6
810_02
7
TDSP
ERCOT
Current CR

## Slide 62: Checkpoint Questions
True or False: If a Switch Hold exists on an ESIID, a MVO transaction (814_24) will automatically reject.
FALSE

## Slide 63: Checkpoint Questions
A date change transaction (814_12) is sent to change the date for which transactions? Select all that apply.
814_01
814_05
814_08
814_16
814_18
814_24

## Slide 64: Transaction Solution to Stacking
11.4.1 REP Operating Rule 1: Cancel Move Out
REPs who have a Pending move out and submit a move in (same REP) with an earlier Requested Date are responsible for canceling the Pending move out if that is what the Customer requires (REP manages Customer expectations). If the REP does not cancel the move out, the move out will be allowed to effectuate.
10/5 MVI New Customer
10/9 MVO Existing Customer
10/8
10/7
10/6
MVO transaction from existing customer has left new customer in the dark.
If a REP enrolls a new customer at the same premise and an existing customer has a future dated MVO, if the REP fails to cancel the future dated MVO, the MVO will be executed leaving the new customer in the dark

## Slide 65: Transaction Solution to Stacking
12/1 MVO CR A
12/2
12/4 SWI CR B
12/3
MVO trumps SWI
CR B will need to submit a MVI (814_16) in order to enroll their customer.
ERCOT will reject a Switch Request if the ESI ID is scheduled to be De-energized at ERCOT on the Requested Date.

## Slide 66: Checkpoint Question
A MVI is submitted and scheduled by CR A and then another MVI is submitted later by CR B requesting the same day. Which entity would receive an 814_17 Not First In (NFI) reject?
TDSP
ERCOT
CR A
CR B

## Slide 67: Checkpoint Question
Which entity is responsible for sending an 814_08 cancel when there is a MVO for Customer A pending for 5/5 and a MVI for Customer B pending for 5/1, both with the current REP?
TDSP
ERCOT
Current REP
Another REP

## Slide 68: Checkpoint Question
Which entity is responsible for sending an 814_08 cancel when there is a MVO for Customer A pending for 5/5 and a MVI for Customer B pending for 5/5 both with different REPs?
TDSP
ERCOT
REP for Customer A
REP for Customer B

## Slide 69: Checkpoint Question
What transaction is used to determine the actual end date of a customer?
814_24
814_01
867_03F
814_22

## Slide 70: Move Out to Continuous Service Agreement (CSA)
TDSP
ERCOT
CSA CR
Current CR
810_02
10
814_24
1
814_03
2
814_04
3
814_25
4
814_22
5
867_03F
6
867_03F
7
867_04
8
867_04
9

## Slide 71: Checkpoint Question
What does CSA mean?
Continuous Service Arrangement
Continued Service Arrangement
Continuous Service Agreement
Country Served Agreement

## Slide 72: Checkpoint Question
If there is a Continuous Service Agreement and the customer moves out what transaction places the service back with the CSA?
867_04
814_18
814_01
814_22

## Slide 73: Disconnect for Non-Pay (DNP)*
TDSP
ERCOT
Current CR
650_01
1
650_02
2
* Does not apply to MOU/EC

## Slide 74: Reconnect after DNP*
650_01
1
650_02
2
* Does not apply to MOU/EC
TDSP
ERCOT
Current CR

## Slide 75: Checkpoint Question
What transaction is necessary in order to re-connect a customer after a disconnect for non-payment or cancel a pending disconnect for non-payment?
650_02
814_08
650_01
814_16

## Slide 76: MIS Portal

## Slide 77: Market Information System

## Slide 78: Find ESI ID
Additional information is accessed via an ESI ID #
Or
An address can be used to find the ESI ID number serving that premise
An asterisk (*) serves as a wildcard for address search

## Slide 79: Find ESI ID
STATUS
A – Active
D – Deenergized
I - Inactive
CSA
Does this ESI ID have a Continuous Service Agreement?
REP of Record
Is the view the ROR?
Premise Type
RES – Residential
SMA – Small Non-Res
LAR – Large Non-Res
Open Svc Ord
Are there any current ‘open’ transactions on this ESI ID such as a pending MVO, MVI, etc?
POLR Customer Class
Calculated ERCOT POLR customer classes:
RES – Residential
SMA – Small Non-Res
MED – Medium Non-Res
LAR – Large Non-Res

## Slide 80: Find ESI ID – Additional information

## Slide 81: Find Transactions
Use drop down arrow features to specify dates for the historical transactions needed.
Default will be only the last seven months of activity and maximum of 5 years.

## Slide 82: Find Transactions – MVI w/ permit required
Customer information is contact information – not necessarily premise address
Status will remain In Review until TDSP sends 814_04 to ERCOT scheduling the order

## Slide 83: Find Transactions – MVO w/ date change & cancel
Customer requests to change the MVO date from 7/2 to 6/29 on 6/27. Both ERCOT & TDSP accept the change.

## Slide 84: Find Transactions – MVO w/ date change & cancel – cont.
Customer now requests to cancel the MVO scheduled for 6/29 on 6/27. Both ERCOT & TDSP accept the cancellation.
Reason for cancellation can be found in the hyperlink.

## Slide 85: Find Transactions – MVO to CSA
Customer at premise issues a MVO which activates the CSA. Notification is sent to CSA holder (814_22).
Premise information is provided in the 814_04 and 814_22 including load profile, meter cycle, TDSP Rate Class, and meter information.

## Slide 86: Find Transactions – MVO trumps SWI
Customer issues a SWI on 7/31 for 8/2.
ERCOT will send a loss notification to the Losing REP - an 814_06 with a
CHA indicating ‘customer changed to another CR’

## Slide 87: Find Transactions – MVO trumps SWI
Existing REP issues MVO for customer – customer possibly indicated they wanted to “cancel their service” with their current REP.
ERCOT will review any pending transactions two retail business days prior to the effectuating date.

## Slide 88: Find Transactions – MVO trumps SWI
814_08 is coded CCE –Cancelled due to Move Out
The REP will now have to submit an 814_16 MVI to energize the premise.
With the submittal of the 814_24 MVO, ERCOT proceeds to cancel the 814_01 SWI with an 814_08

## Slide 89: TX SET Implementation Guides w/ Examples
814_20 EDI transaction guide

## Slide 90: TX SET Implementation Guides w/ Examples
814_20 EDI transaction example – meter exchange

## Slide 91: Electronic Data Interface (EDI) Transactions
EDI code is translated by each Market Participant’s system into a readable format.
One does not have to know the code to understand the transaction

## Slide 92: Checkpoint Question
Which transaction changes the meter and/or meter information?
814_09
814_18
814_26
814_20

## Slide 93: Checkpoint Exercise
Provide each transaction number, who the transaction is from and who it is going to, and at the end who the REP of Record is from the scenario flow listed below.
Customer is moving and calls REP B to start service at a new address and REP A is the current REP of Record at that premise …

## Slide 94: Checkpoint Exercise
From
To
814_16
814_03
814_04
814_05
867_02
1
1
2
2
814_06
Move In
Enrollment
Notification Request
Enrollment
Notification Response
CR Enrollment
Notification Response
Historical Usage
(If requested by REP)
Loss Notification
Transaction Type
ERCOT
TDSP
REP A
ERCOT
TDSP
REP B
REP B
REP A
Trans #

## Slide 95: Checkpoint Exercise
814_08
1
1
2
2
1
1
2
2
814_09
814_08
Cancel Request – on day before MVI schedule
Cancel Response - Accept
Transaction Type
ERCOT
TDSP
REP A
ERCOT
TDSP
REP B
REP B
REP A
Customer calls Rep B to cancel the move in the day before the scheduled date…
Trans #
Cancel Request – Response to Cancel Accept
From
To

## Slide 96: Checkpoint Questions
If the Cancel is Rejected, who is the REP of Record?
REP B
BONUS: What is the end result if the Cancel is Rejected?
Inadvertent Gain

## Slide 97: TX SET Working Group

## Slide 98: TX SET Working Group
Texas Standard Electronic Transaction (TX SET) Working Group:
Reports to the Retail Market Subcommittee (RMS)
Analyzes the need for new or modifications to existing electronic transactions
Recommends changes to retail market processes
Works with the ERCOT Flight Administrator to ensure that testing processes and procedures are defined and administered
Maintains the Texas SET Implementation Guides and the Texas Market Test Plan Guide
Collaborates with other Working Groups and Taskforces as directed by RMS
http://ercot.com/committee/txset
Review & Recommend RMGRR153 & 2019 Test Flight

## Slide 99: TX SET Issue Submission Process
Formal method to initiate review of issues
Notes: This process provides Market Participants with a formal way to communicate transactional or market processing issues that should be reviewed and discussed by the Texas SET Working Group for a recommendation and/or resolution.
Issues brought forth through this process may be used by the Texas SET Working Group representatives to develop a Change Control(s) that may be implemented with a future TX SET version.
Market Participants submitting issues to be considered by the Texas SET Working Group should use the Texas SET Issue Form at this link:

## Slide 100: Retail Market Testing
Flight Testing:
  All retail Market Participants are required to test for ERCOT certification
  Three Market flights per year
  End to End test scripts (i.e connectivity, penny test)
Notes: The Texas Market Test Plan (TMTP) applies to Market Participants doing business in the Texas Electric Choice Market.
The purpose of this document is to define the market plan for testing commercial operations systems and business processes to support the Texas Electric Choice Market.
This document covers all testing requirements and procedures between ERCOT and the Market Participants and Point-to-Point testing between Market Participants.

## Slide 101: Retail Market Testing
  Governed by Texas Market Test Plan:
  Maintained by TX SET working group
  Outlines testing processes and requirements
All retail Market Participants must participate in and successfully complete testing as described in Protocol Section 19.8, Retail Market Testing, prior to commencing operations with ERCOT.

## Slide 102: ListServe
http://lists.ercot.com

## Slide 103: Additional resources
ERCOT Client Services Clientservices@ercot.com
ERCOT Mailing Lists http://lists.ercot.com/
ERCOT Nodal Market Protocols http://www.ercot.com/mktrules/nprotocols/
ERCOT Training http://www.ercot.com/services/training/
Market Education Contact Training@ercot.com

## Slide 104: Survey
Scan this QR code to take the course survey!

## Slide 105: Appendix

## Slide 106: ERCOT Retail Market Guide
Other Binding Documents List | 
File Name and Web Link To Documentation | Description
Commercial Operations Market Guide | Supplements the ERCOT protocols and describes the process through which ERCOT market data is translated into financial settlements in the ERCOT market.
Load Profiling Guide | A reference document used by market participants and ERCOT, expands upon and details the responsibilities and processes listed in the ERCOT protocols.
Retail Market Guide | A reference document for rules affecting the competitive retail electric market in Texas.
Texas Data Transport Guides | Provides information on secure data transport utilized by the Retail Electric Market and enabled by the North American Energy Standards Board (NAESB) Electronic Delivery Mechanism (EDM), ebXML and digital certificates.
Texas Market Test Plan | Defines the market plan for testing retail commercial operations systems and business processes to support the Texas Electric Choice Market.
Texas SET Implementation Guides | Provides details of information contained within the electronic transactions used in the competitive retail electric market in Texas.

## Slide 107: Texas SET Swimlanes
Texas SET Swimlanes Scenarios | 
Description | File Name and Web Link to Documentation
TX SET flow documentation for consolidated billing, remittance and dual billing | Billing Scenarios Version February 2017
TX SET flow documentation for beginning and ending continuous service agreements (CSAs) | Continuous Service Agreement Scenarios February 2017
TX SET flow documentation for handling Move In changes and problems | Customer Move In Scenarios June 2012
TX SET flow documentation for handling Move Out changes and problems | Customer Move Out Scenarios February 2017
TX SET flow documentation for handling customer switch request | Customer Switch Scenarios June 2012

## Slide 108: Texas SET Swimlanes
Texas SET Swimlanes Scenarios | 
Description | File Name and Web Link to Documentation
TX SET flow documentation for Disconnect and Reconnect for Non-Pay | Disconnect Reconnect Non Pay Scenarios February 2017
TX SET flow documentation for customer dropped by Competitive Retailer (CR), disconnect for non-pay services request and Mass Transition from defaulting CR to Provider of Last Resort (POLR) | Mass Transition / Acquisition Scenarios June 2012
TX SET flow documentation for handling Switch Hold add and removal | Switch Hold Scenarios June 2012
TX SET flow documentation of how to report unplanned outages | Unplanned Outages Scenarios June 2012

## Slide 109: TX SET Implementation Guides (IG)
The Texas Standard Electronic Transaction (SET) Implementation Guides provide details of information contained within the electronic transactions used in the competitive retail electric market in Texas.
The current Version 4.0 of the Texas SET Implementation Guides contains updates to retail transactions to support the following:
  PUCT Substantive Rule §25.493 Acquisition and Transfer of Customers from one Retail Electric Provider to Another
  PUCT Substantive Rule §25.480 Bill Payment and Adjustments
  PUCT Substantive Rule §25.483 Disconnection of Service
  PUCT Substantive Rule §25.497 Critical Care Customers
  PUCT Substantive Rule §25.126 Amendments Due to Non-Compliant Meters and Meter Tampering in Areas Where Customer Choice Has Been Introduced
  PUCT PROJECT 34610 Implementation Project Relating to Advanced Metering
  Outstanding Change Controls identified and recommended by the Texas SET Working Group
  http://ercot.com/mktrules/guides/txset/current

## Slide 110: Texas SET Implementation Guides
Service Orders, Invoice and Remittance Transactions | 
Transaction and Version | Web Link to Documentation
Texas SET V4.0 650 Service Orders Point to Point | Guides (Jun 11, 2012 – zip – 162 KB) Examples (Jun 11, 2012 – zip – 42.8 KB)
Texas SET V4.0 810 TDSP’s Invoice Point to Point | Guides (Jun 11, 2012 – zip – 95.1 KB) Examples (May 18, 2017 – zip – 39.1 KB) SAC04 (Sep 19, 2016 – xls – 176 KB)
Texas SET V4.0 820 Remittance Advice Point to Point | Guides (Jun 11, 2012 – zip – 60.1 KB) Examples (Sep 22, 2017 – zip – 31.2 KB)

## Slide 111: Texas SET Implementation Guides
Enrollments, Rejects and Usage Transactions | 
Transaction and Version | Web Link to Documentation
Texas SET V4.0 814 Enrollments, MVI, MVO, Create/Maintenance/Retire, Maintain Customer Information | Guides (Jun 11, 2012 – zip – 1.1 MB) Examples (Jun 11, 2012 – zip – 346.7 KB)
Texas SET V4.0 824 Invoice or Usage Reject Notification | Guides (Jun 11, 2012 – zip – 32.4 KB) Examples (Jun 11, 2012 – zip – 11.6 KB)
Texas SET V4.0 867 Monthly and Final Usage, Historical Usage | Guides (Jun 11, 2012 – zip – 176.3 KB) Examples (Jun 11, 2012 – zip – 71.6 KB)

## Slide 112: Texas SET Implementation Guides
Functional Acknowledgement and CR Option 1 Outage Transactions | 
Transaction and Version | Web Link to Documentation
Texas SET V4.0 997 Functional Acknowledgement | Guides (Jun 11, 2012 – zip – 30.8 KB)
Texas SET V4.0 T-Series CR Option 1 Outage Transactions | Guides (Jun 11, 2012 – zip – 102.8 KB)

## Slide 113: Registration and Qualification/Certification
Registration
  Register with ERCOT as a CR (a REP or an opt-in entity) or a NOIE with the form below.
Qualification/Certification
  CRs must be certified by ERCOT. Please read more about Texas Retail Market Testing and the latest test flight.
  REPs must also be certified by the Public Utility Commission of Texas (PUCT). More information on that certification process may be found on the PUCT website at Retail Electric Providers Certification and Reporting.
  http://ercot.com/services/rq/lse/index.html

## Slide 114: Retail Market Testing
Key Documents | 
Description | File Name & Web Link to Documentation
The ERCOT Retail Testing Website is used by Market Participants to become certified in conducting retail market processes within the ERCOT market. | Texas Retail Testing https://etod.ercot.com/
Retail Market Testing Orientation Weblink | Retail Market Testing Orientation
Retail Market Test Environment User Guide | Retail Market Test Environment User Guide
Retail Market Testing Environment ESI IDs | Retail Market Testing Environment ESI IDs

## Slide 115: Retail Market Testing
Key Documents | 
Description | File Name & Web Link to Documentation
Flight status and agenda for conference calls | Daily Agenda
Repository of Market Participants technical and business testing information | Testing Worksheet
Mechanism for recording and tracking flight testing progress. Market Participants update the checklist as transactions/tasks are sent and received | Checklist

## Slide 116: Retail Market Testing
Key Documents | 
Description | File Name & Web Link to Documentation
Testing scenarios to be executed during flight tests. Ability to download script workbook | Scripts
Document repository | File Cabinet
Business and technical contact information for all Market Participants that is populated from each respective Testing Worksheet | Contacts