## Slide 1
RT Constraints Disabled in DAM
Jian Chen
Market Analysis and Validation
CMWG/QMWG
Nov. 12th, 2018

## Slide 2: Contingency Disabled in DAM due to RAS/RAP
From 01/01/2018 to 09/30/2018
Top 5 Contingencies Disabled in DAM due to a RAS/RAP
Contingency | Total Hours Disabled in DAM
DMTSCOS5 | 918
DCPSJON5 | 593
SRDODES8 | 374
DEVRCPS5 | 255
DHCKRNK5 | 205

## Slide 3: RT constraint activated but disabled in DAM
A look at cases when a constraint associated with a contingency was activated in RT while the same contingency was disabled in DAM
Contingency | Constraint | RAS/RAP Name | RT Congestion Rent ($)
DMTSCOS5 | 6437__F | MGSES_TRG_1 | 12,606,029
DHCKRNK5 | 6270__C | DHCKRNK5_TRG_1 | 888,040
DMTSCOS5 | 6474__A | MGSES_TRG_1 | 211,194
DHCKRNK5 | EMSES_MR1H | DHCKRNK5_TRG_1 | 122,843
SFMRRYS5 | 400__A | MNSESB_TRG_1 | 69,377
SSWDMGS8 | LONGWR_ROBY1_1 | ESKOTA_TRIG_1 | 54,452
SSWDMGS8 | 6780__A | ESKOTA_TRIG_1 | 44,622
DHCKRNK5 | 6277__A | DHCKRNK5_TRG_1 | 33,125
DCPSJON5 | 6017__A | MBDSW_TRG_1 | 276

## Slide 4: RT constraint activated with RAS/RAP triggered
Available data:
  RTCA violation table: Only the constraints close to being violated (>98%) are saved with RAS/RAP info, and only post-contingency
  TCM constraint table: The TCM constraints, including an “activated” flag
  Not all TCM activated constraints can be matched to the RTCA violation table
    The activated constraint remains in TCM even it is no longer violated in RTCA
    Manual constraints (e.g., Generic Transmission Constraints) do not come from RTCA
Real Time Contingency Analysis
Transmission Constraint Manager

## Slide 5: RT constraint activated with RAS/RAP triggered
Using the data from 01/01/2018 to 09/30/2018
With 321,748 records of post-contingency constraint activated in TCM, there were 136,350 of them that could be matched to branch violations in RTCA.
Of those 136,350, only 1,118 of them were associated with RAS/RAP information in RTCA.
It should be noted that this list does not cover all the activated constraints which were disabled in DAM. For example, when the constraint DMTSCOS5:6437_F was binding in RT, no RAS was triggered.