## Slide 1
Must-Run Alternative (MRA) Dispatch and Settlement Basis
Ino González
ERCOT
MRA Workshop
Nov 16, 20186

## Slide 2
Dispatch Instructions

## Slide 3: MRA – Dispatch Instructions
  MRA QSE must be able to receive Verbal Dispatch Instructions (VDI)
      MRA Generation Resources will be issued a VDI not a RUC Instruction
      Other MRA resources will be issued a VDI

## Slide 4
MRA Settlements
Standby
Deployment Event
Variable
Contributed Capital Expenditures
Unexcused Misconduct
Service Charge

## Slide 5
Standby Payment

## Slide 6: Standby - Generation Resource
  Payment hr = Price * CCAP * GRCRF * ARF
  Where,
  GRCRF m = (Testing Capacity + Testing Capacity Adjustment) / CCAP
  And,
  Price ($/MW) = Accepted Offer price per hour per month
  CCAP (MW) = Contract Capacity per hour per month
    GRCRF (MW) = Generation Resource Capacity Reduction Factor
    ARF = Availability Reduction Factor per month1
    1See slide 8 for calculation

## Slide 7: Standby - Other Generation & Demand Response
  Payment hr = Price * CCAP * EPRF * ARF
  Where,
  Price ($/MW) = Accepted Offer price per hour per month
  ARF = Availability Reduction Factor per month
    EPRF = Event Performance Reduction Factor
    Availability of EPRF
    If not available for month  Use most recent value from prior month
    If not available for previous month  Set to 1 for current month

## Slide 8: ARF – All Generation and Demand Response
  Availability Reduction Factor (ARF)
  For an MRA register as a Generation Resource
  CMAF m = (MAH) / MH
  Where,
  CMAF = Calculated monthly availability factor
  MAH = Monthly available hours for the month, based on both Availability Plan and telemetry
  MH = Monthly contracted hours in month
  For an MRA not register as a Generation Resource
CMAF m = Described under MRA Availability Measurement and Verification

## Slide 9: ARF – (cont’d)
  For initial settlement
  ARF = 1
  For all other resettlements
  If CMAF m ≥ 95% * TA m  ARF = 1
  If 85% * TA m ≤ CMAF m < 95% * TA m  ARF = CMAF m
  If CMAF m < 85% * TA m  ARF = (CMAF m)^2
  Where,
  CMAF = Calculated monthly availability factor
  TA = Target availability for month

## Slide 10
Deployment Event Payment

## Slide 11: Deployment Event – Generation Resources
  Payment hour = Max { ED Price , (FIP+FA)* PSUFQ } * FLAG / H
  Where,
  ED Price ($/Deployment Event) = Accepted Deployment Offer price per month
    FIP ($/MMBtu) = Fuel Index Price
    FA ($/MMBtu) = Fuel Adder
    PSUFQ (MMBtu) = Proxy startup fuel quantity
    FLAG = Deployment flag indicator
    H (hr) = Instructed hours

## Slide 12: Deployment Event – Other Generation or Demand Response
  Payment hr = Max { ED Price, (FIP+FA)* PSUFQ } * EPRF/ H
  Where,
  ED Price ($/MW) = Accepted Deployment Offer price per month
    FIP ($/MMBtu) = Fuel Index Price
    FA ($/MMBtu) = Fuel Adder
    PSUFQ (MMBtu) = Proxy startup fuel quantity
    EPRF= Deployment Event Performance Reduction Factor
    H (hr) = Instructed hours

## Slide 14: Variable Payment for a Generation Resource1
  a. Contracted Hours with Deployment Instructions
  Payment hr = { GRCVP - RTREV }
  Where,
  GRCVP ($) = Generation Resource calculated variable payment for hour
    RTREV ($) = Existing Real Time revenues for a Generation Resource
1 For hours outside of contract period, MRA GRs shall be settled as other Generation Resources
Objective: Payment hr = Calculated Variable Payment hr (GRCVP hr )

## Slide 15: Variable Payment for a Generation Resource – (cont’d)
  a. Contracted Hours with Deployment Instructions
  Payment hr = { GRCVP - RTREV }
  And,
  GRCVP hr = Max { VPRICE hr , (FIP+FA )* PHR } *Min (RTMG, CCAP/4)
  Where,
  VPRICE ($/MWh) = Accepted Offer variable price per month
  PHR(MMBtu/MWh) = Proxy average heat rate per month
  RTMG(MWh) = Real Time metered generation
  CCAP(MW) = Contracted capacity per hour per month

## Slide 16: Variable Payment for a Generation Resource – (cont’d)
  b. Contracted Hours without Deployment Instructions
  Payment hr = Min { GRCVP, RTREV } – RTREV
Objective: Payment hr = MIN { Variable Payment hr , RT Revenues hr }

## Slide 17: Variable Payment for Other Generation
  a. Contracted Hours with Deployment Instructions
  Payment hr = { CVP - CRTREV }
  Where,
  CVP ($) = Calculated variable payment for hour
    CRTREV ($) = Calculated Real Time revenues for hour
Objective: Payment hr = Variable Payment hr (CVP hr )

## Slide 18: Variable Payment for Other Generation – (cont’d)
  a. Contracted Hours with Deployment Instructions
  Payment hr = { CVP - CRTREV }
  And,
  CVP hr = [Max { VPRICE hr , (FIP+FA )* PHR } * RTVQ]
  CRTREV hr = [Max(0, Min { RTVQ , CCAP/4 } * RTSPP]
  RTVQ = MRAIPF * CCAP/4
  Where,
  RTVQ (MWh) = Real Time variable quantity for the interval
    MRAIPF (none) = MRA Interval Performance Factor
    CCAP (MW) = Contract capacity per hour per month
    PHR (MMBtu/MWh) = Proxy heat rate per month

## Slide 19: Variable Payment for Other Generation – (cont’d)
  b. Contracted Hours without Deployment Instructions
  Payment hr = Min { CVP , CRTREV } – CRTREV
Objective: Compensation hr = MIN { Variable Payment hr , RT Revenues hr }

## Slide 20: Variable Payment for Demand Response
  Contracted Hours with Deployment Instructions
  Payment hr = [Max { VPRICE hr , (FIP+FA )* PHR } * RTVQ]
  RTVQ = MRAIPF * CCAP/4
  Where,
  RTVQ (MWh) = Real Time variable quantity for the interval
    MRAIPF (none) = MRA Interval Performance Factor
    CCAP (MW) = Contract capacity per hour per month
    PHR (MMBtu/MWh) = Proxy heat rate per hour per month

## Slide 21
Contributed Capital Expenditures

## Slide 22: Capital Expenditures Payment (CAPEX)
  Payment hr = MCAPEX m / MH
  Where,
  CAPEX($) = Approved Capital expenses for month
    MH(hr) = Contract hours in a specific month
Objective: Payment hr = Approved CAPEX Expenditures

## Slide 23: Refund of Capital Expenditures – PUCT Order
§25.502. Pricing Safeguards in Markets Operated by the Electric Reliability Council of Texas.
Par. (6)
  “A resource entity that owns or controls a resource providing RMR or MRA service shall refund payments for capital expenditures made by ERCOT in connection with the RMR or MRA service agreement if the resource participates in the energy service markets at any time following the termination of the agreement. ERCOT may require less than the entire original amount of capital expenditures to be refunded to reflect the depreciation of capital over time.”
  Implementation
  Par. (7)
  “ERCOT, through its stakeholder process, shall establish protocols and procedures to implement this subsection.”

## Slide 24: Capital Expenditures Definition
  Standards for General Accepted Accounting Principles or GAAP, which defines CAPEX as:
    A purchase that a company records as an asset, such as property, plant or equipment
    Purchases must have an expected useful life of more than one year to be considered CAPEX
    Costs can be capitalized if asset value is increased or useful life extended
    Companies can spread the cost over life of asset instead of all at once (expense)
    Assets deliver a probable future benefit

## Slide 25: Capital Expenditures Evaluation
  Evaluation Process:
  MRA QSE submits CAPEX budget by month
    ERCOT reviews budgeted costs to ensure costs consistent with GAAP
      QSE and ERCOT discuss budget
    If approved, ERCOT makes a payment
    After costs are incurred, QSE representing MRA files invoices with ERCOT describing actual capital expenditures
    If required, ERCOT will re-calculate book value straight-line depreciation schedule
    If at the end of the MRA Agreement resource remains operating in the energy or Ancillary Service market,
      ERCOT claws back the Book Value, else
      Salvage Value

## Slide 26: Capital Expenditures Evaluation – (cont’d)

## Slide 27
Unexcused Misconduct

## Slide 28: Unexcused Misconduct
  MRA Misconduct Events
    A “Misconduct Event” means any MRA Contracted Hour during which the MRA, in a deployment event, is directed to but does not make available to ERCOT the power injection or Demand response in the amount shown in the MRA Availability Plan.
    ERCOT will assess a single charge to the QSE for each Operating Day on which one or more Misconduct Event occurs.
    The QSE may be excused by ERCOT from a Misconduct Event charge if ERCOT determines, in its discretion, that the Misconduct Event was not due to intentionally incomplete or inaccurate reporting to ERCOT regarding the availability of the MRA.

## Slide 29: Unexcused Misconduct
  Charge hr = $10,000 * UMFLAG / CH
  Where,
  UMFLAG (none) = Unexcused Misconduct flag for the day
    CH (hr) = Contract hours for the day

## Slide 30
MRA Service Charge

## Slide 31: Service Charge
  Charge hr = {Standby + Deployment + Variable + CAPEX + Unexcused} * HLRS
  Where,
  Standby ($) = Total Standby payment per hour
  Deployment ($) = Total Deployment payment per hour
    Variable ($) = Total Variable payment per hour
    CAPEX ($) = Total Capital Expenditures payments per hour
    HLRA (none) = QSE hourly load ratio share for hour

## Slide 32: The End
Questions?