## Slide 1
RAS modeling in DAM
Carrie Bivens
Manager, Forward Markets
December 3, 2018

## Slide 2: Network Security Monitor (NSM) overview

## Slide 3: Current RAS modeling in DAM
Model the 1st level RAS trigger only
If the RAS triggers in a contingency case, then assume the RAS actions fix any overload and don’t send contingency constraints to NCUC for that hour
  After 5 iterations, if the RAS is triggered then the contingency remains disabled for all future NSM iterations
If the RAS triggers in the base case, then the RAS itself is disabled and constraints are sent to NCUC as normal
  Otherwise all contingencies would be disabled

## Slide 4: RENA issue
From 01/01/2018 to 09/30/2018, DMTSCOS5 was the top contingency disabled in DAM by RAS but binding in RT, causing ~$12M in congestion rent. This contingency was disabled due to the MGSES_TRG_1 RAS.
What happens:
  Thousands of MWs of PTPs sourcing/sinking at settlement points in the West are awarded in the early iterations of DAM before constraints are developed to constrain them. These large MW awards cause huge violations under the DMTSCOS5 contingency. One of the violations is a line monitored by the MGSES RAS.
  MGSES RAS is triggered due to the high MW flow, which then disables DMTSCOS5 and no other contingency in later iterations is able to constrain the PTP awards down to a level where the RAS stops triggering -- for these hours, DMTSCOS5 will continue to be disabled.
  If DMTSCOS5 were able to be analyzed, other constraints in the system, such as the one that showed up in RT, would have developed and constrained the awards in the area such that it would not trigger the MGSES RAS.

## Slide 5: Options
Option #1 – Manage with the watchlist
DAM uses a watchlist to pre-prime the solution with constraints that are frequently binding (improves solution time)
Adding constraints binding in RT but disabled in DAM due to RAS triggering to the watchlist would prevent inaccurate constraint sets in future DAM runs
  DAM operators would monitor RT constraints and update the watchlist after-the-fact
Pro | Con
Enhancement to existing processes | Reactive
Based on correct topology | Requires system change to persist the watchlist constraints for contingency constraints

## Slide 6: Options
Option #2 – Refine list
Use engineering judgment to identify all transmission elements that are protected by the RAS, input those elements and then if RAS is triggered, do not send constraints on that transmission element to NCUC
  For CRR, this is done per auction (twice a month). However, DAM would NOT be able to do this daily for topology that changes hourly (CIM+outages), so would have to be based on normal status.
  List will be updated, if required, based on observations of outcomes in RT and regular DAM constraint analysis
*could do option #1 now, then #2 upon system implementation
Pro | Con
Similar to but more accurate than CRR implementation | Requires system change to model the list of RAS-protected elements and other current RAS modeling features
Proactive in normal cases | Reactive in outage cases
 | Adds a new study for DAM operators to perform with each CIM load, and adds work day-of when RAS are outaged

## Slide 7: Options
Option #3 – CRR implementation
Use engineering judgment to identify all transmission elements that are protected by the RAS, and then change the emergency ratings to 9,999 MW
  Effectively, those transmission elements will not be binding in any contingency case
  For CRR, this is done per auction (twice a month). However, DAM would NOT be able to do this daily for topology that changes hourly (CIM+outages), so would have to be based on normal status.
  If helpful, ERCOT can provide an analysis of CRR overselling due to this implementation at a future meeting
Pro | Con
DAM and CRR in alignment | Would be incorrect in outage cases
Can be implemented without a system change | Assumes that the RAS action resolves all contingency constraints for that element in RT
 | Assumes that the RAS will always trigger before the contingency constraint would be become binding in RT
 | Adds a new study for DAM operators to perform with each CIM load, and adds work day-of when RAS are outaged

## Slide 8: Options
Option #4 – Delay RAS trigger evaluation
Don’t evaluate RAS in initial iterations, delay until iteration X (TBD)
  Would curtail awards with full constraint set early and only trigger RAS afterwards
  Still evaluating this option
Pro | Con
Based on correct topology | Requires system change (minimal)
Proactive | May not resolve some cases

## Slide 9: Options
Option #5 – Model the RAS action
Modify software to model the RAS action itself
Pro | Con
Would be in best alignment with RT | Likely very expensive
Programmatic | May not be able to complete DAM within current timeline
 | Complex implementation for certain types of RAS due to DAM Energy Only Offers/Bids and PTPs