## Slide 1
Overview of NPRR 885 Demand Response and DG Participation in an MRA
Carl L Raish
Principal Load Profiling and Modeling
DSWG Meeting – December 14, 2018

## Slide 2: Demand Response & Other Generation MRAs
MRA Resource Types
  Demand Response – weather sensitive and non-weather sensitive
  Other Generation – registered or unregistered that is not dispatchable by SCED
  Co-located Demand Response and Other Generation MRA
  Aggregated MRA consisting of multiple MRA Sites … all sites of the same type
  MRA that is not aggregated (not referred to as an MRA Site)
  Demand Response MRA must qualify for a ‘Default’ baseline.
Offers from QSEs only
  QSEs may submit more than one offer
  ERCOT may award more than one offer to a QSE
  An MRA and an MRA Site may not be included in more than one offer
  No clearing price … payment based on offer
  Minimum offer 5 MW
  QSE must be capable of receiving XML and VDI instructions from ERCOT
  If a Load Resource, the QSE representing the LR is the only QSE that can offer it as MRA

## Slide 3: Demand Response & Other Generation MRAs
MRA metered with AMS or EPS meter subject to qualification testing at least 10 days prior to the first day of MRA contracted service
Other MRAs – 45 days
Availability plan submitted and updated continuously for each contracted hour for the current operating day and the next 6 operating days.
My not submit DAM offers or carry AS responsibility for any MRA contracted hours
Offer information Required
  Capacity, months and hours offered … for an aggregated MRA, the capacity allocated to each MRA site for all months and months
  Resource ID, ESIID, Unique Meter ID
  The MRA Standby Price ($/MW/Hr)
  Capital Expenditure, if any
  MRA Event Deployment Price ($/deployment)
  Ramp Period
  MRA Variable Price ($/MW/Hr)
  Target availability
Only one MRA deployment event per day … no other provision for a recovery period

## Slide 4: Demand Response & Other Generation MRAs
Preliminary review of Demand Response MRAs
  Similar to the ERS ERID Process … optional but recommended
  Schedule established in MRA RFP
  ERCOT will perform validations on the MRA similar to ERS
  ERCOT will provide availability using actual meter data and effective actual load (adjusted using shift factors) and baseline information similar to ERS
  Substation information for each site in a competitive area
Substitutions
  Similar to the ERS Substitutions
  Substitution is subject to ERCOT approval and the same obligations as the original MRA
  Effective for the whole day
  Must provide the equivalent reliability benefit as the original
  For a month in which both the original MRA and one or more substitutions are in effect, payment to QSE will be based on the combined performance
Dispatch
  By VDI
  ERCOT will consider the ramp period for the MRA and may issue the instruction prior to contracted hours so the capacity is fully deployed at the beginning of the obligation

## Slide 5: Demand Response & Other Generation MRAs
Telemetry Requirements
  Other Generation: Status, HSL, LSL, Current Output Level, Gross Reactive Power, Net Reactive Power
  Demand Response MRA: NPC and LPC
Metering Requirements
  Similar to the ERS
  For MRAs/MRA Sites in NOIE areas … QSE must arrange for NOIE TDSP to send data to ERCOT
  Meter data will be adjusted for deemed actual distribution losses as with ERS

## Slide 6: Demand Response & Other Generation MRAs
Availability (comments to use ‘effective’ quantities will be submitted by ERCOT)
  The ratio of available intervals to number of contracted intervals
  Evaluated on monthly basis, with reports provided by ERCOT within 45 days after the end of the month
  Intervals with missing meter data will be treated as unavailable
  Based on contracted intervals and the most current Availability Plan
  Evaluated on monthly basis, with reports provided by ERCOT within 45 days after the end of the month
  Intervals during deployment events and tests as well as the intervals on that day following the recall are excluded from the availability calculation
Demand Response MRA Availability
  Interval deemed available if effective actual load is greater than 95% of the effective contract capacity and if the availability plan indicates the interval is available
  For a non-aggregated MRA, effective quantities are multiplied by the absolute value of the MRA shift factor
  For an aggregated MRA, effective quantities are the sum of the MRA Site quantity weighted by the absolute value of the MRA shift factor
Other Generation MRA Availability
  Interval deemed available if export to the grid is zero and the availability plan indicates the interval is available

## Slide 7: Demand Response & Other Generation MRAs
Event Performance (comments to use ‘effective’ quantities will be submitted by ERCOT)
  Ramp Period is specified by the QSE and is part of the MRA
  MRA Deployment Period starts at the later of the end of the Ramp Period or the beginning of the MRA Contracted hours and ends at the earlier of the last full interval prior to the recall instruction or at the end of the last contracted hour
  Within 45 days after a test or deployment event ERCOT will provide a performance report to the QSE
Event Performance Calculations (Demand Response MRA)
  MRAEPRF: time weighted average of MRAIPF for the event/test
  MRAIPF: Max(Min(((Effective Base_MW i – Effective Actual_MW i) / (IntFrac i
* Effective Contracted_Capacity_MW i)),1),0)
  Effective Base_MW: For aggregated MRA, the sum of the product of the absolute value of the MRA Site Shift Factor and the MRA Site baseline MW. For non-aggregated MRA, the product of the absolute value of the MRA Site Shift Factor and the MRA baseline MW.
  Effective Actual_MW: For aggregated MRA, the sum of the product of the absolute value of the MRA Site Shift Factor and the MRA Site metered MW. For non-aggregated MRA, the product of the absolute value of the MRA Site Shift Factor and the MRA metered MW.
  Effective Contracted_Capacity_MW: For aggregated MRA, the sum of the product of the absolute value of the MRA Site Shift Factor and the MRA Site portion of the MRA Contracted Capacity. For non-aggregated MRA, the product of the absolute value of the MRA Site Shift Factor and the MRA Contracted Capacity
  IntFrac: the fraction of the interval in the deployment period

## Slide 8: Demand Response & Other Generation MRAs
Event Performance Calculations (Other Generation MRA)
  MRAEPRF: time weighted average of MRAIPF for the event/test
  MRAIPF: Max(Min(((Effective Base_MW i – Effective Actual_MW i) / (IntFrac i
* Effective Contracted_Capacity_MW i)),1),0)
  Effective Base_MW: For aggregated MRA, the sum of the product of the absolute value of the MRA Site Shift Factor and the MRA Site MW injection to the ERCOT system. For non-aggregated MRA, the product of the absolute value of the MRA Site Shift Factor and the MRA MW injection to the ERCOT system.
  Effective Actual_MW: always set to zero.
  Effective Contracted_Capacity_MW: For aggregated MRA, the sum of the product of the absolute value of the MRA Site Shift Factor and the MRA Site portion of the MRA Contracted Capacity. For non-aggregated MRA, the product of the absolute value of the MRA Site Shift Factor and the MRA Contracted Capacity
  IntFrac: the fraction of the interval in the deployment period

## Slide 9: Demand Response & Other Generation MRAs
Event Performance (continued)
  If the MRAEPRF < 0.95 for a test or event, or the MRAIPF for the first full interval of the deployment period < 0.95 the MRAIPF values are multiplied by an adjustment factor, such that the adjusted MRAEPRF is equal to the square of the original value
  For a weather sensitive Demand Response MRA, the adjustment above is not applied if the normalized peak demand reduction across the contracted hours is greater than 95% of the largest contracted capacity offered for any hour
Co-located Demand Response and Other Generation
  For an Aggregated Demand Response MRA each site is also in the Aggregated Other Generation MRA
  A non-aggregated Demand Response MRA is also in an Other Generation MRA
  The contracted hours are the same
  The Demand Response MRA is not classified as a Weather Sensitive MRA
  If co-located, event and test performance will be calculated as a combination … the Effective Base_MW, Effective Actual_MW and Effective Contracted Capacity will be summed and the MRAEPRF for the combination will be deemed to apply to both the Demand Response MRA and the Other Generation MRA

## Slide 10: Demand Response & Other Generation MRAs
MRA Testing
  MRA will be tested prior to the initial MRA Contracted Month
  Non-weather sensitive MRAs subject to testing once per month
  Weather sensitive MRAs subject to testing twice per month
  No testing will be conducted during a contracted month following an MRA deployment
  Substitution is subject to testing in a month regardless of tests done in the month prior to the beginning of the substitution
Misconduct Event
  An hour during an MRA deployment event in which the MRA does not make available to ERCOT the injection to the ERCOT system or a load reduction as specified in the availability plan

## Slide 11: Demand Response & Other Generation MRAs
Settlement to be discussed at a later meeting if desired

## Slide 12: Questions?
ON
OFF
craish@ercot.com 512/248-3876