## Slide 1
Annual TAC Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2018
David Maggio
Sr. Manager, Market Analysis & Validation
Technical Advisory Committee
ERCOT Public
January 30, 2019

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: RUC-Committed Resource-Hours in 2018
(*) - The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, or still being off-line for some portion of the RUC-committed hours or Resources not following RUC instructions.
 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 642 | 140 | 502
Effective Resource-Hours (*) |  |  | 
Total Count | 613 | 137 | 476
Average LSL | 52 | 64 | 50
Average LDL | 63 | 132 | 51
Average BP | 70 | 149 | 55
Average HSL | 107 | 204 | 90

## Slide 4: RUC Commitment Reasons
613 effective RUC resource-hours in 2018
  504 resource-hours (82%) for local thermal congestion or voltage concerns
  109 resource-hours (18%) for system capacity
There were no resource-hours of commitment for Ancillary Service shortages, system inertia or extreme cold weather/startup failures
137 effective resource-hours (22%) were successfully bought back
  This value is lower than last year (31% bought back in 2017)

## Slide 5: RUC-Committed Effective Resource-Hours

## Slide 6: May 2018 Details
373 effective RUC resource-hours in May alone (59% of annual total), with the vast majority in the first half of the month
333 effective resource-hours in the first part of May were for Permian Basin Resources, to help resolve local issues associated with high load in the area as well as transmission outages
  These hours alone account for 54% of the annual total.
Excluding the Permian Basin Resources in May, 127 effective resource-hours (45% of the remaining 280 resource-hours in 2018) were successfully bought back for the year.
  This percentage is higher than last year (31% bought back in 2017).

## Slide 7: RUC-Committed Resources Dispatched above LDL
When Resources did not successfully opt out, there were 108 resource-hours when the Resource was dispatched above its LDL.
  For all of these resource-hours, the RUC-instructed Resource was mitigated.
  For 11 of these resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 97 of these resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
NPRR744 (implemented 6/1/2017) remedied a historical issue in which submitted Energy Offer Curves could be below the offer floor.

## Slide 8: Reliability Deployment Price Adders
Month of 2018 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
Jan | 33 | 1.94
Feb | 0 | 0
Mar | 3 | 0.33
Apr | 3 | 0.24
May | 265 | 1.68
Jun | 0 | 0
Jul | 0 | 0
Aug | 15 | 2.27
Sep | 4 | 2.36
Oct | 11 | 5.26
Nov | 16 | 1.91
Dec | 14 | 2.36

## Slide 9: RUC Make-Whole and Claw Back 2015 - 2018
** 2018- $457K in Make-Whole paid out. Only $0.35 was uplifted to Load.

## Slide 10: RUC Improvements in 2018
OBDRR002, ORDC OBD Revisions for PUCT Project 47199, was implemented in May 2018 (R3)
  Removes ONRUC capacity from RTOLCAP calculation for ORDC price adder
NPRR864, RUC Modifications to Consider Market-Based Solutions, was implemented in October 2018 (R5)
  Scales down the startup and minimum generation costs used by the RUC optimization engine for Resources with Cold Start Time <= 1 hour so that the RUC optimization engine prefers to use these Resources over longer startup time Resources, even if their actual costs are higher than other alternatives

## Slide 11: Conclusions
In 2018, 642 instructed RUC resource-hours resulted in 613 effective RUC resource-hours.
  As compared to 562 and 534 for all of 2017, respectively
  22% of effective resource-hours were bought back
  Over half of the annual total resource-hours were for Permian Basin Resources during the first half of May, to help resolve local issues associated with high load in the area as well as transmission outages.
The total RUC make-whole amount was ~$0.46M.
  Almost exclusively covered through capacity-short charges
ERCOT continues to work with stakeholders on issues and questions related to RUC.

## Slide 12: Appendix

## Slide 13: RUC-Committed Effective Resource-Hours by Opt Out Status
Month | 2015 | 2016 | 2017 | 2018
Jan | 8 | 33 | 7 | 46
Feb | 0 | 28 | 20 | 0
Mar | 0 | 47 | 14 | 0
Apr | 8 | 62 | 47 | 3
May | 71 | 74 | 33 | 333
Jun | 9 | 111 | 52 | 0
Jul | 6 | 222 | 39 | 0
Aug | 10 | 83 | 76 | 15
Sep | 75 | 111 | 54 | 4
Oct | 75 | 155 | 16 | 11
Nov | 0 | 20 | 8 | 50
Dec | 0 | 0 | 5 | 14
Month | 2015 | 2016 | 2017 | 2018
Jan | 0 | 11 | 2 | 0
Feb | 0 | 12 | 0 | 0
Mar | 0 | 0 | 0 | 0
Apr | 0 | 11 | 0 | 0
May | 6 | 57 | 20 | 40
Jun | 45 | 165 | 76 | 21
Jul | 5 | 96 | 27 | 4
Aug | 6 | 49 | 23 | 28
Sep | 9 | 59 | 12 | 16
Oct | 64 | 13 | 0 | 15
Nov | 0 | 0 | 3 | 12
Dec | 0 | 0 | 0 | 2
Did Not Opt Out
Opted Out

## Slide 14: RUC Make-Whole and Claw Back 2015-2016
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2015 | 2016 | 2015 | 2016 | 2015 | 2016 | 2015 | 2016 | 2015 | 2016
Jan | 0 | -29 | 0 | 29 | 0 | 0 | 23 | 0 | 0 | 499
Feb | 0 | -4 | 0 | 4 | 0 | 0 | 0 | 38 | 0 | 192
Mar | 0 | -13 | 0 | 13 | 0 | 0 | 0 | 608 | 0 | 212
Apr | -5 | -70 | 5 | 70 | 0 | 0 | 0 | 3 | 114 | 1673
May | -240 | -45 | 240 | 45 | 0 | 0 | 3 | 88 | 941 | 1569
Jun | -16 | -176 | 16 | 176 | 0 | 0 | 0 | 115 | 203 | 2229
Jul | -2 | -372 | 2 | 372 | 0 | 0 | 10 | 156 | 33 | 3341
Aug | -13 | -138 | 13 | 138 | 0 | 0 | 0 | 2 | 318 | 2427
Sep | -139 | -240 | 139 | 240 | 0 | 0 | 175 | 46 | 1688 | 2447
Oct | -76 | -153 | 76 | 153 | 0 | 0 | 126 | 81 | 1098 | 3581
Nov | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 275 | 0 | 145
Dec | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 15: RUC Make-Whole and Claw Back 2017-2018
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2017 | 2018 | 2017 | 2018 | 2017 | 2018 | 2017 | 2018 | 2017 | 2018
Jan | 0 | -42 | 0 | 42 | 0 | 0 | 228 | 385 | 0 | 1227
Feb | -7 | 0 | 7 | 0 | 0 | 0 | 0 | 0 | 204 | 0
Mar | -79 | 0 | 79 | 0 | 0 | 0 | 0 | 0 | 467 | 0
Apr | -175 | 0 | 175 | 0 | 0 | 0 | 0 | 4 | 1387 | 0
May | -21 | -102 | 21 | 102 | 0 | 0 | 640 | 2372 | 208 | 2845
Jun | -40 | 0 | 40 | 0 | 0 | 0 | 163 | 0 | 490 | 0
Jul | -57 | 0 | 57 | 0 | 0 | 0 | 34 | 0 | 627 | 0
Aug | -121 | -35 | 121 | 35 | 0 | 0 | 15 | 1 | 873 | 523
Sep | -25 | -24 | 25 | 24 | 0 | 0 | 79 | 0 | 759 | 205
Oct | -4 | -24 | 4 | 24 | 0 | 0 | 47 | 213 | 159 | 538
Nov | -10 | -230 | 10 | 230 | 0 | 0 | 25 | 79 | 147 | 0
Dec | -2 | 0 | 2 | 0 | 0 | 0 | 0 | 20 | 77 | 0