## Slide 1
Resource Definition Task Force
Load Resources Review
Feb 2019

## Slide 2: Agenda
Brief review of Resource Definition Task force (RTF) work on Generation Resources
Update on Load Resource Definitions
  Existing Framework
  NPRR863 Framework
  Resource Options requested by Stakeholders.
  Other responsive loads (small l, small r)
  Proposed Load Resource Framework

## Slide 3: Original Generation Resource Definition Framework

## Slide 4: Proposed Generation Category Nomenclature – using existing requirements
Transmission Generation Resource (TGR) Transmission-connected Registered with ERCOT as GR Participates in the market SCED A/S Modeled in ERCOT systems Telemetry, etc. Settled Nodally I |  | Settlement Only Transmission Generator (SOTG) Transmission-connected less than 10 MW Registered with ERCOT as SOG Settled for exported energy only Intermittent sources will typically export based on fuel availability. Self-dispatched may choose to export based on prices Modeled in ERCOT systems Reliability systems only Not scheduled/dispatchable Settled - Load Zone II | Settlement Only Transmission Self-Generator (TSG) Transmission-connected Registered with PUC as a Self-Generator and registered with ERCOT as SOG May occasionally export, but does not generate with the intent to sell at wholesale If it exports, then settled for exported energy only Continuous exports will be re-evaluated for TGR Modeled in ERCOT systems Reliability systems only Not scheduled/dispatchable Settled - Load Zone III |  | 
Distribution Generation Resource (DGR) Distribution connected Registered with ERCOT as GR >10 MW require to register as GR Participates in the market SCED A/S Pseudo-Modeled in ERCOT systems Future--Modeling light? Telemetry, etc. Settled Nodally IV |  | Settlement Only Distribution Generator (SODG) Distribution connected but less than 10 MW Registered with ERCOT as SOG Settled for exported energy only Intermittent sources will typically export based on fuel availability. Self-dispatched may choose to export based on prices Mapped in ERCOT systems Not scheduled/dispatchable Telemetry not required Settled - Load Zone V | Unregistered Distribution Self-Generator (UDSG) Distributed generation greater than 1 MW co-located with larger load, but smaller than minimum facility load. Registered with PUC as a Self-Generator but not registered with ERCOT May not export—otherwise must register with ERCOT as SODG. Neither Mapped nor modeled in ERCOT systems (future mapping?) No ERCOT settlement policy since no exports. VI | Unregistered Distributed Microgenerator* (UDMG) Distribution connected less than 1 MW No requirement for registration Reported by DSP per PUCT 25.211(n) (competitive choice) Reported by NOIEs per ERCOT protocol 10.2.2.1.b(ii) for 50kW -1 MW Not reported by NOIEs for <50kW Neither Mapped nor modeled in ERCOT systems (future mapping of accumulations?) ERCOT settles as negative load in competitive choice areas once meter configuration updated to DG No ERCOT settlement policy for NOIE areas. VII | 
 | **Settlement Only means that the generator may not participate in Ancillary Services Market, RUC, SCED, or make Energy OffersNote: Transmission connected resources are required to be modeled in ERCOT NMMS systems. Studies are determined based on requirements for size and resource category type. *Microgenerator definition may need resolution with PUC |  |  |  | 

## Slide 5: Proposed Generation Resource Definition Framework
NPRR889 RTF-1
NPRR921 RTF-2

## Slide 6
Load Resources
Non-Controllable Load Resources*
Controllable Load Resources
UFR @ 59.7 Hz Required
Distribution Connected Loads Only
Single Site
Aggregate Load Resource (ALR)
Each site < 10 MWs of Demand Response Capability and all sites located in same Load Zone
Current Protocol Load Resource Framework
* Also referred to in the Protocols as Load Resource controlled by high-set under-frequency relay, Load Resource other than Controllable Load, and other variations

## Slide 7
Current Markets For Load Resources
Regulation
Responsive Reserve Service
Non-Spin
Controllable Load Resource (SCED Dispatched)
Controllable Load Resource w/ Gov Resp & LFC base points)
Controllable Load Resource w/ Gov Resp & LFC (SCED Dispatched)
Non-Controllable Load Resource (UFR-30 cycle)
Real-Time Energy Market
SCED Qualified Controllable Load Resource
Aggregate Load Resource (SCED Dispatched)
Controllable Load Resource providing FRRS

## Slide 8
Controllable Load Resource w/ Gov Resp & LFC basepoints
Controllable Load Resource (SCED Dispatched)
Real-Time Energy Market
SCED Qualified Controllable Load Resource
NPRR 863 Framework
Controllable Load Resource (SCED Dispatched)
Aggregate Load Resource (SCED Dispatched)
Basic Load Resource
UFR Load Resource (30 cycle)
UFR Load Resource (30 cycle)
Auto Dispatch Controllable Load Resource (30 cycle)
UFR Load Resource (15 cycle)
Auto Dispatch Controllable Load Resource (15 cycle)
Controllable Load Resource w/ Gov Resp & LFC base points
Controllable Load Resource providing FRRS
Existing Load Resource Type
New Load Resource Type

## Slide 9
List of Load Resource Types by Qualification Badge
  Controllable Load Resource w/ Gov. Resp. & LFC basepoints
  UFR Load Resource (15 cycle)
  Auto Dispatch Controllable Load Resource (15 cycle)
  UFR Load Resource (30 cycle)
  Auto Dispatch Controllable Load Resource (30 cycle)
  Controllable Load (SCED Dispatched)
  Basic Load Resource
  Aggregate Load Resource (SCED Dispatched)
  SCED Qualified Controllable Load Resource
  Grouped by similar qualification Badge
  Controllable Load Resource w/ Gov. Resp. & LFC basepoints
  Controllable Load Resource (SCED Dispatched)
  Aggregate Load Resource (SCED Dispatched)
  SCED Qualified Controllable Load Resource
  UFR Load Resource (15 cycle)
  Auto Dispatch Controllable Load Resource (15 cycle)
  UFR Load Resource (30 cycle)
  Auto Dispatch Controllable Load Resource (30 cycle)
  Basic Load Resource
Similarities between Qualification
Controllable Loads
UFR Controlled w/ Manual Deployment
Manual Deployment only

## Slide 10
Framework - Minimal Changes
Controllable Load Resource
Load Resource
UFR Load Resource
Basic Load Resource
Responsive Reserve Service
FFR
UFR
Fast Frequency Response Responsive Reserve Service
Fast Response Regulation Service
Register as a Basic Load Resource and deployed through Verbal Dispatch Only to provide ECRS,
Register as a UFR Load Resource with either a 15 cycle (FFR) or 30 cycle(UFR) response time and may qualify to provide ECRS or Responsive Reserve Service.
Regulation Service
Primary Frequency Response
ECRS
Non Spin (SCED Qualified)
Real-Time Energy Market (SCED qualified)
Register as a Controllable Load Resource to qualify to provide one or more of the following: FRRS, Regulation Service, Fast Frequency Response, Primary Frequency Response, ECRS, Non-Spin, and Real-Time Energy Market. May be an aggregation for providing Non-Spin only.
ECRS
ECRS

## Slide 11
Basic Load Resource
UFR Load Resource
Load Resources
SCED LR
Frequency Responsive LR
Reserve LR
Primary Frequency Responsive
Fast Response Regulation Service
ECRS
Non-Spin
Framework Option 1- Modified Merit Badge
ECRS
Responsive Reserve Service
FFR
UFR
ECRS
RT Energy Market
Regulation Service
Fast Frequency Response Regulation Service

## Slide 12
Basic Load Resource
UFR Load Resources
Load Resources
SCED LR
30 Minute Reserve Controllable LR
Responsive Reserve Service
Fast Response LR
Balancing Controllable LR
10 Minute Reserve Controllable LR
Framework Option 2 - Full Merit Badge
ECRS
ECRS
ECRS
Non-Spin
Fast Response Regulation Service
Fast Frequency Response Regulation Service
Regulation
PFR
RT Energy Market

## Slide 13
Other Responsive loads - *not* Load Resources
*Remotely controlled thermostats, etc, etc.

## Slide 14
Proposed Load Resource Framework
*attribute

## Slide 15
Combined Proposed Resources Framework