## Slide 1: FOR DISCUSSION Study Methodology for Interconnects (With regards to NPRR913)
(February 20, 2019)

## Slide 2: NPRR913 Generator Interconnection Neutral Project Classification
Facilities needed to connect a new Generation Resource to a substation on the existing ERCOT Transmission Grid and any projects needed to ensure that the Generation Resource can reliably generate at capacity under P0, P1, and P7 conditions of the NERC Reliability Standard addressing Transmission System Planning Performance Requirements, other than a P1 or P7 contingency loss of a radial generator tie line, assuming other Generation Resources with a shift factor greater than 2% on an overloaded facility can be redispatched or have their commitment status changed in the study case.

## Slide 3: FOR DISCUSSION Study Methodology
Study Base Case(Same case(s) used for Steady State Study):
  Use SSWG Case(s) that are indicative of the New Resource’s COD
  Check the accuracy of the topology and add or remove transmission projects based on their approval status
  Check that Generation Resources that meet Planning Guide Section 6.9 are appropriately modeled and unit retirements are captured
  Ensure all the nearby resources are modeled and dispatched appropriately
  Create study base case scenarios: New Resource not modeled and modeled at full net output.
  Define monitored elements/system

## Slide 4: FOR DISCUSSION Study Methodology (Cont.)
  Run simulation to compute Generation shift factors (distribution factors) for P0, P1 & P7:
    Identify elements that violate planning criteria; (i.e., exceed their thermal rating with New Resource at full net output)
    For an overload element identify those Generators with shift factors greater than 2%
    Redispatch those Generators to determine if the full net output of the New Resource can be achieved
    If not, then determine and test possible upgrade(s) necessary to achieve full net output from the New Resource

## Slide 5: Questions/Issues to Address
  1….