## Slide 1
PDCWG Report to ROS
Chair: Chad Mulholland, NRG
Vice Chair: Jimmy Jackson, CPS
ROS
March 7th, 2019

## Slide 2: Report Overview & Notes
Report Overview
  Meeting Minutes
  BAL-001-TRE-1 FMEs & IMFR
    1 FME in the month of January
  Frequency Control Report

## Slide 3: Meeting Minutes
PDCWG Meeting 2/13/19
  Southern Cross DC Tie - Preliminary Findings in ERCOT Frequency Overshoot Study/Impacts to RRS
    Topic generated a great deal of discussion in PDCWG
    Southern Cross is expecting to file a written response to ERCOT’s analysis findings for review by the stakeholders
  NOGRR Revisions for to Align with NPRR863
    PDCWG participants made minor comments and suggestions, but the group seems to be approaching consensus on text for the NOGRR
  RRS Limits for NPRR863
    PDCWG recommends calculation of RRS offer/responsibility limits based on generator historical performance should:
    not account for generator MW ramping (up or down) prior to frequency events (this differs from BAL-001-TRE-01)
    reflect only the Initial PFR assessment (R9 from BAL-001-TRE-01), not Sustained PFR
    utilize the same 12 month rolling average PFR evaluation scoring, with an 8 event evaluation minimum, similar to BAL-001-TRE-01
    might utilize median of rolling average rather than average of rolling average scores
    scoring would be updated and published quarterly
  Regulation & Frequency Control Reports

## Slide 4: Frequency Measurable Events Performance

## Slide 5: Frequency Measurable Events
There was 1 FME in January
  1/27/2019 06:03:05
    Loss of 510 MW
    Interconnection Frequency Response: 1,086 MW/0.1 Hz
    10 of 43 Evaluated Generation Resources had less than 75% of their expected Initial Primary Frequency Response.
    10 of 43 Evaluated Generation Resources had less than 75% of their expected Sustained Primary Frequency Response.

## Slide 6: Interconnection Minimum Frequency Response (IMFR) Performance
IMFR Performance currently 1038.82 MW/0.1Hz
Frequency Response Obligation (FRO): 381 MW/0.1 Hz

## Slide 7: Frequency Control Report
January 2019

## Slide 8: CPS1 Performance

## Slide 9: RMS1 Performance of ERCOT Frequency

## Slide 10: Frequency Profile Analysis

## Slide 11: Time Error Corrections

## Slide 12: ERCOT Total Energy

## Slide 13: ERCOT Total Energy from Wind Generation

## Slide 14: ERCOT % Energy from Wind Generation

## Slide 15
Questions?