## Slide 1
2019 Summer Peak and Fall Off-Peak Voltage Profile Kick Off
Operations Planning
Voltage Profile Working Group (VPWG)
March 5th, 2019

## Slide 2
Agenda
SSWG Case and Contingency Information
Change Submissions
Voltage Profile Conversations
Voltage Profile Schedule
Additional Information

## Slide 3: SSWG Case and Contingency Information
Cases:
  18SSWG_2019_SUM1_U2_Final_02222019
    Load: 82,831.8 MW*
  18SSWG_2019_FAL2_U2_Final_02222019
    Load: 45,642.9 MW*
Contingencies:
  Autogenerated Single
    …
  NERC P1 & P7
    …
*Includes PUNs

## Slide 4: Change Submissions
Please review and verify that the information in the SSWG files are correct, including (but not limited to):
  generation pattern,
  mothballed unit information,
  generator reactive capabilities, and
  autotransformer tap settings.
IDEV/CON files must be submitted with the proposed changes.
  For CON files, only contingencies that are being modified, added, or deleted should be included.
  File naming convention: [TDSP]_2019_VP_[SUM1/FAL2]_Pass[#].[IDV/CON]
    Example: ONCOR_2019_VP_SUM1_Pass0.IDV

## Slide 5: Change Submissions
All changes must be solved in the case with the PSSE solution file “solution.idv” before submittal.
  Changes should improve the quality and strength of the case.
  Changes that cannot solve in the case will not be accepted.
  Any issues solving the case with proposed changes may be brought to ERCOT. ERCOT will help coordinate these changes with the case and any other applicable TDSPs, if necessary.
Voltage set points of ALL generation resources must be of the High Side of the GSU Transformer/POI.

## Slide 6: Voltage Profile Conversations
Please direct all emails relating to the Voltage Profile to VPWGSubmittals@ercot.com
  Also, copy ERCOT staff.
Please include [SUMFAL19] in the subject line of these emails.
  This conventions reduces the possibility of ERCOT missing any emails related to our Voltage Profile Study.
  Example subject lines:
    2019 Summer/Fall Voltage Profile - CNP Pass 0 Submission [SUMFAL19]
    [SUMFAL19] RE: 2019 SUMMER_FALL Voltage Profile Study
    Voltage Profile Pass0 Changes [SUMFAL19]

## Slide 7: Voltage Profile Schedule
Pass # | ERCOT Scheduled Date | TDSP Submittal Date
Pass 0 | 3/6/2019 | 3/20/2019
Pass 1 | 3/27/2019 | 4/10/2019
Pass 2 | 4/24/2019 | 5/1/2019
Pass 3 | 5/8/2019 | 5/15/2019
Final Pass | 5/22/2019 | Review Spreadsheet
Review Meeting | 5/21/2019(?) | 
Posted | 6/1/2019 | 
ERCOT will send out “interim updates” during passes that will contain:
  Change requests/solutions received from TSPs (tracking sheet);
  Updated profiles;
  Any outstanding issues.
2 weeks
1 week
2 weeks
1 week

## Slide 8: Additional Information
PSS/E Version:
  ERCOT will be using the PSS/E Version 33.5.2 during the studies.
Power World Version:
  ERCOT will be using Simulator 19 during the studies.

## Slide 9: Questions?
Thank you!